## Slide 1: 802.1Qbg VSI Discovery and Configuration State Machine
Paul Bottorff
Paul Congdon
V2
July 12, 2010

## Slide 2: Local Change Events
Current VDP state machines uses the shorthand term “localChange-” to indicate a local event from the Hypervisor or the Bridge control plane.
Other 802.1 state machines use variable tests to identify events.
Definitions to identify events at Station:
  HyperCmd = request TLV from the Station’s Hypervisor
  rxResp = most recent Bridge response TLV received at the Station
  A new command event is indicated by HyperCmd != NULL
  A new response event is indicated by rxResp != NULL
Definitions to identify events at Bridge:
  rxCmd = most recent Station command TLV received at the Bridge
  Resp = response TLV constructed by the Bridge resourcing module
      bridgeExit = a boolean which is set TRUE whenever the Bridge wants to exit
      A new command event is indicated by rxCmd != NULL
      A Bridge resource response is indicated by Resp != NULL
      An Bridge exit event is indicated when bridgeExit = TRUE

## Slide 3: Command-Response TLV Fields
All TLVs have the same format as in draft 1.0
Mode1 is 1 octet encoding the command or response
  PREASSOC: 1
  ASSOC: 2
  DEASSOC: 3
  Note1: PREASSOC without resource reservation removed
  Note2: Response does not always reflect command (DEASSOC case)
Mode2 is 1 octet encoding the completion code
  SUCCESS: 0
  Fail Codes: 1-255
State machine may references TLV fields as follows:
  operCmd TLV: operCmd.Mode1 and operCmd.Mode2
  rxCmd TLV: rxCmd.Mode1 and rxCmd.Mode2
  Resp TLV: Resp.Mode1 and Resp.Mode2
  rxResp TLV: rxResp.Mode1 and rxResp.Mode2
  Note: TLV.Mode1 and TLV.Mode2 = NULL when TLV = NULL
  Note: Current state machine uses shorthand for the content of the TLV mode field, ASSOC_ACK_rx, ASSOC_NACK_rx, PREASSOC_ACK_rx, PREASSOC_NAK_rx, DEASSOC_ACK_rx

## Slide 4: Timer Events Using Local Variables
Current Station state machine uses two timers for an response timeout and for a keep alive.
Current Bridge state machine uses one timer for a keep alive time out.
Change Station to count down timers
  StartRespTimer() to WaitRespWhile = respWaitDelay
  ACTIVITY_TIMER_EVENT to keepAliveWhile = reinitKeepAlive
  Response timeout when waitRespWhile == 0
  Keep alive event cycle when keepAliveWhile == 0
Change Bridge to count down timers
  INACTIVE to keepAliveWhile = toutKeepAlive
  Keep alive timeout when keepAliveWhile == 0

## Slide 5: Bridge Resourcing States
The bridge state machine must hand the command to another machine which may query network management system before sending a response.
The Bridge state machine needs to break the command request into two states to allow the command hand-off
  Need a timeout for the resource request from the Bridge
  Need to build the response for the station from the resource request response

## Slide 6: Reverting to Last Successful Associate
The current VDP machines reverts to the previous successful associate in the event of an associate failure.
Even though the machine includes the transition they are not very specific about retaining the existing state.
In addition, it may be desirable to revert on a failed preassociate rather than quite.
Also no revert should occur on a failed keep alive.

## Slide 7: Error Processing
Current VDP machine illustrates error checks on procedure calls, however these are not conventionally illustrated in our machines unless we specify the specific errors possible and how they affect the machine outcomes.
We suggest removing these from the illustration unless we fully specify the operation of the procedures.
Also we normally want to remove the if…then…s from state blocks to fully expand the state machine.

## Slide 8: VDP Draft 1.0: State consolidation
localChange
-
PreAssoc
PreAssoc_NAK_Rx
II
ACKTimeout
||
DeAssocAck
Rx
vsiError
||
localChange
-
DeAssoc
localChange
-
Assoc
vsiLocalTLV
= NULL
vsiState
= UNASSOCIATED
INIT
vsiLocalTLV
= NULL
vsiState
= UNASSOCIATED
INIT
TxTLV(PreASSOC
)
StartACKTimer
()
PREASSOC_PROCESSING
TxTLV(PreASSOC
)
StartACKTimer
()
PREASSOC_PROCESSING
vsiError
=
ProcRxAndSetCfg(vsiRemoteTLV,vsiLocalTLV,
vsiState
);
If (!
vsiError
)
vsiState
= PREASSOCIATED
PREASSOCIATED
vsiError
=
ProcRxAndSetCfg(vsiRemoteTLV,vsiLocalTLV,
vsiState
);
If (!
vsiError
)
vsiState
= PREASSOCIATED
PREASSOCIATED
localChange
-
PreAssoc
||
ACIIVITY_TIMER_Event
PreAssoc_ACK_Rx
TxTLV(DeASSOC
)
StartACKTimer
()
DEASSOC_PROCESSING
TxTLV(DeASSOC
)
StartACKTimer
()
DEASSOC_PROCESSING
TxTLV(ASSOC
)
StartACKTimer
()
ASSOC_PROCESSING
TxTLV(ASSOC
)
StartACKTimer
()
ASSOC_PROCESSING
vsiError
=
ProcRxAndSetCfg(vsiRemoteTLV,vsiLocalTLV,vsiState
);
If (!
vsiError
)
vsiState
= ASSOCIATED
ASSOCIATED
vsiError
=
ProcRxAndSetCfg(vsiRemoteTLV,vsiLocalTLV,vsiState
);
If (!
vsiError
)
vsiState
= ASSOCIATED
ASSOCIATED
(
Assoc_NAK_Rx
&&
VsiState
== !Assoc)
II
ACKTimeout
||
DeAssocAck
Rx
Assoc_ACK_Rx
||
(
Assoc_NAK_Rx
&&
VsiState
== Assoc)
localChange
-
Assoc ||
ACIIVITY_TIMER_Event
localChange
-
PreAssoc
localChange
-
Assoc
ACKTimeout
||
DeAssoc
Rx
vsiError
||
localChange
-
DeAssoc
Local VSI
-
START
EXIT
vsiError
||
DeAssocAck
Rx
Yellow states may be consolidated
Orange states may be consolidated

## Slide 9: Proposed VDP State Machines

## Slide 10: Procedures in Proposed VDP Machine
TxTLV( TLV ) sends a TLV to the VDP listener for packing into a ECP frame.
Bridge Procedures:
  resourceCmd( rxCmd) makes a resource request from the Bridge and builds a response TLV from the current received command. The response may be PREASSOC, ASSOC or DEASSOC with success or fail. The response is returned in the variable Resp.
  resourceFree() frees all the resources associated with this state machine instance
  Dea = buildDea() builds a DEASSOCIATE TLV for the current state machine and returns it in the return parameter.

## Slide 11: Backup Slides

## Slide 12
Station VDP State Machine: operTLV
12
7/12/2010
EVB
PreAssoc_NAK_Rx
II
ACKTimeout
||
DeAssocAck
Rx
vsiError
||
localChange
-
DeAssoc
vsiLocalTLV
= NULL
vsiState
= UNASSOCIATED
INIT
operTLV
= NULL
vsiState
= UNASSOCIATED
INIT
PREASSOC_PROCESSING
PREASSOC_PROCESSING
vsiError
=
ProcRxAndSetCfg(vsiRemoteTLV,vsiLocalTLV,
vsiState
);
If (!
vsiError
)
vsiState
= PREASSOCIATED
PREASSOCIATED
vsiError
=
ProcRxAndSetCfg(vsiRemoteTLV,vsiLocalTLV,
vsiState
);
If (!
vsiError
)
vsiState
= PREASSOCIATED
PREASSOCIATED
localChange
-
PreAssoc
||
ACIIVITY_TIMER_Event
PreAssoc_ACK_Rx
TxTLV(DeASSOC
)
StartACKTimer
()
DEASSOC_PROCESSING
DEASSOC_PROCESSING
ASSOC_PROCESSING
ASSOC_PROCESSING
vsiError
=
ProcRxAndSetCfg(vsiRemoteTLV,vsiLocalTLV,vsiState
);
If (!
vsiError
)
vsiState
= ASSOCIATED
ASSOCIATED
vsiError
=
ProcRxAndSetCfg(vsiRemoteTLV,vsiLocalTLV,vsiState
);
If (!
vsiError
)
vsiState
= ASSOCIATED
ASSOCIATED
(
Assoc_NAK_Rx
&&
VsiState
== !Assoc)
II
ACKTimeout
||
DeAssocAck
Rx
Assoc_ACK_Rx
||
(
Assoc_NAK_Rx
&&
VsiState
== Assoc)
localChange
-
Assoc ||
ACIIVITY_TIMER_Event
localChange
-
PreAssoc
localChange
-
Assoc
ACKTimeout
||
DeAssoc
Rx
vsiError
||
localChange
-
DeAssoc
Local VSI
-
START
EXIT
vsiError
||
DeAssocAck
Rx
localTLV == PREASSOC
localTLV == ASSOC
TxTLV( localTLV )
WaitAckWhile = ackWaitDelay
TxTLV( localTLV )
WaitAckWhile = ackWaitDelay
TxTLV( DEASSOC-TLV )
WaitAckWhile = ackWaitDelay

## Slide 13: Bridge VDP State Machine: Draft 1.0