## Slide 1: Meshed Tree Algorithm for Loop Forwarding in Switched Networks
Nirmala Shenoy, Daryl Johnson, Bill Stackpole, Bruce Hartpence
Rochester Institute of Technology

## Slide 2: Outline
Objectives
What is the problem to be solved
Current Tree Solutions
Meshed Trees Algorithm
  How can it be used
  Convergence
  Multi Meshed Trees
Why 802.1 is the group
Some operational scenarios
  Link Failures
  Packet forwarding
  Broadcast

## Slide 3: Objective of the PAR
Apply meshed trees algorithm for loop free forwarding at layer 2
Leveraging properties of Multi Meshed Trees
Candidate – Spanning Tree, Dijkstra Tree (IS-IS)

## Slide 4: Problem to Solve
Current Tree algorithms – logically undo the mesh topology attributes
Spanning Tree: Single tree rooted at a single bridge that touches all nodes (segments) once.
  MSTP
Dijkstra Tree: Every node is a root and has a tree that touches all nodes once.
Meshed Tree: single root – several tree branches mesh– nodes / segments reside on several branches
  Use the mesh topology capabilities to mesh the branches

## Slide 5: Problem Solved
Single Tree Algorithms
  Messages reach all nodes to construct the tree
  Link/node failure – tree resolve by sending messages
  Link State – flood the topology changes
    Run Dijkstra after Link State Database (LSDB) stabilizes
    Back up paths can be constructed – overhead/complexity
  convergence delays
Meshed Trees Algorithm
  Constructed using local messaging
    Link/ Node failure – resolved locally
    Tree branch pruned
      without impacting frame forwarding
      Without impacting other tree branches

## Slide 6: Problem Solved
Convergence time = Failure detection time + resolution time by protocol
Failure detection time – depends on layer
Resolution time by protocol
    Meshed Trees – node that detects resolves locally
    Local decision time
    Bypasses frame forwarding through another branch
    Prunes the broken branch
    Transparent to rest of the network

## Slide 7: Spanning Tree
Changes in topology
  Tree has to be resolved
  Messages are exchanged
  Convergence time
  RSTP – speeded convergence

## Slide 8: Link State Algorithms
IS-IS based
SPB and TRILL on RBridges
Link State Database
Dijsktra algorithm
Designated forwarder
Still uses RSTP
Complexity

## Slide 9: Questions so far?

## Slide 10: Meshed Trees (Focus on Nodes)
Multiple trees/ tree branches from a single root
Tree branches overlap at nodes
Nodes reside on multiple branches /
Fallback to another branch on link failure
  No resolution impacts
Normal tree (b) Meshed tree (limited meshing)
Root
Root
tree branch 1
tree branch 2
tree branch 3

## Slide 11: Meshed Trees Building
Single root
Multiple tree branches
Tree construction uses local information
Low overhead / quick resolution
How to?
Loop Avoidance
Broadcasting
Packet forwarding
Resolution on Link Failure

## Slide 12: Meshed Tree Algorithm
Root bridge
1
11
12
111
121
122
1111, 1212
1221
1112, 1213
A
B
F
E
C
D
Uses a smart numbering scheme – Virtual IDs (VID)
Assume A is root bridge – has BridgeID/ VID = 1
Hello messages, one-hop bridges decide to join the root – get a Virtual ID (VID)
Advertising bridge – assigns VID to listening bridge by append Port number)
VIDs are associated to ports on which the VID was acquired
Packet take the path of VIDs – route – no loops

## Slide 13: Questions so far?

## Slide 14: Broad Casting - Primary VID Tree
Root bridge
1
11
12
111
121
122
1111, 1212
1221
1112, 1213
A
B
F
E
C
D
To forward broadcast packets, packets to unknown destinations
RULE (still working)
Packets from non primary VID port - send on primary VID port
Packet from primary VID port - send on all other ports where a child bridge has a primary VID derived from parent primary VIDs
Send on all ports that have end nodes –
  Differentiate edge nodes/switches
  Edge nodes do not join the Meshed Tree

## Slide 15: On Link Failure
Root bridge
12
122
1111, 1212
Primary VID Tree after Failure of Link CE/
Tree is pruned /
Packet forwarding continues on backup VID
1. CE Link failure
2. Bridge E detects loss of VID 122
3. Loss of VID 122 announced to ‘F’
4. F invalidates VID 1221
E
C
1
11
111
121
1221,
1112, 1213
A
B
F
D

## Slide 16: Meshed Tree Tables

## Slide 17: MTPDUs
Root Election Security
00 – Bridges will participate in dynamic election. 00 – Default, non-secure
01 – Bridge cannot be a root 01 – Administratively
assigned certificates
10 – 10 –
11 – Bridge is the designated root 11 –

## Slide 18: Questions?

## Slide 19: Multiple Meshed Trees
Root bridge
1
11
12
111
121
122
1111, 1212
1221
1112, 1213
A
B
F
E
C
D
Let us Assume C is another root – C can remove the first digit from its shortest VID – prepend its BID.
Is it necessary for every node to be a root – optimalilty?

## Slide 20: Questions
Slides that follow are operational comparison with TRILL on RBridges
Most arguments would apply to IS-IS based solutions.

## Slide 21: TRILL on RBridges
Operates above layer 2
Uses IS-IS protocol
  Compute pair-wise optimal paths between bridges
To avoid inconsistencies and loops
  Use hop counts
Operation
  Designated RBridge election (typical of link sate)
    Learn membership of end nodes on that link
  Egress Rbridge encapsulates all forwarding frames
    Hop count in the header
  Also calculate spanning tree for multicasting / unknown dest
  End Station Address distribution – ESADI
    used by RBridge to inform other RBridges of end node addresses connected on its link
  An appointed forwarder responsible for loop avoidance
    Blocks frame transmission when RBridge change is noticed

## Slide 22: Implementation TRILL on RBridges

## Slide 23: SPT -> MT Implementation
Replace with Meshed Tree algorithm
ENVIRONMENT FRIENDLY – GREEN SWITCHING

## Slide 24: Comparison MT vs TRILL
Feature | TRILL on Rbridges | Meshed Tree on Bridges
Tree structure | One shortest path spanning tree originating at the root Rbridge Each Rbridge is present on only one branch of a single tree originating from a root bridge | Several overlapped spanning trees with one of them being the shortest path spanning tree Each bridge can reside on multiple branches of a single meshed tree originating from a root bridge
Multiple trees originating at different bridges | Possible | Possible
Knowledge of network topology | required | NOT required Has Path Knowledge
Flooding of topology messages | required | NOT required

## Slide 25: TRILL MT
Action on link failure Addition / removal of bridges and links | Generate link state updates and disseminate. Flood topology control messages | Repair locally. Inform bridges downstream that have a VID which is derived from the lost VID. Prune tree. Build tree branches as nodes join
Formation of temporary loops | Yes. Loop is broken when hop count (6 bits in the header) reaches 0. | Loop formation prevented – Path Vector
Avoidance of loop formation | Not completely avoided. | Avoided using the numbering scheme – Path Vector
Unicast frames (known destination address) | Forwarded on pair-wise optimal paths determined by the link state routing protocol if ESADI is used. Next hop path should be specified. Encapsulated in TRILL header Every Rbridge that forwards decapsulates and encapsulates again | As per optimization 1, neighboring bridges can forward directly to the appropriate port. Forwarded on the optimal path decided by primary VID tree at the originating bridge. During the path – when packet reaches a bridge that has knowledge – forwarded directly

## Slide 26: TRILL MT
Multicast traffic Unicast frames (destination unknown) | Forwarded on distribution trees, using multi path to multi destination. Tree pruning advised ( no specifications provided) | Can follow the current process using multicast addresses at layer 2. Meshed tree at originating bridge can be used as explained
End node address learning | Open the internal Ethernet frame to determine the source address Use ESADI protocol and inform all RBRridges | Learn from source address as no encapsulation is used Can use ESADI protocol
Computing complexity (Dijkstra’s algorithm) | O(n2) in a dense network for node selection with ‘n’ nodes. O(m) for edge (link) updates with ‘m’ edges O(m log n) by using an adjacency list representation and a partially ordered tree data structure for organizing the set of edges . | Convergence or decision making iteration is of O(1) on every new VID that is heard. Greener Solution Less control traffic Less computation

## Slide 27: TRILL MT
Implementations | Dynamic nickname protocol to reduce TRILL header Topology control message dissemination Encapsulation and de-encapsulation at forwarding Rbrdiges. Every transit frame has to be encapsulated with an external Ethernet header. Overhead per encapsulation equals 144 bits End Station Address Dissemination (ESADI) protocol is optional Election of a designated Rbridge per link Designated VLAN required for Rbridge communication Differentiate between IS_IS at layer 2 and layer 3 Requires ‘reverse path forwarding check” to control looping traffic | Replace the ST algorithm with the MT algorithm. Define software to run the MT algorithm Works on the same principle as STA. VIDs will be sent in BPDUs.

## Slide 28: Security Schemes- Recent Work
Ad hoc joining mode – non-secure
Configured joining mode – secure mode
  Key distribution
BPDUs will be encrypted
False BPDU injection avoided
Designated root failure / compromised
1 hop bridges by default will be backup
Monitor root bridge

## Slide 29
Questions and Discussions

## Slide 30: Loop Avoidance in the Algorithm
C may join under D with VID 1113
It will not join under 121 – as 12 is its VID
12
111, 121
111, 121
111, 121
A
B
C
D
Root bridge
1
11
111
121
1113