## Slide 1: 802.1AX -- Link Aggregation: Editor’s Report: July 2017 Version 3
Stephen Haddock
July 12, 2017

## Slide 2: Draft 0.1
Draft generated for first Task Force ballot
  Change bars relative to draft 0.0 (merge of 802.1AX-2014 and 802.1AX-2014-Cor1-2017)
  Bulk of changes in Clause 6. Other clauses, in particular Clause 9 (DRNI), have very few updates as of yet.
Significant changes to Clause 6:
  Replace Mux state machine with proposal from http://www.ieee802.org/1/files/public/docs2017/ax-rev-seaman-wait-to-restore-0117-v01.pdf
  Integrate the per-Aggregation Port portions of Conversation-sensitive Distribution and Collection (CSDC) into existing LACP state machines.
  Modify CSDC Update Mask state machine to correct behavior when defaulted, specify behavior when management changes administrative variables, and (hopefully) clarify information flow.
  Added informative text on how CSDC works (and a little on why you might want it).

## Slide 3: Task Group Ballot results
Ballot Results
  Approve: 4
  Disapprove: 4
  Abstain: 12
Comments
  Commenters: 5
  Comments: 199
    TR: 67 T: 34
    ER: 24 E: 74

## Slide 4: Comment Resolution
Proposed dispositions in
  http://ieee802.org/1/files/private/ax-rev-drafts/d0/802-1AX-Rev-d0-1-pdis-v01.pdf
Large number of comments are “Propose Accept” or “Propose Accept in Principle” with minor variations on the suggested remedy.
  Includes any comments not mentioned in subsequent slides.
  These will be accepted as is unless someone specifically requests discussion of them.

## Slide 5: Comments to Discuss
Port Algorithms: 16
TLV length: 133
Bit order: 129
Point-to-point support: 91, 92, 178
Addressing: 97
ISS MAC_Enable: 171, 191
Digests: 77, 78
Parameter names: 26, 27, 11, 161, 39
Determinism: 189
Mis-ordering: 145, 151, 157
Loopback: 184
Individual: 185
Conformance: 17, 18, 19
Misc.: 20, 82, 47, 135, 162, 188, 132
Items in blue discussed July 11-12 2017 in Berlin

## Slide 6: Mux/WTR comments
Comments to be discussed
  Transition with “|| (Wtr_timeout == 0)”?: 29, 192
  NTT in DETACHED?: 9
  Optional WTR?: 35, 38
  Timer semantics and names?: 29, 33, 30, 31
  Detached when non-revertive?: 139, 177, 72
  Coupled_control and COLLECTING?: 146
Items in blue discussed July 11-12 2017 in Berlin

## Slide 7: Individual Ports
A port designated as “Individual” (i.e. not “Aggregateable”) will not form a Link Aggregation Group with any other link.
What does this mean in terms of selecting an Aggregator?
  An Individual Aggregation Port always has an associated Aggregator that is dedicated to that port. This Aggregation Port cannot select any other Aggregator and no other Aggregation Port can select this Aggregator.
    This is explicitly the case in the context of “Recommended default operation” in revisions prior to 802.1AX-2014-Cor-1.
    This functionality can be achieved by assigning the Aggregation Port and Aggregator a key not used by any other port or Aggregator, independent of designating the port Individual
  An Individual Aggregation Port selects an Aggregator using the same selection rules as any other port, with the added constraint that no other Aggregation Ports can select the same Aggregator. The fact that a port is designated “Individual” does not, in itself, give that port a higher claim to any particular Aggregator.
    This seems to be what is envisioned in the “Selection Logic requirements”
July 12 2017:
Prefer b)

## Slide 8: Possible diagram for 6.6.3 re: Comment #161
Aggregator
variables
Aggregation Port
variables
Mgmt
Link
Actor
_Port_Algorithm
_Conv_Service_Map_Digest
_Conv_Link_Map_Digest
Partner_Admin
_Port_Algorithm
_Conv_Service_Map_Digest
_Conv_Link_Map_Digest
Partner
_Port_Algorithm
_Conv_Service_Map_Digest
_Conv_Link_Map_Digest
Actor_Oper
_Port_Algorithm
_Conv_Service_Map_Digest
_Conv_Link_Map_Digest
Partner_Oper
_Port_Algorithm
_Conv_Service_Map_Digest
_Conv_Link_Map_Digest
TX LACPDU
RX LACPDU
Port_Algorithm_TLV
Conv_Service_Map_Digest_TLV
Conv_Link_Map_Digest_TLV
when SELECTED
when actor.sync
&& partner.sync
1
2
5
3
4

## Slide 9: Backup Slides