## Slide 1: Link Aggregation Simulator Version 1
Stephen Haddock
January 19, 2017

## Slide 2: Link Aggregation Simulator
This presentation gives an overview of a Link Aggregation Simulator developed to demonstrate and test LACP and DRCP operation.
My hope is to post this on Github (or somewhere) as open source code.
  But still trying to understand software licensing implications.
The code is one person’s interpretation of 802.1AX, but
  The code is not the standard and the standard always takes precedence
  On the other hand the code can help “debug” the standard.

## Slide 3: Step 1: Create some Devices
A “Device” is just a shell to network components

## Slide 4: Step 1a: Put some MACs in each
All Devices contain MACs to allow interconnection of Devices.
MACs have a Service Access Point (SAP) internal to the Device.

## Slide 5: Step 1b: Add some Components
Bridge
End
Stn
Bridge
End Station Components have a single SAP pointer.
Bridge Components have a SAP pointer for each Bridge Port.
Can have multiple components in a Device.
End
Stn

## Slide 6: Step 1c: Add Link Aggregation
Bridge
Link Agg
Link Agg
Link Agg
Bridge
Link Agg
A Link Aggregation Component is a “shim” with a SAP in each Aggregator and SAP pointer in each Aggregation Port.
End
Stn
End
Stn

## Slide 7: Step 2: Schedule Events
Bridge
Link Agg
Link Agg
Link Agg
Bridge
Link Agg
Specify times to create/destroy links between MACs, modify managed objects in Components, or generate data Frames.
End
Stn
End
Stn

## Slide 8: About Time
The main loop of the simulation increments a Time variable on every iteration. Each iteration executes any scheduled events, and then calls “timerTick” and “run” in each Device.
  Each Device then calls “timerTick” and “run” in each Component.
    Each component calls “timerTick” and “run” in each object.
      Each object calls “timerTick” and “run” in each state machine.
timerTick():
  Decrements any timer that is running.
run(bool singleStep):
  Calls any periodic functions or state machines, and propagates Frames
    If singleStep is true a state machine will make at most one state transition.
    If singleStep is false a state machine will re-evaluate transition conditions after any transition, and loop until no transitions occur or a maximum loop count is reached.

## Slide 9: Step 3: Run the Simulation
Bridge
Link Agg
Link Agg
Link Agg
Bridge
Link Agg
End
Stn
End
Stn
Link Aggregation Groups are built, destroyed, rebuilt, etc. in response to the scheduled events.

## Slide 10: Link Aggregation Service Sublayer
Aggregator
Ports
Aggregation
Ports
LinkAgg
Class/Object
Aggregator
Class/Objects
AggPort
Class/Objects
Agg
Port
Agg
Port
Agg
Port
Agg
Port
Agg
Port
Agg
Port
Aggregator
Aggregator
Aggregator
Aggregator
Aggregator
Aggregator
Aggregator maintains a list
of attached AggPorts
AggPort maintains the identifier of the selected Aggregator

## Slide 11: Link Aggregation code structure
LinkAgg Class
  Includes vector of Aggregator objects and vector of AggPort objects
    Aggregator and AggPort objects always come in a pairs
  Implements functions that use parameters of multiple Aggregator and/or AggPort objects
    E.g. Simulation Logic, Conversation Sensitive Collection and Distribution
Aggregator Class
  Provides the Aggregator Port SAP
    By inheriting the IssQ class which inherits the Iss class
  Stores Aggregator specific state, but no significant functions.
AggPort Class
  Client of the Aggregation Port SAP
    Has a pointer to the Iss of a class that provides the Port SAP (typically a MAC)
  Contains nested classes that implement LACP per-port state machines

## Slide 12: “Canned” Tests
Edit main program to define simulation scenarios.
Can create customized scenarios.
There are a number of “canned” scenarios provided:
  Basic LAG test
  LAG Loopback test
  Non-Aggregatable Port test
  Preferred Aggregator test
  Limited Aggregators test
  Dual-homing test
  802.1AXbk (LAG of LAGs) test

## Slide 13: Dual-Homing test
Bridge
Link Agg
Link Agg
Bridge
Link Agg
End
Stn
End Station Components have a single SAP pointer.
  Therefore Link Agg configured so only one Aggregator shares a key value with the Aggregation Ports. (Assures Ports don’t select an Aggregator with no client.)
Both links become operational, but only one can select the Aggregator.
  Since the Bridges have different System IDs, the two links cannot be in the same LAG.
  One link will attach to the Aggregator and provide connectivity to the End Station; the other link waits …
  If the link initially attached goes down, the other link will select the Aggregator and continue to provide connectivity to the End Station.

## Slide 14: 802.1AXbk (LAG of LAGs) test
S-VLAN Bridge
Link Agg
S-VLAN Bridge
Link Agg
End
Stn
Link Agg
Link Agg
End
Stn
Link Agg
Link Agg
“Outer”
Link Agg shim uses Nearest Customer Bridge DA
“Inner”
Link Agg shim uses Slow Protocols DA

## Slide 15: The bad news …
The User Interface is basically non-existent.
  “Input” means editing the main program to create the desired simulation scenarios, then re-compile.
  “Output” is a text file containing reports of significant events, state changes, etc.
    Volume of reports controlled by setting a “debug level”
  It is a windows console program, so …
    a console window opens with notifications of Aggregation Links going up or down and Aggregators going up or down
    (mostly just to let you know something is happening when you run the program)

## Slide 16: Backup Slides

## Slide 17
Bridge

## Slide 19
Bridge
BridgePort
BridgePort
BridgePort
BridgePort
Aggregator
Aggregator
Aggregator
Aggregator
AggPort
AggPort
AggPort
AggPort
MAC
MAC
MAC
MAC