## Slide 1: MEF 10.4 Notes

## Slide 2: Structural Changes to MEF 10.3 reflected in MEF 10.4
An EVC EP represents the logical attachment of an EVC to a UNI.
MEF 10.3 refers to “EVC at the UNI” while MEF 10.4 will refer to “EVC EP at the UNI”.
EVC EP is analogous to OVC End Point in MEF 26.2.
EVC EP introduced into MEF 10.4 to facilitate data modeling similar to the data modeling for MEF 26.2.
An EVC is defined as an association of EVC EPs.
No hairpin switching is allowed at a UNI so an EVC can associate at most one EVC EP at a UNI.
Service Provider CEN
UNI
EVC
EVC End Point (EP)

## Slide 3: Terminology
A Service Attribute that applies to an EVC is now called “EVC X Service Attribute”
  E.g., CE-VLAN ID Preservation Service Attribute  EVC CE-VLAN ID Preservation Service Attribute
A Service Attribute that applies to a UNI is now called “Subscriber UNI X Service Attribute”
  E.g., All to One Bundling Service Attribute  Subscriber UNI All to One Bundling Service Attribute
  Makes it clear that the value is agreed to by the Subscriber and Service Provider (and not between the Service Provider and an Operator)
A Service Attribute that applies to an EVC per UNI is now called “EVC EP X Service Attribute” (EP = End Point)
  E.g., Ingress Bandwidth Profile per EVC  EVC EP Ingress Bandwidth Profile
  Reflects the introduction of the EVC End Point
Appendix H.1 lists all of the terminology changes