## Slide 1
Synchronization and Scanning
in
DFWMAC
Greg Ennis Symbol Technologies
Wim Diepstraten NCR
Phil Belanger Xircom
November 9, 1993
IEEE P802.11-93/193

## Slide 2
Basic Synchronization Approach
All stations maintain a local synchronization timer.
Timing Synchronization Function
  keeps timers in synch
  centralized in infrastructure networks
  distributed function for ad hoc networks
Beacons provide timing reference for each BSS.
  not required to hear every Beacon to stay in synch
  Beacons used to calibrate clocks
Flexible Beacon Interval
  BSS parameter
Compatible with CSMA.

## Slide 3
Beacon Generation
Beacon transmission scheduled at Beacon Interval.
Transmission may be delayed by CSMA deferral.
  subsequent transmissions at expected Beacon Interval
  not relative to last Beacon transmission
Timestamp contains timer value at transmit time.
AP sends Beacons in infrastructure networks.
Time Axis

## Slide 4
Ad Hoc Beaconing
Distributed Beaconing
  any station in BSS may send a Beacon
  randomized Beacon generation

## Slide 5
More Ad Hoc Beaconing
Ad Hoc Beacon Sender’s actions:
  wake up before expected Beacon time
  defer to current transmission if any
  execute access backoff procedure
    even when network was idle
    randomizes send attempts
  if heard another Beacon cancel Beacon transmission
    else transmit Beacon
Beacon collisions are possible.
  Beacons are multicasts, so no retransmission
  other station likely to succeed after collision
Only SYNCed stations send Beacons.

## Slide 6
Beacon Contents
TYPE
CONTROL
MPDUID
NetworkID
Dest
Source
Timestamp
Beacon Interval
Weight
CRC-32
2
2
3
6
6
4
3
2
4
1
TYPE
CONTROL
MPDUID
NetworkID
Dest
Source
Timestamp
Beacon Interval
CRC-32
Optional Power Management Elements:
TIM
DTIM Period
Broadcast
2
2
3
6
6
4
3
4
1
Ad Hoc:
Infrastructure:

## Slide 7
Timer Accuracy
Timestamp included in every Beacon.
  Sending station’s TSF timer in microseconds
  31 bit value and 1 bit SYNC flag
Beacon sender actions:
  Timestamp is sender’s timer at SFD transmission time.
Beacon receiver actions:
  Save local TSF timer when Beacon SFD received.
  Validate received Beacon.
  If OK, compare saved timer with Beacon timestamp
  Difference is amount to adjust local station timer
    could adjust for propagation and transceiver delay
Precise synchronization is possible.

## Slide 8
Applications of TSF
Power Management
  Beacons are sent at well known intervals
  All station timers in BSS are synchronized
  Beacons may contain TIM element
  Stations can wake up just before expected Beacon
Superframe Timing
  TSF Timer used to predict start of Contention Free burst
  Beacon is not required in each superframe
Hop Timing for Frequency Hopping PHY
  TSF Timer used to time Dwell Interval
  stations’ TSF Timers synchronized, so hop at same time
  Beacon is not required on each hop

## Slide 9
Frequency Hopping and TSF
STAs use their TSF timer to maintain hop synch.
Only PHY dependency is Max TSF value.
  maximum TSF value is total time for hop sequence
    MaxTSF = NumHops * Dwell_Interval
  TSF timer value describes progress in hopping sequence
    which hop and how long in that hop
STAs independently time Dwell_Interval.
  each station knows when to hop
Hop stretching is possible.
Hop timing fields not required in MAC header.
Dwell_Interval and Beacon_Interval independent.

## Slide 10
Passive Scanning
Find networks simply by listening.
Beacons are sent at a known rate.
Scanner listens to each channel.
  waits at least Beacon Interval on empty channels
Practical for PHYs with a few channels or with a short Beacon Interval.
When network found, save Network ID and Timestamp delta.
  only information required to “tune” to that network

## Slide 11
Active Scanning
Can be much faster than passive scanning.
On each channel, scanner sends a Probe .
  Request message sent to broadcast address
  NetworkID specifies the network for which the scanner is looking.
Wait for a Probe Response.
  wait for a bounded time T1
  if detect energy, wait longer
Multiple Probe Responses are possible.
  more than one AP on same channel
  ad hoc network

## Slide 12
Scanning Process
1. Tune to new channel and CSMA defer
2. Send Probe with Broadcast Destination, Specific ESSID, and desired BSSID
3. Start T1 timer
4. If receive energy within T1
then start T2
Else If hear nothing within T1
then Scan next channel.
5. When T2 expires, process all received Probe Responses.
6. Scan next channel.

## Slide 13
Scanning for APs
More than one AP may be on the same channel.
  scanner wants to hear all Probe Responses
Directed Probe Response.
  invokes positive ACK protocol
  automatic collision recovery

## Slide 14
Scanning for Ad Hoc Networks
Any station in the BSS may respond.
Access Backoff before Probe Response.
If collision then
  sender does Backoff with larger Contention Window
  other station may respond before retries...

## Slide 15
Probe Contents
Probe sent to broadcast Dest.
  BSSID can be specific or “broadcast”
Probe Response is directed to specific Dest.
  NetworkID matches Probe
  Source NetworkID required to identify source BSS
TYPE
CONTROL
MPDUID
NetworkID
Dest
Source
Timestamp
Source
NetworkID
Weight
CRC-32
2
2
3
6
6
4
3
2
4
1
Probe Response:
TYPE
CONTROL
MPDUID
NetworkID
Dest
Source
CRC-32
2
2
3
6
6
4
1
Probe:

## Slide 16
Weight Concept
Used for ad hoc network synchronization.
  APs have” infinite” weight. They are always in sync.
Each station maintains its own Weight variable.
Each station maintains its own SYNC flag.
Weight increases as STA participates in BSS.
  more Beacons heard = more Weight
  more SYNCed stations heard = more Weight
Whenever a STA sends Beacon or Probe Response, it includes its Weight and SYNC.
Weight is used to decide which timer is better.

## Slide 17
Timer Adjustment Policy
TSF Timer Adjustment for unSYNCed receiver:
  if receive Beacon or Probe Response with SYNC =1
    then adopt timestamp
  if receive Probe Response with SYNC = 0
    then AdjustTimer
TSF Timer adjustment rules for SYNCed receiver:
  if receive Beacon or Probe Response with SYNC = 1
    then if difference between timers is above threshold then Coalesce
else AdjustTimer
  if receive Probe Response with SYNC = 0 ignore

## Slide 18
More Timer Adjustment
STAs quickly synchronized with APs.
Established ad hoc networks cause new STAs to synchronize quickly.
In new ad hoc networks, STAs adjust towards a common timer.
AdjustTimer
  Receiving STA uses weighted average to determine how much to adjust time.
  Receiving a Beacon or Probe Response with a higher Weight than STA Weight causes large adjustment.

## Slide 19
Initializing Ad Hoc Networks
1. Scan (BSSID = specific) for 5 seconds
2. If hear something then JoinNet
3. else StartNet
4. Stay active for T3 seconds
JoinNet
  adopt NetworkID and timing of that BSS.
StartNet
  SYNCed =1
  send Beacons to establish BSS timing

## Slide 20
Clusters
Separate clusters of the same BSS may form.
  executed ad hoc startup at same time
  started out of range and moved closer together
Clusters can’t communicate.
  hop timing doesn’t match in FH SS PHY
  ad hoc “superframe timing” doesn’t match
    not awake at same time
Awake
Period
Scan Opportunity
Scan Opportunity

## Slide 21
Coalescing BSS Clusters
Stations in ad hoc networks periodically scan.
If find other cluster, then do Coalesce procedure.
  Weight used to determine which cluster is better
  If scanner’s cluster loses then
    return to old cluster
    send Beacon+ indicating other cluster is better
    switch to cluster
  else
    send Beacon+ on scanned cluster
      defines how to find scanner’s cluster
    return to old cluster

## Slide 22
Synchronization Conclusions
Time synch. is required for many MAC functions.
  Proposed a general mechanism that can be used for:
    Power Management
    Superframe Timing in Contention Free Service
    Hop synchronization in FHSS PHYs
Network events are timed by station TSF timers.
  Not necessary to send frames to indicate network events
  Stations can maintain sync while sleeping or out of range
TSF is efficient.
  periodic Beacon transmission calibrates timers
  time fields not required in all MAC frames
TSF is precise.
  microsecond accuracy is possible

## Slide 23
Scanning Conclusions
Scanning required for many functions.
  joining a network
  initializing an ad hoc network
  maintaining a single ad hoc network
  finding a new AP for BSS transitions
DFWMAC uses a common technique that supports all.
  PHY independent
  single or multi channel
  passive or active scanning