## Slide 1
IEEE 802.11 Mobility requirements
What are the IEEE 802.11 Requirements / goals for mobility?
"To assure that a station can maintain full connectivity while moving around in an area covered by the ESA ".

## Slide 2
Protocol functions to perform the association and re-association functions
Functionality for communication across, and with the DS.
Provide hooks for an arbitrary Distribution System
An “Inter Access Point Protocol“ (IAPP) in the AP, is introduced to support this DS dependent function.
The IAPP is not part of the MAC, but an interface needs to be defined.
Functions to support Mobility:

## Slide 3
IAPP interoperability:
Different IAPP's will be needed per DS
It is important to provide IAPP interoperability.
What organization will be responsible for this standardization.
As a minimum 802.11 should be responsible to standardize the IAPP to support a MAC level bridge based DS.

## Slide 4
Handoff Model
Station to determine what AP to (re-)associate with (scan for best AP).
Station to synchronize to the selected AP.
Issue (Re-)Association Request
New-AP to identify the change of a station presence (logical location) to the DS .
Communicate with the Previous AP using the IAPP to establish a disassociation of the station with that AP.
New-AP responds with Associate Response.
Connectivity is now re-established and communication can be resumed.

## Slide 5
When to start a Reassociation:
Only Stations can start re-association.
Stations need to “Scan for a better AP”.
  They start the scanning process based on “Link Quality” triggers.
  Can be signal level/quality, Retransmission Rate increase, Lack of Beacon, etc.
  Scanning needs to be invoked, independent of the activity of the station.
Stations can loose connectivity suddenly.
  They lost their AP before they have found a new one.
The algorithm used to start the scanning process does not need to be standardized because they do not affect interoperability.

## Slide 6
Seemless Handoff:
What are the performance requirements for the scanning and re-association process.
Effect only relevant when stations need to re-associate during an active (file) transfer.
Communication disruption should preferably be limited to well below the higher layer recovery timeout.
Longer disruptions can not be avoided in Wireless.
For a user, seamless communication means that temporary traffic disruptions are tolerable, but the communication sessions/connections should be maintained, so that no user intervention is needed to restore communication.

## Slide 7
Scanning process:
The DFWMAC describes two scan and subsequent synchronization methods.
  A passive scanning method (just listen to Beacons)
  An active scanning method using “Probe” and “Probe Response” frames for a multichannel environment.
Duration of scanning process will depend on the PHY used, and the scanning strategy used (vendor specific).
Question: Does the standard need to specify scanning performance limits.
Answer: Probably not.

## Slide 8
Pending traffic handling:
Previous-AP can have traffic buffered for the station when the station issued a re-association request with the new AP.
Value of this traffic depends on its age.
  This depends on the retransmission timeouts of the higher layers (not for broadcasts).
  When traffic is too old, then recovery will only increase the delay problem.
Two strategies could be followed:
  This traffic can be recovered over the DS, before new traffic is accepted (need to preserve frame sequence).
  Traffic can be disgarded and the buffer can be flushed.

## Slide 9
Handover Process:

## Slide 10
Frame Formats:
DFWMAC specifies a X-Request and X-Response frames with a flexible element structure.
Request {Element type=Associate, Associate parameters}
with parameters:
{Previous-AP-Address, Original-AP-Address,}
Response {Element type=Associate Response, Associate Response parameters}
with parameters: {Station ID, AP-Address}
Original-AP-Address is an example of a parameter that migth be usefull to support a Router based DS (Mobile-IP tunneling scheme)

## Slide 11
IAPP Function Requirements:
Need to specify IAPP (minimal) functions and the MAC/IAPP interface.
Minimum Functions required:
  Remote dis-associate to Previous-AP
  Confirm dis-associate from Previous-AP
  Notify Association to the DS
DS
IAPP
IAPP
MAC
MAC
Previous-AP
New-AP

## Slide 12
Conclusions:
An IAPP is needed to support handoff, and standardization is very desirable. 802.11 should at least standardize one flavor.
(Start) scanning algorithm does not need to be standardized.
Seamless handoff means that no user interaction is needed to resume communication.
IAPP function and MAC/IAPP interface needs to be further refined.

## Slide 13
Issue’s:
What organization will be responsible for IAPP standardization.
Does the standard need to specify performance limits for handoff.
What pending traffic handling strategy should be used: Flushing or recovery strategy.
What information needs to be provided by the MAC to the IAPP to support a variety of DS’s.