## Slide 1
Fragmentation / Reassembly at the MAC Layer
Presented by
Mark Demange
Motorola
Wireless Data Group

## Slide 2
Background
Foundation MAC doesn’t specify fragmentation capability
Fragmentation enhances system performance
  Improves performance in presence of microwave ovens
  Improves performance with hidden stations within BSA
  Allows optimal hopping FH PHYs
  Reduces or Eliminate Variation in Start of Time Bounded Services Superframe
Authors believe MAC without fragmentation is a broken MAC

## Slide 3
Goals
Include Fragmentation in MAC (issue 20.6)
Adopt Proposal Given In doc: IEEE P802.11-94/37 as basis for inclusion in MAC

## Slide 4
Outline Of Presentation
Advantages of Fragmentation
Cost of Fragmentation
Fragmentation Proposal
Conclusion

## Slide 5
Advantages of Fragmentation - Enhanced Performance in Presence of Microwave Oven Interference
Characteristics Of Microwave Oven Interference
  Pulse Amplitude Modulated Signal
  60 Hz Square Wave – 8.3 ms. ON, 8.3 ms. OFF
  Typically Occupies 10 to 20 MHz of the band at any time
    Rising and Falling Edges of Pulse ‘splatter’ Across the Band
  Center Frequency of Oven Drifts By Up to 10 MHz
Impact of Oven Interference
  Both DS and FH Systems Effected
    Systems Effected If Desired Signal to Interfered Signal Ratio is too Small
  Any Frames Greater than 8.3 ms Guaranteed Not To Be Received Correctly (1100 Byte Ethernet Packet = 8.8 ms @ 1 Mbps)

## Slide 6
Advantages of Fragmentation - Enhanced Performance in Presence of Microwave Oven Interference

## Slide 7
Advantages of Fragmentation - Enhanced Performance in Presence of Microwave Oven Interference

## Slide 8
Advantages of Fragmentation - Enhanced Performance in Presence of Microwave Oven Interference

## Slide 9
Advantage of Fragmentation – Better Performance With Hidden & Sleeping Stations
DS and FH Systems Vulnerable to Interference From Hidden Stations
RTS/CTS Helps IF Stations Are Awake To Hear RTS/CTS Transmissions
Consider System With No RTS/CTS:

## Slide 10
Advantage of Fragmentation – Better Performance With Hidden & Sleeping Stations
Consider System With RTS/CTS:

## Slide 11
Advantage of Fragmentation – Removes Constraints On Dwell/Superframe Times
‘MAC Should Maximize Use Of Bandwidth In Each Hop Interval’ – January 1993 PHY Committee (Passed)
Three Options To Achieve Above Goal – more details in submission
  Fix Dwell/Superframe – No Fragmentation
    Requires Long Dwells To Compensate For Wasted Bandwidth – Long Dwells Undesirable For Effective FH
  Stretched Dwell/Superframe
    High Retransmission Rate Due To Unsynchronized Hopping
    Does not meet PHY Motion January 1993 “The hop rate shall be configurable in the MAC but fixed within a given BSA. It does not have to adapt.” PASS 20-1-1
  Fix Dwell/Superframe – With Fragmentation
    Allows Short Dwells Without Lost Bandwidth Penalty
    Eliminates Unsynchronized Hopping And Its Drawbacks
    Eliminates Variation In Start Time Of Time Bounded Services Supperframe

## Slide 12
Advantage of Fragmentation – Removes Constraints On Dwell Times
Fixed Dwell Duration with Fragmentation
  Transmit Frames That Will Fit Within Current Dwell
  Dynamically Adjust Frame Length To Fully Utilize End Of Dwell

## Slide 13
Cost Of Fragmentation
Stations In Fringe Areas (No Interference or Hidden Stations)
  10 % Of Stations In Outer 5% of Coverage Radius
    Frame Error Rate (FER) approximated from BER (1 * 10-5)
    Expected Bytes Transmitted per 1100 Byte MSDU

## Slide 14
Cost Of Fragmentation
Stations Not In Fringe Areas (No Interference or Hidden Stations)
  BER of PHY Better Than 1 * 10-6 Yields FER < 1%
  Expected Throughput Typical Stations
    Table Assumes Network Level Request-Reply protocol with 1100 byte packets, 100 byte acknowledgments, client response time of 3 ms., server response time of 3 ms., and MAC level windowing of frames. Table does not include effects of interference.
Fragmentation yields less than 5 % degradation in performance at 1 Mbps
Fragmentation yields less than 4% degradation in performance at 2 Mbps

## Slide 15
Fragmentation Proposal
Control Of Channel
  Fragmentation Protocol Must Ensure Control Of the Channel Is Maintained
  Current Foundation MAC Provides A Mechanism To Provide Channel Control
  Channel Control With Windowing

## Slide 16
Fragmentation Proposal
Fragmentation Rules
  Payload Of A Packet Shall Typically Be Some Fixed Number Of Bytes: (max_payload) (except when near the end of a dwell)
  The Payload Of A Packet Shall Typically Be Greater Than Some Fixed Number Of Bytes: (min_payload) (except when fewer than min_payload bytes are remaining in the packet)
  The Number Of Bytes In A Payload Can Be Reduced From max_payload To Allow More Efficient Usage Of The Time Near The End Of A Dwell.
  When A Data Packet Needs To Be Transmitted, The Number Of Bytes In The Payload Of A New Fragment Is Determined By:
    The Time Remaining In The Current Dwell.
    The Number Of Bytes In The Packet That Have Not Yet Been Transmitted For The First Time.

## Slide 17
Fragmentation Proposal
Fragmentation Rules (continued)
  Once The Payload Of A Fragment Has Been Established, That Fragment Will Remain Fixed Until The Fragment Is Successfully Delivered To The Immediate Destination.
  An Access Point Relaying A Packet Will Be Allowed To Re-Fragment The Packet.
  Devices Must Transmit Only If There Is Enough Time Remaining In The Dwell To Allow The Transmission Plus The Acknowledgment If One Is Due.
  If A Fragment Requires Retransmission Near The End Of A Dwell And There Is Not Enough Time Left For The Fragment Plus The Ack: The Device Must Defer Until The Next Dwell.

## Slide 18
Fragmentation Proposal
Fragmentation Rules (continued)
  Fragmentation Near Dwell Boundary:
Maximum Frame Size = 200 Bytes, Minimum Frame Size = 25 Bytes, MSDU of 385 Bytes

## Slide 19
Fragmentation Proposal
Fragmentation Rules (continued)
  Fragmentation Near Dwell Boundary: (another example)
Maximum Frame Size = 200 Bytes, Minimum Frame Size = 25 Bytes, MSDU of 585 Bytes

## Slide 20
Fragmentation Proposal
Fragmentation Rules (continued)
  Retransmission of Window Due To Lost Acknowledgment

## Slide 21
Fragmentation Proposal
Packet Reassembly
  Each Data Frame Requires Sufficient Information To Allow Reassembly At Receiving Station
    Frame Type (data, acknowledgment, etc.)
    Source Address
    Destination Address
    Packet Sequence Number
    Fragment ID Number – fragments of MSDU sequentially numbered
    End-Of-Packet indicator – indicates current fragment ID number corresponds to total frames in MSDU

## Slide 22
Fragmentation Proposal
Frame Formats
  Data Frame
    1 additional element required
  Acknowledgment Frame
    Bitmap Field Of Fragments Received Is Required
Fragment ID # is a binary field – not bit-mapped

## Slide 23
Conclusion
Fragmentation enhances system performance
  Improves performance in presence of microwave ovens
  Improves performance with hidden stations
  Allows optimal hopping FH PHYs
  Reduces or Eliminate Variation in Start of Time Bounded Services Superframe
Benefits Of Fragmentation Offsets Minimal Overhead
  1 Element Per Frame of OH
  Frame Windowing Minimizes Additional Acknowledgments
Fragmentation Proposal Easily Integrated Into Foundation MAC
  Mechanism To Control Channel Already Exists
  Data Frames and Acknowledgment Frames Altered Slightly

## Slide 24
Conclusion
Goals:
  Close Issue 20.6 “Is there a need for fragmentation/reassembly at the MAC layer?” – YES
  Motion: Use the proposal given in this submission as a basis for implementation in the draft standard? – YES