## Slide 1
Wireless MAC
Foundation MAC Protocol
Tutorial presentation
for the
802.11 PHY subgroup
By: Greg Ennis
Phil Belanger
Wim Diepstraten

## Slide 2
Overview / Agenda:
Overview / Basic Access mechanism Wim
  DCF access scheme.
  Simulation results.
  Functions required from the PHY.
  PCF access scheme (optional).
Power Management provisions Greg
  Functions required from the PHY.
Roaming provisions Phil
  Scanning provisions
  Functions required from the PHY.
Synchronization provisions Phil
  Synchronization timer
Frame formats Greg
Quiz results Wim/John

## Slide 3
Wireless Network Architecture

## Slide 4
802.11 MAC Requirements:
Single MAC to support multiple PHY’s.
  Support single and multi-channel PHY's.
Also PHY’s for future bands like:
  1.9 GHz PCS band (Voice and / or Data band).
  Future 5.2 GHz.
  Other ISM bands (915 MHz and 5.8 GHz)
Support Infrastructure mode.
Support Ad-Hoc mode.
Support mobility.
  “Roaming” provisions.
  Power Conservation Management provisions.

## Slide 5
Supported services:
Asynchronous Data Service:
  Short response time with high instantaneous throughput, suitable for Bursty traffic.
  No BSS isolation required.
Contention Free Service (optional):
  Time Bounded service (can be dimensioned for Voice).
    Connection oriented (reserved bandwidth).
    Allows mixed Voice/Data operation.
    Allows variable bitrates (frame sizes).
  Asynchronous Contention Free Service.
    Allows “centralised Control”.
  Requires sufficient BSS isolation.

## Slide 6
Basic Access Protocol:
Use Distributed Access Protocol for efficient medium sharing without overlap restrictions.
Robust for interference.
  CSMA/CA + Ack for unicast frames.
With MAC level recovery
  CSMA/CA for Broadcast frames.
Parameterized use of RTS / CTS to provide a “Virtual CCA” funtion to protect against “Hidden Nodes”.
Support Ad-Hoc operation seamlessly, so does not require any infrastructure.
  Ad-Hoc can overlap with Infrastructure.

## Slide 7
CSMA/CA explained:
Reduce collision probability where mostly needed.
Efficient Backoff algorithm stable at high loads.
  Exponential Backoff for retransmissions.
Implement different fixed priority levels.
  To allow immediate Ack and PCF coexistence.
When no Ack received then retransmit frame after a random backoff (up to max. limit).

## Slide 8
CSMA/CA+Ack Protocol
Defer access based on CCA and NAV state.
Direct access when medium is sensed free longer then DIFS, otherwise defer and backoff.

## Slide 9
Throughput efficiency:
Efficient and stable throughput.

## Slide 10
RTS/CTS medium reservation:
Net Allocation Vector (NAV) follows “Duration” info in RTS and CTS.
Use of RTS / CTS is optional but must be implemented.
Defer on NAV and "CCA", also for the Contention Free service.
RTS / CTS use is controlled by a NoRTS parameter per station. Can be usefull for long inbound frames.

## Slide 11
NoRTS parameter:
RTS/CTS is not benificial for short frames.
The NoRTS parameter indicates per station that frames shorter then the parameter will be transmitted without RTS/CTS.
Allows optional use on long inbound frames.

## Slide 12
RTS/CTS Performance:
60% Short, 40% Long Frames @ 2 Mbps
Good mixed use (long inbound frames) efficiency.

## Slide 13
Backoff timer behaviour:
Backoff timer elapses only when medium is Free.
So higher relative priority for stations that were already deffering.
Exponential Contention window increase at every retransmission.

## Slide 14
Required PHY Functions:
Continuous “Clear Channel Assessment” (CCA) signal indicating when medium is Free.
PHY frequency channel selection under MAC control.

## Slide 15
Important PHY parameters:
The following parameters have effect on the throughput performance and access delay:
  CCA response time.
  Net Rx-Tx turnaround time.
  Slot time=CCA response + Rx-Tx turnaround + medium delay (determines the collision window)
  PHY preamble time.
  Tx-Rx turnaround + medium delay determines SIFS.
  CCA sensitivity level.
  Channel switching delay.
It is better to decrease the Rx-Tx turnaround time while increasing the PHY preamble length (this decreases the slot time).

## Slide 16
CCA sensitivity:
CCA sensitivity determines “Hidden node” vulnerability.
Interference area is much larger then coverage area.

## Slide 17
Effects of Tx-Rx turnaround:
Throughput drops with 15-30%

## Slide 18
Effect of Turnaround times:
Throughput performance drops at equal cw.

## Slide 19
Coordination Functions:
Contention Free Service uses Point Coordination Function (PCF) on a DCF Foundation.
Async Data, Voice or mixed implementations possible.
Contention Free capability is a minimum burden for the Async service implementation.

## Slide 20
Point Coordination Function
SuperFrame to allow mixed "Contention" and "Contention Free" operation under PCF control.
NAV prevents "Contention" traffic until reset by the last PCF transfer or other contention traffic.
Both PCF and DCF Defer for each other causing SuperFrame Stretching.

## Slide 21
PCF Burst operation
CF-Burst by Polling bit in CF-Down frame.
Immediate response by Station on a Poll.
Stations to maintain NAV to protect Up-traffic.
Variable length or no response possible.
“Reset NAV” bit in last frame from AP.
"Ack Previous Frame" bit in Header.

## Slide 22
Next:
Power Conservation Management
Why is it important?
Principle of operation.
Infrastructure and Ad-Hoc operation.
Dynamic behaviour.
Functions required from the PHY.

## Slide 23
Power Management:
Power Conservation Management is very important to support mobility (battery life).
Idle receive state is dominating power consumption.
Current LAN’s assume Rx is always ready to receive.
Basic power conservation principles:
  Turn transceiver off as much as possible.
  Assure that traffic is temporarily buffered while stations are sleeping.
  Solution should be application independent, and provide high throughput when needed.

## Slide 24
Power Management principle:
Need application independent solution.
MAC transmitter need to buffer packets until remote receiver is Awake.
Transmitter announces for which station frames are buffered.
Transmitter and receiver needs to be synchronized.
  Transmitter needs to know when Rx is Awake.
  Rx needs to be Awake when relevant data is expected.
  Accurate synchronization needed to allow extreme low Power operation.

## Slide 25
Basic operation:
Synchronize all stations.
  AP in Infrastructure Networks.
  Distributed among stations in Ad-Hoc networks.
Stations can be in different PM-modes and can dynamically switch PM-modes.
  CAM: Continuous active mode.
  TAM: Temporary active mode.
  PSM: Power Save Mode (two flavours).
Transmitters know the PM-mode of the receivers.
  Two bits in each frame header.
Transmitters will send "Traffic Information Map" (TIM) at regular intervals indicating buffer status.

## Slide 26
Station Power Save states:
Transmit State:
  Transmitter is turned On.
Awake State:
  Receiver is fully powered and capable to receive.
Doze State:
  Transceiver is not able to transmit or receive, and consumes very low power. TIM interval Timer and some other circuitry may still be active.
Stations using Power Save mode will cycle from Doze to Awake, only when relevant traffic is expected, or just before a transmission starts.
  Stations can maintain in an awake state until a no activity timer expires (no Tx or Rx to station activity) (TAM).
CAM stations will be continuous Awake.

## Slide 27
Power Conservation modes:
Two different Power Save Modes available:
PSNP: Power Save Non-Polling.
  Buffered traffic will immediately follow the DTIM.
  Stations identified in the DTIM stay awake to accept traffic.
  Stations need to listen to every (D)TIM (in Beacon).
  Multicast traffic will follow every DTIM.
PSP: Power Save Polling.
  Stations do not have to listen to every TIM. This allows very long sleep times.
  Stations identified in the TIM need to retrieve the buffered frames by a Poll cycle.
  This allows very low power operation (months on battery)

## Slide 28
Dynamic behaviour support:
Stations can dynamically switch to TAM mode.
Return to PSM after “No-activity” time-out is signalled to remote through PM bits.

## Slide 29
Infrastructure mode:
Synchronization allows station awakening just before a (D)TIM.

## Slide 30
Ad-Hoc Power Management
Stations are synchronized using distributed Beacons.
All stations have a common awake period.
Stations that want to send will announce frames using a short ATIM frame in the common awake period.
  Short frames will be send without a prior ATIM.
  The PSP mode is not supported.
Stations that do not receive an ATIM during the common awake will go to sleep again.
Others will stay awake to accept the actual frame.

## Slide 31
Required PHY functions:
For Power Management:
PHY Sleep/Awake under MAC control.
Fast wake-up time.
MAC need to know when PHY is stable (Tx and Rx)
CCA activation also in the middle of a frame (response time less critical).

## Slide 32
Support for Mobility
Stations may move from one BSS to another
MAC must support fast BSS transitions
  switch to a new AP when the current AP is unacceptable
  find the “best AP” to associate
  join the BSS of that AP
Initial “association” support.
  find the desired BSS
  join the desired BSS

## Slide 33
How to find other stations
All networks send Beacons at known interval
Stations use Scanning to find:
  a specific BSS at initialization time
  a better Access Point when “roaming”
    triggered by deteriorating signal quality or other events like “No Beacon” time out
Scanning stations tune to channels other than the one used by their current BSS.
  to see what else is out there
  they are “off line” during scans
    can go into PSP mode to ensure frames are buffered
The MAC determines which channel to use.

## Slide 34
Passive Scanning:
Find networks simply by listening.
Beacons are sent at a known rate.
Scanner listens to each channel.
  waits at least Beacon Interval on empty channels
Practical for PHYs with a few channels or with a short Beacon Interval.
When network found, save Network ID and Timestamp delta.
  only information required to “tune” to that network

## Slide 35
Active Scanning:
Can be much faster than passive scanning.
On each channel, scanner sends a Probe .
  Request message sent to broadcast address
  NetworkID specifies the network for which the scanner is looking.
Wait for a Probe Response.
  wait for a bounded time T1
  if detect energy, wait longer
Multiple Probe Responses are possible.
  more than one AP on same channel
  ad hoc network

## Slide 36
Scanning for APs:
More than one AP may be on the same channel.
  scanner wants to hear all Probe Responses.
  Probe responses should be randomized in time.
  Fast responses possible
    when no activity on channel then Wait T1
    when activity then Wait T2
    when no response, then scan next channel.
Directed Probe Response.
  invokes positive ACK protocol
  automatic collision recovery

## Slide 37
Scanning for Ad-Hoc Networks
Any station in the BSS may respond.
Access Backoff before Probe Response.
If collision then
  sender does Backoff with larger Contention Window
  other station may respond before retries...

## Slide 38
Initializing Ad-Hoc Networks:
1. Scan (BSSID = specific) for 5 seconds
2. If hear something then JoinNet.
3. else StartNet.
4. Stay active (don’t go in power save mode) for T3 seconds.
JoinNet
  adopt NetworkID and timing of that BSS.
StartNet
  SYNCed =1
  send Beacons to establish BSS timing

## Slide 39
Scanning Conclusion:
Scanning required for many functions.
  joining a network
  initializing an ad hoc network
  maintaining a single ad hoc network
  finding a new AP for BSS transitions
Foundation MAC uses a common technique that supports all.
  PHY independent
  single or multi channel
  passive or active scanning

## Slide 40
Required PHY Functions:
To support Scanning:
MAC tells PHY “Go to channel x “
(Channel selection delay must be known)
PHY to provide a Signal Level/Quality indication to the MAC per frame.

## Slide 41
Next:
Timing Synchronization function (TSF).
  What is it used for.
  How is it done.
Beacon to distribute Timing Synchronization.
Use of TSF for Frequency Hopping PHY’s.

## Slide 42
TSF applications:
Power Management
  Beacons are sent at well known intervals
  All station timers in BSS are synchronized
  Beacons may contain TIM element
  Stations can wake up just before expected Beacon
Superframe Timing
  TSF Timer used to predict start of Contention Free burst
  Beacon is not required in each superframe
Hop Timing for Frequency Hopping PHY
  TSF Timer used to time Dwell Interval
  stations’ TSF Timers synchronized, so hop at same time
  Beacon is not required on each hop

## Slide 43
Synchronization Approach:
All stations maintain a local synchronization timer.
Timing Synchronization Function (TSF)
  keeps timers in synch
  centralized in infrastructure networks
  distributed function for ad hoc networks
Beacons provide timing reference for each BSS.
  not required to hear every Beacon to stay in synch
  Beacons used to calibrate local clocks
Flexible Beacon Interval
  BSS parameter
Fully Compatible with CSMA (Beacons can defer).

## Slide 44
Beacon Generation
Beacon transmission scheduled at Beacon Interval.
Transmission may be delayed by CSMA deferral.
  subsequent transmissions at expected Beacon Interval
  not relative to last Beacon transmission
Timestamp contains timer value at transmit time.
AP sends Beacons in infrastructure networks.

## Slide 45
Ad-Hoc Beaconing:
Distributed Beaconing
  any station in BSS may send a Beacon (distributed)
  Beacon generation is randomized in time

## Slide 46
More Ad-Hoc Beaconing:
Ad Hoc Beacon Sender’s actions:
  wake up before expected Beacon time
  defer to current transmission if any
  execute access backoff procedure
    even when network was idle
    randomizes send attempts
  if heard another Beacon cancel Beacon transmission
    else transmit Beacon
Beacon collisions are possible.
  Beacons are multicasts, so no retransmission
  other station likely to succeed after collision
Only SYNCed stations send Beacons.

## Slide 47
Timer Accuracy:
Timestamp included in every Beacon.
  Sending station’s TSF timer in microseconds
  31 bit value and 1 bit SYNC flag
Beacon sender actions:
  Timestamp is sender’s timer at SFD transmission time.
Beacon receiver actions:
  Save local TSF timer when Beacon SFD received.
  Validate received Beacon.
  If OK, compare saved timer with Beacon timestamp
  Difference is amount to adjust local station timer
    could adjust for propagation and transceiver delay
Precise synchronization is possible.

## Slide 48
Frequency Hopping and TSF:
STAs use their TSF timer to maintain hop synch.
Only PHY dependency is Max. TSF value.
  maximum TSF value is total time for hop sequence
    MaxTSF = NumHops * Dwell_Interval
  TSF timer value describes progress in hopping sequence
    which hop and how long in that hop
STAs independently time Dwell_Interval.
  each station knows when to hop (MAC)
Hop stretching could be possible.
Hop timing fields not required in MAC header.
Dwell_Interval and Beacon_Interval independent.

## Slide 49
Synchronization Conclusion:
Time synch. is required for many MAC functions.
  Proposed a general mechanism that can be used for:
    Power Management
    Superframe Timing in Contention Free Service
    Hop synchronization in FHSS PHYs
Network events are timed by station TSF timers.
  Not necessary to send frames to indicate network events
  Stations can maintain sync while sleeping or out of range
TSF is efficient.
  periodic Beacon transmission calibrates timers
  time fields not required in all MAC frames
TSF is precise (microsecond accuracy is possible)

## Slide 50
Required PHY functions:
For synchronization support:
PHY frequency channel selection under MAC control (Go to channel x ).
Fixed deterministic PHY delay
(no variable buffering)

## Slide 51
Frame Format:

## Slide 52
Foundation MAC Frames:

## Slide 53
PHY Requirement summary:
Continuous “Clear Channel Assessment” (CCA) signal indicating when medium is Free.
PHY frequency channel selection under MAC control. “Go to channel x”
PHY Sleep/Awake under MAC control.
Fast wake-up time. MAC need to know when PHY is stable (Tx and Rx)
CCA activation also in the middle of a frame (response time less critical).
PHY to provide a Signal Level/Quality indication to the MAC per frame.
Fixed deterministic PHY delay

## Slide 54
Quiz results:
1: F Nack
2: A 32
3: D “free” appears twice
4: B harmless
5: B DIFS<PIFS
6: A all the buffered frames are sent immediately
7: D A & B
8: B false
9: B false
10: D

## Slide 56
Mixed bitrate support:
What is needed for speed migration:
Primary assumptions:
  Not all PHY's can receive all rates.
  PHY is capable to receive a Nominal rate and a number of fallback rates automatically.
  Higher speed PHY's can support lower speed standards (multi-standard implementation).
Mixed Rate consequence:
  Broadcast traffic at lowest common rate.
  "Control" traffic (short frames) transmission at "Highest common capable rate" may be acceptable.

## Slide 57
Mixed bitrate support:
To allow easy migration to future PHY’s.
  To support fallback rates.
  Does not require ESS to change speed as a whole.
Functionality required from the PHY:
Tx-bitrate under MAC control on a per frame basis.
Automatic bitrate detection in Rx, with “received bitrate” indication to the MAC.