## Slide 1
New Foundation functionality:
Distributed Time Bounded Service
provided by
DCF with priority
By: Wim Diepstraten AT&T-GIS (NCR)

## Slide 2
Time Bounded Alternative:
Foundation protocol defines optional PCF to support Time Bounded.
  Limitation due to PCF overlap problems.
  This limits larger installations.
  Relevant for current and future frequency bands.
    high speed in 1.9 GHz PCS band.
    high speed in potential 5.2 GHz band (HIPERLAN).
Alternative for reservation based “Time Bounded” Service needed.
Solution: Distributed Time Bounded Service (DTBS) using priority access mechanism.

## Slide 3
TBS voice Application:
Delay variance is less important.
  Only variable transfer delay up to a given maximum is needed.
  Timing can be restored in the receiver using a FiFo.

## Slide 4
Required Characteristics:
No overlap limitations between the Asynchronous and DTBS service.
Low transfer delay for all priority levels to support “Bursty” traffic.
Low transfer delay probability distribution for High Priority traffic.
Maximum delay limit for DTBS acceptable to support Voice applications.
  20-30 msec frame times should be acceptable.
  longer delays acceptable for local connections.
Low impact on “Low Priority only” delay and throughput characteristics.

## Slide 5
How to provide priority:
Different IFS values per priority (HPIFS<LPIFS).
  Low priority traffic will defer earlier.
  Low priority will decrease Back-off delay later compared to high priority traffic.
  Full independence between priority levels possible but not necessary.
Different Contention Window (CW) values per priority.
  Average selected Back-off delay will depend on CW-ratio.
Different CW increase policies per priority.
  CW can be constant or even decrease for retransmissions.
  Load of High Priority traffic should best be limited.

## Slide 6
Priority in CSMA/CA:
Only need differentiation in existing CSMA/CA parameters.

## Slide 7
Simulation approach:
Two parameter sets analyzed:
  LPIFS=HPIFS + 16, LPcw = 64, HPcw = 32 slots.
  LPIFS=HPIFS + 32, LPcw = 32, HPcw = 32 slots.
Frame length distribution:
  60% Short (64 Bytes) and 40% Long (576 Bytes).
3 High and 6 Low priority stations.
Simulations as function of Load.
Characteristics analyzed:
  Average delay with and without High Priority load.
  Delay distribution per priority level.
  Average delay impact for “Low Priority only” (compared to LPIFS=HPIFS case)

## Slide 8
Average Delay performance:
Significant priority difference when load increases.

## Slide 9
Low Priority only impact:
No difference at low Loads, minor impact during higher loads, showing lower Throughput.

## Slide 10
Delay Distribution:
20 msec max delay can be met even in high priority overload case.

## Slide 11
More Delay Distribution:
Load from .05-3.05 in steps of .2
Both Low and High Priority traffic load increases in this simulation.

## Slide 12
Throughput:
High priority traffic gets higher throughput.

## Slide 13
Throughput impact:
Minimal impact for “Low Priority only”.

## Slide 14
Independent priority case:
Very similar priority behaviour.

## Slide 15
Impact on “Low Priority” only:
Impact at higher loads causing somewhat lower Throughput.

## Slide 16
HP Delay Distribution:
Very similar performance despite incomplete priority separation.

## Slide 17
LP Delay Distribution:
Somewhat different profile at high loads.

## Slide 18
Repetitive High Priority Load:
Voice traffic is not “Bursty”
  Repetitive Connection oriented traffic is a fixed Load.
  Assumption is that High Priority Load is limited.
Fixed High Priority Load Simulation:
  Assumed 3 (simplex) Voice channels (32 Kbps ADPCM)
  Framing period of 30 msec (120 Bytes / frame)
Need more evaluation to determine effect as function of High Priority Load, and at different Framing periods.

## Slide 19
Fixed load characteristics:
Fixed 120 Byte high priority frame size at 30 msec frame intervals.

## Slide 20
Fixed High Priority Load:
= 12 msec
Lower maximum delay limit possible

## Slide 21
Low Priority Delay Distribution:
Low impact on Low Priority distribution:

## Slide 22
Howmany Priority levels:
Only two levels needed to distinct Asynchronous from DTBS traffic.
It makes much sense to have different priority levels between stations and AP’s.
  AP will typically handle large percentage of the total traffic.
Multiple priority levels can be provided.
  High priority: HPIFS = 2, HPcw = 32 For DTBS.
  Medium priority: MPIFS = 2+16, MPcw = 32 For Async AP.
  Low priority: LPIFS = 2+16, LPcw=64 For Async stations.
Stations can manage their Queue’s such that the DTBS Queue can given higher access priority.

## Slide 23
How to use Priority:
Use Quality-of-Service (QoS) parameter.
  QoS to contain a “Max. transfer delay” value.
  For Async traffic this can be set to “MAX.”
  For DTBS it can be set to the desired Max. Transfer Delay.
MAC to translate QoS into Priority level.
If QoS is anything other then “MAX.”, then the MAC could put the QoS value in a “Time_to_Live” element code.
  MAC could maintain this by substracting the actual transfer delay that the frame experienced in the MAC + Medium.
DTBS to use the Asynchronous frame formats.

## Slide 24
Possible DTBS I/F:
A possible TBS-LLC could have Header containing:
  Max. Delay parameter
  Discard parameter (to allow drop of frame that experienced a too long delay, and allow recovery of timing in the receiver).

## Slide 25
Conclusion:
DTBS based on DCF with priority does not have an overlapping network limitation.
In CSMA/CA priority can be controlled by 3 access protocol parameters.
Multiple priority levels can be provided.
  High priority: HPIFS = 2, HPcw = 32 For DTBS.
  Medium priority: MPIFS = 2+16, MPcw = 32 For Async AP.
  Low priority: LPIFS = 2+16, LPcw=64 For Async stations.
A QoS based I/F can be defined.
A “Time_to_Live” parameter could be maintained in the MAC.

## Slide 26
Motion:
Move:
To add a “Distributed Time Bounded” service functionality to the Foundation MAC and to determine by the end of the May meeting whether one or both of the TBS’s will remain in the standard.

## Slide 27
Motion:
Move:
To add a “priority access mechanism” to the DCF of the 802.11 MAC.

## Slide 28
Motion:
Move:
To use the mechanisms proposed in doc P802.11-94/58 as a basis for the “priority access mechanism” to be included in the DCF, and to further investigate its sensitivity to relevant parameters.