## Slide 1
Protocol elements needed for:
Tx-Power Control
Presented by:
Wim Diepstraten
AT&T-GIS (NCR)

## Slide 2
Dynamic Tx-Power control:
Concept introduced in doc P802.11-92/76 in July 1992.
Potential re-use efficiency simulations provide in 92/76.
Was included in the original WMAC proposal but not in DFWMAC proposal, because it was concentrating on the Access scheme and mobility provisions.

## Slide 3
Why Tx-Power Control:
Purpose is medium re-use efficiency improvement, and reducing interference potential.
PHY’s specify requirement for Tx-Power Control above 100 mWatt.
The use of it should be optional as long as Tx-Power is lower then the 100 mWatt boundary.
Mixed use should be possible.
The algorithm needed does not need to be specified.

## Slide 4
Dynamic Tx-Power Control:
MAC maintains attenuation list per station
  List is build from reception history.
  Tx-Level indication in the frame.
  Rx-Lvl of the received frame in the returning Ack.
  Noise/Interference level at destination is usefull input for the Power Control algorithm.
MAC need to control the PHY per frame.
  Tx-Power level.
  CCA-Threshold level.
CCA-Threshold relates to the Tx-Level
  For every dB the Tx-Level drops, the CCA-threshold can be made 1 dB less sensitive.

## Slide 5
Protocol elements:
Two possible methods
Rx-Lvl in Ack is preferable because it eliminates need for absolute accuracy.
N-Lvl is long term average of background.

## Slide 6
Tx Procedure:
MAC determines “Tx-Lvl” and “CCA-Thresh” and sets the PHY accordingly, and put “Tx-Lvl” also in the frame.
MAC will follow the CSMA/CA access mechanism (CCA inactive for at least xIFS).
MAC / PHY to Xmit the frame.
MAC or PHY to reset “CCA-Thresh” to nominal sensitivity level.
MAC will receive the Ack and the “Rx-Lvl” and maintains the “Attenuation History” for that station.

## Slide 7
PHY Functionality required:
Functions to support Tx-Power Control:
Tx-Power level control on a per frame basis by the MAC.
  granularity TBD. Not only above 100 mWatt.
CCA threshold / sensitivity under MAC control.
  granularity at least equal to Tx-Control granularity.
Receive level (Signal Quality) indication per frame.
  granularity TBD (1 dB expected to be sufficient)

## Slide 8
Motion:
Move:
That the 802.11 MAC should support the necessary protocol elements to allow “Tx-Power control” on a per frame basis.

## Slide 9
Motion:
Move:
To accept the protocol mechanisms that are proposed in doc. P802.11-94/59 for inclusion in the 802.11 MAC.