## Slide 1
Fragmentation
Dave Roberts
Advanced Micro Devices, Inc.

## Slide 2
Assumption
Propagation effects coupled with frame error-rate goals will suggest a maximum 802.11 MAC frame size of about 1/2 KB or so.

## Slide 3
The Problems
The optimum size frame may not meet the minimums necessary for typical network layer packets.
A small frame size may cause problems when routing or bridging a larger frame from another network (e.g., Ethernet, token ring).

## Slide 4
Definitions
SDU vs. PDU
Fragmentation
Windowing

## Slide 5
SDU vs. PDU
Layer n + 1
LnSDU
Ln+1PDU
Layer n
LnPDU
SDU
= what the layer accepts
PDU
= what the layer passes on

## Slide 6
Fragmentation
The breaking up of a layer n+1 PDU into multiple layer n PDUs.
Implies that layer n has a max SDU size ( = layer n+1 PDU size) > max PDU size

## Slide 7
“Windowing”
Giving medium access priority to subsequent frames of a frame group once the first frame has seized the medium.

## Slide 8
Fragmentation vs. Windowing
Fragmentation does not require windowing.
Typically, windowing implies fragmention, however.
This talk will not address windowing.

## Slide 9
L3 PDU Required Maximums
All L3 devices must be capable of handling frames this size or less
AppleTalk - 600 bytes max ever
IP - 576 bytes
IPX - 576 bytes
NetBIOS - ??

## Slide 10
Possible Solutions
Make 802.11 L2 PDU size >= 600 bytes
Let each L3 deal independently
Fragment in L2

## Slide 11
Small L2 SDU Precedence
ARCNET has 508 byte frames (extended version).
In this case, each protocol handled it on its own.
ARCTalk doesn’t exist
IPX developed a L2.5 fragmentation scheme
NetBIOS ??
IP fragments at L3

## Slide 12
Routing/Bridging Problem
Distribution
System
AP
Portal
Ethernet
1024 byte frame
~512 byte frame

## Slide 13
Possible Solutions
Drop packet
Fragment in L3
  Solves routing problem
  Doesn’t solve bridging problem
Fragment in L2

## Slide 14
Routing/Bridging Precedence
A token ring can generate a 4500 byte frame to an Ethernet.
Appletalk - no problem (600 byte max)
IPX - drops packet (“Well, don’t do that.”)
NetBIOS - drops?
IP - fragments at L3
A bridge will not handle this solution at all.

## Slide 15
Observations
These problems aren’t new.
They have been solved before.
Bridging dissimilar LANs is always hazardous.
L2 fragmentation could address both problems at the cost of 802.11 complexity.

## Slide 16
How Complex?
Fragmentation would require:
Buffering in all stations - how much?
  All fragments from all possible datagrams in progress
Fragment ageing timers - how long?
Recovery mechanism to deal with missing fragments
  Interaction with sleeping and power managment?
What max SDU size do we choose?
  1500?
  4500?
  Larger?
  Why?
  If no fragmentation, SDU size = MAC frame size

## Slide 17
A Layer 2.5 Approach
Layer 3
Layer 2
LLC
MAC
Layer 2.5
Fragmentation
This is basically what IPX does with ARCNET
Layer 2.5 is basically the network driver code

## Slide 18
Possible Layer 2.5 Implementations
SNAP is layer 2.5
Do something similar to SNAP or use SNAP
Define a “fragmentation” LLC DSAP/SSAP or
Define a SNAP “fragmentation” protocol ID

## Slide 19
Layer 2.5 Benefits
Isn’t a burden where not needed
  Appletalk has 600 byte max frames
  IP already has fragmentation
Can be implemented in drivers
  No L3 vendor support required
Could be used to solve the bridging problem in general

## Slide 20
Recommendation
Don’t add the complexity to 802.11.
Use the same solutions as before or
Use a layer 2.5 approach (which does not fit 802 reference models).