## Slide 1
Low Power, High Speed FQPSK Solution for Infrared and Other Wireless Systems
Chuck Brown
Sr. Application Engineer
Intel Corporation
(916) 356-3770

## Slide 2
Agenda
Assumption and Issues
Review of FQPSK Carrier Modulated Design
FPGA and Analog/RF ASIC Components
Test Results
Summary and Comments

## Slide 3
Assumptions
Combined Baseband and Multichannel IR-PHY for EXIRLAN
4/16 Level PPM for Baseband Modulation and FQPSK for Carrier Modulation
Proposed Data Transfer Rate in the 1 Mb/s to 10 Mb/s range
Low Cost/High Power Infrared Transmit Diodes support DC to 30 MHz range
There is a need for low power, high performance solutions suitable for implementing EXIRLAN

## Slide 4
Proposed Spectral Template
0.6 6 9 12 15 18 21 24 27 30 MHz
P. Blomeyer IEEE P802.11-94/62
Modulated Carrier Channels (FQPSK)
IEC 84 Band V
Baseband (16-PPM)
6 MHz baseband supports up to 1-Mb/s with 16-PPM
Carrier band channels support 1- to 10-Mb/s (or higher) in a TBD bandwidth
Constant envelope nonlinearly amplified IR system for power efficiency

## Slide 5
Issues
Constraints
  Battery operation
  Limited spectral bandwidth
  Physical size (hand held devices)
Needs
  Low power carrier modulated solutions
  High performance designs to achieved desired data rates
  Compact solution
  Fast time-to-market at a reasonable cost
Recommendation: Combine today's field programmable gate arrary
technology with low power Analog and RF ASICs

## Slide 6
FQPSK Carrier Modulation

## Slide 7
Baseband Processing
11001100... NRZ Data Stream

## Slide 8
FPGA Technology
SRAM/EPROM architecture on 0.8 micron CHMOS process
Low power - typical uA standby with 1 mA/MHz active power
Configurable Function Blocks (CFBs) configured as 24V10 logic or SRAM
IEEE 1149.1 JTAG supports boundary scan testing and in-circuit
reconfiguration and programming
Low cost path to mask programmed version
Small PLCC packaging

## Slide 9
Low Power Analog ASIC Technology
Qualcomm Baseband Analog and RF ASIC in 64 pin TQFP package
Consumes 385 mW at 5V in full transmit and receive operation

## Slide 10
Test Setup
Tested FQPSK and other quadrature modulation techniques
Tested 1 Mb/s and 4 Mb/s (device supports up to 16 Mb/s)
Power consumption, tansmit and receive baseband, and power
spectrum measurements taken

## Slide 11
Test Results
(Vcc = 5.0V at room temperature, Measured Icc + Icco)
Data Master Power Consumption
Rate Oscillator Lot # V3471001 Lot # L4091644
(Mb/s) (MHz) Nov. ‘93 Feb. ‘94
standby 0 35uW 145uW
0.1 0.4 4.0mW 12.0mW
0.25 1.0 9.0mW 17.5mW
0.5 2.0 17.5mW 19.5mW
1.0 4.0 34.0mW 24.0mW
2.0 8.0 60.0mW 29.5mW
4.0 16.0 132mW 46mW
5.0 20.0 176mW 57mW
10.0 40.0 n/a 103mW
February lots include new power screens in wafer test

## Slide 12
Test Results
1 Mb/s Baseband Signal and Constellation Diagram
No ISI nor jitter in baseband signal
Baseband
Constellation
Measured at input of quadrature modulator (unfiltered)

## Slide 13
Test Results
1 Mb/s FQPSK Out-of-Band Power Spectrum
Carrier modulated at 10 MHz
Measured
(Fc = 10 MHz, Span=3 MHz, RBW=3KHz)
Simulated
8 Bit Resolution

## Slide 14
Summary and Comments
FPGA technology provides a low-power, flexible means to implement first generation carrier modulated EXIRLAN systems
8 Bit quantization achieved nearly equal power spectrum and equal BER as 12 bit resolution
The iFX740 based FQPSK baseband processor consumed less then 35 mW at 1 Mb/s and typical standby power less than 150 uW and is able to support data rates up to 16 Mb/s
FQPSK carrier modulated transmission in a NLA channel provided IJF signaling and spectral compactness