## Slide 1
Active Priority DCF Proposal
CSMA/CA with Active Priority Signalling
CSMA/CA-APS
Proposed By:
Symbionics
&
AT&T-GIS/WCND

## Slide 2
DTBS History:
Distributed Time Bounded service (DTBS) introduced by Apple in January meeting following Hiperlan approach.
CSMA/CA with priority mechanism introduced in March meeting by AT&T (doc 94/58).
Committee decides to support DTBS, but method is still to be decided.

## Slide 3
Priority proposal History:
Previous proposal introduced (doc 94/58) in IEEE and ETSI to support DTBS. (Priority through IFS differences).
Alternative priority mechanism (based on priority signalling) suggested in IEEE by Apple in their January DTBS proposal.
AT&T, Apple and Symbionics propose in May IEEE meeting to drop the reservation based TBS of the Foundation MAC in favor of the priority based DTBS approach. This was adopted as a recommendation.
Priority signalling method analysed, and solutions were found for identified potential problems.

## Slide 4
Vision:
It is important to have a World-wide standard for high speed WLANs.
The 5.2 GHz band is a good candidate to become World-wide available (unused extension band for obsolete MLS).
Unlike Hiperlan in Europe, the FCC is not expected to exclusively assign such large amount of unlicensed spectrum to a single standard.
  Etiquette needed to allow coexistence between dissimilar systems in the same band.
The current (1.9 GHz) Etiquette does not support priority access as would be needed to support the Hiperlan and IEEE services (DTBS) in the 5.2 GHZ band.

## Slide 5
World-wide 5.2 GHz standard possible.
If ETSI and IEEE are coexistent because they are based on the same Channel Access Method (CAM) supporting priority access, then this CAM can be:
“The 5.2 GHz Etiquette”
The 5.2 GHz band is needed for High speed LANs
  It can be the next unlicensed world-wide band.
  Adequate spectrum available for High Speed.
  Non spreading modulation types could be possible.

## Slide 6
Combined proposal:
Updated proposal supported by AT&T and Symbionics in both IEEE 802.11 and ETSI RES10.
  Priority signalling method accepted for Hiperlan.
  Contention resolution method still under discussion.
Original random backoff based CSMA/CA proposal is upgraded with a priority signalling mechanism.
  Provides for efficient priority separation and contention resolution.
  Supports multiple priority levels with efficient hierarchical separation.
  Maintains low criticality on PHY requirements.
    Tx-Rx turnaround time is not critical.
No IPR ownership involved.
  Original publication by Rom and Tobagi in 1981.

## Slide 7
Basic Medium Access Mechanism:
Channel Access Mechansm is split into two parts
  Priority resolution
  Contention resolution

## Slide 8
Low traffic model:
If medium is idle, transmit immediately
Medium Free Condition (MFC) avoids “Channel Idle” decision during a contention.
No priority resolution, no contention resolution needed.

## Slide 9
Priority Resolution:
Priority Resolution is split into two parts
  Priority Detection Period (PDP)
  Priority Assertion Signal (PaS)

## Slide 10
Priority levels:
Active Priority Signalling
  Length of Priority Detection Period (PDP) together with length of PaS period sets priority level.
  Linear coding (for priority n, the PDP is n-1 units long).

## Slide 11
Contention resolution:
No changes compared to Foundation MAC.
  Randomly chosen back-off delay
  Decrement Backoff only while Medium Free
  Binary exponential CW increase for retransmissions for stability at high loads.

## Slide 12
Physical Requirements:
Active signalling is one pulse
  Lowest priority does not need to send the PaS.
  All stations need to be able to detect the PaS.
  PaS detection of multiple overlapping sources, so impacts CCA detection strategy.
PaS duration depends on synchronization tolerance

## Slide 13
Transmitter State Machine:
PDP=0 for Highest Priority
PaS=0 for lowest Priority
Priority resolution phase added.
When in decrementing backoff, then do not react on a PaS, but wait longer (frame detection) before restarting priority assesment.
Random delay to randomize subsequent transmissions of the same node.

## Slide 14
CAM Parameters:
Slot Period: Transmit turn-on time + medium propagation delay + CCA detection time in the receiver.
SIFS: Determined by Tx-Rx or Rx-Tx turnaround time, to allow proper reception of the Ack, whichever is greater. Expected in range of 1 usec to slot time.
DIFS: Period likely determined by the Ack duration. Expected in range of 6-8 slots.
PDP: Duration dependent on signalling delay variance, and (n-1) slots detection time.
PAS: Duration dependent on signalling delay variance, and detection time on one antenna.
CW: Period determines collision probability. Assumed 32 slots.
MFC: Continuous idle medium requirement for period of IFS + PDP + Cw / n

## Slide 15
How many priorities needed:
At least two hierarchical independent priority levels needed to support the main services:
  Quality of Service (QoS) should map to priority.
  Asynchronous service Low priority
  Distributed TBS (optional) High priority
Additional relative priorities possible within a service level using Contention Window size differences.
Relative Priority difference between AP and station makes sense.
  Most traffic will be via the AP.
  So AP would generate close to 50% of frames.
  Use of separate hierarchical independent levels for AP may not be optimum.

## Slide 16
Priority levels in the standard.
If number of levels could increase in future.
  Then need manageable PDP and PaS parameters.
AP and Station priority separation by CWmin parameter.
High priority:
PDP = 0; PaS = x
Low Priority:
PDP = x; PaS = 0

## Slide 17
Minimum comformance level:
“Low Priority only” implementations are possible.
  They do not need PaS generation capability.
  But they do need PaS detection capability.
“Low Priority only” is very similar to current Foundation behaviour.
  No PaS generation required but detection facility is mandatory.

## Slide 18
PaS and PDP duration:
Duration depends on:
  “Busy Medium ” -off detection tolerance.
  Medium propagation delay.
  Energy/signal detect time.
    Only single antenna measurement acceptable.
Antenna slotting synchronization will help decrease tolerances.
PaS detection can effect CCA method.
  Multiple PaS signals will overlap

## Slide 19
DIFS duration:
PaS impact of the “Hidden node problem” which depends on the Defer threshold.
  PaS may jam the Ack consistently.
  Solution: DIFS should be > SIFS+Ack
Also shows the unsynchronized PaS case due to the same phenomena.
  Will cause leakage between priority levels.

## Slide 20
Draft standard updates needed:
Change “Medium Free DIFS”
into: “MFC”.
Text changes in several sections.

## Slide 21
Performance:
No simulation environment currently available to assess total system behaviour.
Within priority level the following can be said relative to the doc 94/58 proposal (Multiple IFS priority).
  Performance very similar to results presented sofar.
  Less overhead for Low Priority traffic.
  Little more overhead of High Priority traffic.
  Delay distribution as function of priority traffic load has different characteristics (more hierarchical separation).
The RFMACSIM simulator should be upgraded.
  evaluate “Hidden node” behaviour.
  evaluate parameterization.

## Slide 22
Conclusion:
Efficient priority method proposed to support the defined Foundation MAC services.
Priority based DCF definition is needed now to assure coexistance with optional (future) Time Bounded Services.
  Low priority only is very similar to current Foundation
    No PaS generation required but detection facility is mandatory.
Different AP and Station priorities can be achieved through different CWmin parameters

## Slide 23
Motions:
Move
That 802.11 should adopt the priority based DCF proposal as documented in 94/150.
Move
That 802.11 should adopt two hierarchical independent priority levels mapped to the services provided by the Foundation MAC.
Move
That 802.11 should specify different CWmin parameters for AP and Stations, to allow relative priority difference.