## Slide 1
How to continue with
Time Bounded Services
By: Wim Diepstraten

## Slide 2
Status:
We adopted to use DTBS, and delete the original CF-TBS specification.
The Active priority based DTBS proposal was voted down in the Orlando planery after acceptance by the MAC.
We did not get any feedback from the PHY people about their Active priority signalling conserns.
How to continue??

## Slide 3
A generic priority approach.
Goal:
Implement a generic approach in the MAC for the DCF priority mechanism, that allows both an active and passive implementation on a per PHY basis.
Every PHY standard should also specify the parameters for selecting the priority control method.

## Slide 4
What is needed to comply with our PAR?
We need a MAC that can support DTBS, to comply with the PAR.
Does all PHY’s need to specify support for DTBS?
  Current lower speed PHY’s are less or not suited for support of actual applications.
  Higher speed PHY’s are better suited for most applications.
So, do all PHY’s need to support DTBS???

## Slide 5
Generic Priority mechanisms proposal:
Allows for different priority implementation mechanisms on a per PHY basis.
  DIFS=L,H with PDP=PaS=0 for multiple IFS method.
  DIFS= fixed with PDP and PaS parameterization for active priority signalling (future PHY’s)
AP and Station priority separation by CWmin parameter (MAC).
High priority:
DIFS=y; PDP = 0; PaS = x
DIFS=H; PDP = 0; PaS = 0
Low Priority:
DIFS=y; PDP = x; PaS = 0
DIFS=L; PDP = 0; PaS = 0

## Slide 6
Priority mechanism selection:
Each PHY standard should specify the three channel access parameters per priority level (DIFS, PDP, PaS).
  Current PHY standards can select the multiple IFS approach if they have a problem with active signalling.
  Future 5.2 GHz PHY’s should select active priority signalling, to be compatible with a “priority based Etiquette”.
MAC state machine should include active priority signalling under parameter control.
This allows acceptance of the generic mechanism while postponing or circomventing the PHY specific issue’s associated with active priority signalling.