## Slide 1
Multi Rate Support in the MAC
By: R. Valadas - University of Aveiro,
B. Dobyns - Photonics,
W. Diepstraten - AT&T GIS,
P. Brenner - LANNAIR

## Slide 2
Why Multiple Rates?
Extensibility
  Migration Path to future higher rates.
  We want to re-use the current spectrum for the future rates.
Speed/Range Tradeoff
  Providing the best speed on all the area will be difficult or expensive to the customer. The user will prefer that some areas would be served with a different Quality of Service, rather than having "black spots".
Speed/Power Consumption Tradeoff
  IR case: higher rates transmission consume more power, hence the AP may transmit in high rates, while the stations may choose lower rates.

## Slide 3
Possible Configurations
Fixed Rate for ESS
  Not recommended because it restricts ESS to use a single PHY. This limits migration to a complete new network and infrastructure.
  Would still have an ESS overlap problem.
Fixed Rate for BSS
  Would require overlapping BSS’s on the different speeds.
  The NAV will not work when BSS’s of different rates overlap.
  Therefore this is not recommended.
Multi Rate BSS
  Need a way to resolve the NAV update issue.
  This is the recommended approach.

## Slide 4
MAC Concerns to be analyzed:
Control Packets (Probes, Beacons, etc) must be heard by all stations
Multicast/Broadcast must be heard by all stations
How does a station know which rate to use for transmission?
How do stations update their NAV for transactions in other speeds?
What is the effect of fragmentation.
How are hidden-stations affected?
How does CCA work for different speeds?.
How are Contention Free Services Affected?
What hooks are needed?

## Slide 5
Basic assumptions / definitions:
BSS_BASIC_RATE_SET:
  A set of rates that all the stations on the given BSS are capable of receiving.
  According to the PHYs definitions the default BSS BASIC RATE SETs for the different PHYs will be:
    For DS: {1,2}
    For FH: {1}
    For IR: {1,2}
STATION_BASIC_RATE:
  A value belonging to the BSS BASIC RATE SET, that is used by the station for its transmissions.

## Slide 6
Basic assumptions / definitions (cont):
EXTENDED_RATE_SET:
  The set of rates beyond the BASIC_RATE_SET that a station supports, this could in the future be {1,2 and future x Mbit/s} for any of the existing plus future PHYs.
PLCP_RATE:
  The rate used for transmitting the PHY preamble, and PLCP header,
  This is transparent to the MAC, but must be the same for all stations in the BSS.
  This assumption is already implemented on all the current PHY proposals.

## Slide 7
Assumptions:
The Preamble and the PLCP Headers are transmitted always at the PLCP_RATE
SIFS, PIFS, DIFS are the same for the whole ESS.
All the Control, Multicast and Broadcast Messages are sent at one of the STATION_BASIC_RATE set.
All RTS/CTS are sent at one of the STATION_BASIC_RATE set.
The RTS/CTS "duration" field is specified in time (usec). This is already in the 802.11 Draft.

## Slide 8
How is the rate selected?
Multiple approaches possible:
Transmitter to determine rate (Does not require interaction with the receiver).
  Tx-only decision based on gathered information.
  Decide on station characteristics (Power Save mode).
  Or decide on link condition.
Negotiate rate using the RTS/CTS exchange.
  This requires Tx-Rx interaction.
Recommend to allow both mechanisms

## Slide 9
Example:
Unicast Data Frames are sent on any rate as selected by the transmitter.
The algorithm for selecting this rate is implementation specific.
  Some trivial algorithms could be:
    Try high, retransmit on lower (go back to high after T time).
    Keep fixed tables for each peer.
      Active query using management Supported_Rate Request/Responses
    Keep dynamic tables for each peer using a signal quality (or any other parameter) dependent algorithm.
    And, obviously, transmit always in BASIC_RATE.

## Slide 10
What is needed:
To allow rate switching, the transmitter should know:
  The supported rate of the local PHY.
  The supported rate of the destination PHY.
  Link quality, Power Saving, or other relevant condition if dynamic switching is used (implementation specific).

## Slide 11
Hooks required:
Define a "Supported_Rate" Element to be included in:
  The "Association Request"
  The "Association Response"
  The "Beacon" (usefull for the Ad Hoc networks)
  Request / Response Management frame to query the capabilities of a destination.

## Slide 12
Hooks required:
To support rate negotiation, the following elements are defined.
  "Requested_Rate" in RTS Frame
    Indicates the rate that the sender wants to transmit the data.
  "Granted_Rate" in CTS Frame
    Set to "Requested_Rate" if supported and conditions allow, or BASIC_RATE if not.

## Slide 13
How is the NAV updated:
RTS/CTS messages are send in BASIC_RATE.
  No NAV update problem.
Situation for fragmented frames:
  Ack (with CTS function) is transmitted at the BASIC_RATE.
  Not all Stations can understand the duration field in the data frame, but Physical CS will assure deferal.

## Slide 14
Hidden station effects:
The CTS function (Distribute duration around the receiver) is working fine.
The RTS function (Distribute duration around transmitter) has a potential problem.
  NAV is not or incorrectly updated.
  Stations will hear this transmission and do properly defer until DIFS after !CCA drop.
The danger is that the Ack gets jammed by those stations that are outof Rx range.
This problem is basic to the MAC and unrelated to the rate switching (need DIFS>2*SIFS+Ack).
  Has been detected also in the DTBS proposal.
  Is also present when RTS/CTS is not used.
  Same effect occurs when RTS or Data frame has CRC errors.

## Slide 15
Effect on CCA for different speeds:
Assumptions about the CCA function:
  Current PHY’s use “Length” to aid in “End Delimiter detection”.
  “Length” is encoded at the common PLCP rate.
  Use “Length” to control CCA indication, independent of the modulation used in the Payload area.
Suggest to code the “Length” in “Time”(usec) rather then bits/octets.
  This makes it bitrate independent.
  Rate Coding for future speeds can freely be defined in future standards.

## Slide 16
How is Contention Free affected:
Contention Free services are not affected:
CF-Ack to be transmitted at the BASIC_RATE.
The Poll Messages are sent in BASIC_RATE, and NAV operation of hidden stations (or stations not supporting the transmitted rate) is guaranteed by the stations setting their NAVs to the Maximum CF-Burst length.

## Slide 17
Summary:
To support Multiple Rate BSSs in a flexible way, we need to specify:
"Supported_Rate" element.
  In Association, Beacon and Mngt Request/Response PDU’s.
"Requested_Rate" element / Field (in RTS)
"Granted_Rate" element / Field (in CTS)
And a simple set of rules defined above.

## Slide 18
Motion:
Move:
To adopt the recommendations in 94/164 as the basic hooks for the support of Multi rate support in the MAC.