## Slide 1
FRAME FORMATS
AN APPROACH BASED ON MINIMAL CHANGES

## Slide 2
The Emphasis
The emphasis was on changing the functionality as little as possible.
    Defer that to another paper (94/171)
    Lots of history behind fields
        Don’t want to break something by accident
        look at each functionality change, one by one
    Focus on field order
        How to PARSE the frame
    Better definition for some Elements

## Slide 3
The First Byte
Version Field
    Reduce it to two bits
    Provide two reserved bits
Type Field
    There are only 9 types currently defined
    do not need the distinction for data, management etc.
    4 bit field

## Slide 4
Second Byte
The Control Bits
    To AP, From AP ( no change)
        History
    Elements Present, More (no change)
    Power Management Bits (no change)
    Contention Free
        Not gone yet, two bits
  Retry
    Redundant, but....
    Vote to put back if CF goes.

## Slide 5
Network ID, Sequence #
Put NID here for consistency
    Needed in nearly every frame type
Sequence #
    MSDU-ID is a poor choice of name
    Only need to have a “negligible” rate of packet duplication
        A count is easier and good enough
        What was the HASH algorithm

## Slide 6
Elements
Could go in any frame TYPE
    Needed for PHY specific needs
        Microcells for DS PHY
    Backward compatibility
Every frame is handled the same way
    Elements are handled consistently
    Always in the same place
    Refer to flow chart for parse
    Placed before any TYPE dependant fields
Many undefined elements

## Slide 7
Version Field and Elements
How does the version field work?
    VERSION 1 device will:
      Reject higher version frames
      Backward compatibility
        Table driven?
Elements
    VERSION 1 device will:
      Ignore Elements it doesn’t understand
        It can PARSE them but ignore contents
      Added only when needed

## Slide 8
TYPE Dependant Fields
Duration there etc.
Minor change
    Beacon timestamp, now a fixed field

## Slide 9
CRC
Is the CRC 8 really OK?
  NO
      PHY work suggests CRC 16 OK for very short fields
  MAC should standardize on one CRC
    IEEE 32 CRC

## Slide 10
Frame Lengths
No significant change in frame lengths

## Slide 11
Parsing the Frame
Consistent for every frame type
    Simple state machine or code
Remember that the frame might be bad
    May need to back everything out if CRC bad
    Need ‘temporary’ storage anyway

## Slide 12
94/171 - Fixing the Fields
PHY Specific Elements
Time Stamp in Beacon
Removing Asynchronous Contention Free
Fragmentation Field only when needed
New LOAD Element
Restore ‘RETRY’ bit