## Slide 1
FRAME FIELDS
FIXES TO THE FIELDS AND MISCELLANEOUS ISSUES

## Slide 2
Missing Elements for PHY
Lots of PHY specific Elements missing from the list.
    Need to get the info out in PROBE responses and during Association.
        GEOGRAPHIC LOCATION
        SET
        PATTERN
        CHANNEL INDEX
        HOP TIMING

## Slide 3
Motion
Add the PHY dependent Elements to the list. Do so by adding the relevant text from 94/171.

## Slide 4
Time Stamp in Beacon
The time stamp field is currently a 32 bit time of when the frame was transmitted.
    Doesn’t do what is required
    Should be delta between when the frame should have gone out, and when it actually did go out.
    Allows a STA to really sync to the Beacon interval without memory.

## Slide 5
Time Stamp
Beacon
Delta between earliest delivery
and actual delivery
Beacon
late
On time

## Slide 6
Motion
Change the Time Stamp field to be 16 bits of delta time in microseconds. Do this by using the relevant text in 94/171.

## Slide 7
Remove Contention Free
The current draft is at odds with the recent vote to make Distributed Time Bounded Service (DTBS) the only Time Bounded Service (TBS) scheme. This vote did not instruct the editors to remove the references to the old Point Coordination Function.

## Slide 8
Motion
Instruct the editors to remove all of the references to Asynchronous Contention Free service from the draft standard.

## Slide 9
Fragmemtation
A must for success
  However
      Most MSDU’s will not need fragmemntation
      Some PHY’s will not need it
      Many installations will not need it
Make an Field ‘Present When Needed’
    Two ways
      A bit in the control field
        More efficient
      A new Element
        More consistant

## Slide 10
Add field to indicate total number of frags in MSDU
    Allows a receiving STA to allocate memory based on number of frags and size of first frag.
    looks like ‘# of N’, where N is the total for the MSDU.
    Only need up to 15 frags (two 4 bit fields).

## Slide 11
Motion
Make the fragmentation field a ‘Present when needed’ field.

## Slide 12
Motion
The method for the ‘Fragmentation field’ will be ....
This will be implemented using the appropriate text from 94/171

## Slide 13
The LOAD Element
It means:
    The load on a given Access Point from 0 to 256.
        0 means no load
        256 means its hopeless
    STA can use this info to choose AP
    Numbers are used as relative numbers, not absolutes.
    Included in Probe Response Frames

## Slide 14
Motion
Add a new LOAD Element. Use the text in 94/171 to do so.

## Slide 15
The RETRY bit
It was usefull even though it was totally redundant.
    Restore it if room in Control field
    It does make for a very quick check to reject a frame.

## Slide 16
Motion
To restore the RETRY bit to the draft using the text in 94/171. Let the editors choose the required bit in the control field.