## Slide 1
Presented by
Rick White
Motorola
Wireless Data Group
Concerns with Priority Assertion Signal Based DTBS

## Slide 2
Concerns with Priority Assertion Signal
Priority Assertion Signal (PAS) has impacts on Clear Channel Assessment.
Interference could be detected as a PAS.
Unreliable detection of the PAS could degrade the performance of the protocol.

## Slide 3
Priority Assertion Signal Impacts on CCA
Priority Assertion Signal (PAS) is not a complete frame. May be some or all of the radio preamble.
Detection of PAS could be different than detection of normal frame (Radio Preamble).
Detection of PAS should be reliable in presences of collision.
Probability of collision is higher for PAS than a normal frame.
CCA is required to detect both PAS and Radio Preamble at any point in time.
A PAS could collide with a frame.

## Slide 4
Effects of Unreliable Detection of PAS
False Detection of PAS
  Causes station to unnecessarily defer until next contention window of given priority
  Interference could cause station to defer indefinitely
Undetected PAS
  Could preempt or collide with higher priority traffic

## Slide 5
Priority Assertion Signal and Hidden Station
A hidden station will not detect the PAS.
The PAS from the hidden station may collided with a frame or may cause the media to appear busy to a higher priority station.

## Slide 6
Priority Assertion Signal Detection
Station A transmits PASA
Station B does not detect PASA
Station B transmits PASB in a later Priority Resolution Slot.
PASB could collide with a frame from Station A or preempt Station A if it detects PASB

## Slide 7
Conclusion
Unreliable detection of PAS decreases performance of the MAC.
Current Clear Channel Assessment algorithms have not been concerned with detecting a PAS. Reliability of CCA decreases in the presence of collision. Timing is very critical.
Probability of collision of the PAS is much higher than that of a normal frame.
ISM Band is a high interference environment.
Detect of the Priority Assertion Signal should be reliable in the presence of collision or interference.
Content of the Priority Assertion Signal must be defined in order to maximize reliable detection of the signal.

## Slide 8
Conclusion (con’t)
Priority Assertion Signal based DTBS is more appropriate for low interference environments (licensed spectrum).
Priority Assertion Signal based DTBS should be optional.
  This means that a STA is not required to implement DTBS.
  It also means that a STA is not required to detect a Priority Assertion Signal PAS if it does not implement DTBS.