## Slide 1
Priority Assertion Signal Impacts on CCA
Priority Assertion Signal (PAS) is not a complete frame. May be some or all of the radio preamble.
Detection of PAS could be different than detection of normal frame (Radio Preamble).
Detection of PAS should be reliable in presences of collision.
Probability of collision is higher for PAS than a normal frame.
CCA is required to detect both PAS and Radio Preamble at any point in time.
A PAS could collide with a frame.

## Slide 2
Effects of Unreliable Detection of PAS
False Detection of PAS
  Causes station to unnecessarily defer
Undetected PAS
  Could preempt or collide with higher priority traffic

## Slide 3
Priority Assertion Signal and Hidden Station
A hidden station will not detect the PAS.
The PAS from the hidden station may collided with a frame or may cause the media to appear busy to a higher priority station.

## Slide 4
Priority Assertion Signal Detection
Station A transmits PASA
Station B does not detect PASA
Station B transmits PASB in a later Priority Resolution Slot.
PASB could collide with a frame from Station A or preempt Station A if it detects PASB