## Slide 1
Proposal for Transmitter Splatter Specification for the 2.4 GHz Frequency Hop Phy

## Slide 2
Need for Specification
Out of channel radiation from a transmitter in the 2.4 GHz band has the potential to interferewith the reception of another signal by a receiver operating on a different frequency in the band
DECT specification provides a reference for this type of consideration

## Slide 3
Need for Specification, cont’d
The asynchronousaspect of data communications provides more opportunitiesfor near-far scenarios that have the potential for interference.
Thus, it is proposed that the 2.4 GHz Phy Splatter specification be more aggressive than the DECT specification. What is proposed is illustratedon the next slide

## Slide 4
Proposed 802.11 FH Spec
Static
Dynamic

## Slide 5
Transient Splatter
Transient splatter is the out of channel emissions that exist during the ramp up or ramp down periods.
Transient splatter puts only a few bits at risk in terms of potential interference, whereas, static splatter exist for the entire length of a packet transmission, which may be thousands of bits.

## Slide 6
Transient Splatter, cont’d
From the standpoint of probabilityof packet error rate, one could tolerate a BER of several orders of magnitudehigher during the ramp transient period than during the static periods.
It is proposed, therefore, that the dynamic splatter specification be 10 dB less than the static splatter specification.

## Slide 7
Test specification
Measured in a 1 MHz bandwidth
Measured while on a fixed channel
Measured in static mode with random data modulation
Measured during ramp periods with ramp modulation. This is a peak reading measurement