## Slide 1
802.11 Frame Body Contents
David Bagby
Bob O'Hara Rick White
Dave Roberts Mark Demange
AMD Motorola
One AMD Place 50 East Commerce Dr.
Sunnyvale, CA 94088-3453 Schaumburg, IL 60173
Jon Rosdahl
Novell
122 East 1700 south
m/s C-22-1
Provo, UT 84606-6194

## Slide 2
802.11 frame information contents
Specifies information required for each frame
  field name
  data type
    fixed length
    variable length
  length of info if fixed length
Does not specify how the information items are encoded with in the frame.
  separate proposals will cover encoding issues.

## Slide 3
Frame types
Data
Control
Management

## Slide 4
Frame Subtypes
Data
  Asynchronous Data
  CF Up
  CF Down
Control
  RTS
  CTS
  ACK
  CF-ACK

## Slide 5
Frame Subtypes
Management
  POLL
  Beacon
  ATIM
  Probe
  Association
  Reassociation
  Disassociation
  Authentication
  Privacy

## Slide 6
Frame information contents.

## Slide 7
Data contents
Asynchronous Data
  MSDU
CF Up
  MSDU
CF Down
  MSDU

## Slide 8
RTS contents
Null
  header contains all needed information

## Slide 9
CTS contents
Null
  header contains all needed information

## Slide 10
ACK contents
Null
  header contains all needed information

## Slide 11
CF-ACK contents
Null
  header contains all needed information

## Slide 12
POLL contents
  PSP and POLL are both used as names for the same frame in B2; editors please clean up.
SID

## Slide 13
Beacon contents
Time stamp
  B2 4.3.1
    fixed length, 4 octets
Weight
  B2 4.3.9
    fixed length, 2 octets
Beacon interval
  B2 4.3.2
    fixed length, 1 octet
DTIM period
  B2 4.3.5
    fixed length , 1 octet
continued...

## Slide 14
Beacon contents
DTIM count
  B2 4.3.4
    fixed length, one octet
Channel sync info
  Referenced in B2, but not fully defined.
    Hop sequence, where in sequence etc.
  variable length structure
ESS ID
  string
    variable length
    max size of 128 octets
continued...

## Slide 15
Beacon contents
TIM
  B2 4.3.3
    variable length
Broadcast indicator
  B2 4.3.6
    fixed length, Boolean

## Slide 16
ATIM contents
Null
  header contains all needed information

## Slide 17
Probe contents
Request / Response indicator
  Fixed length, Boolean
Request:
  null

## Slide 18
Probe contents
Response:
    Same as beacon w/o TIM and Broadcast indicator
  Time stamp
    B2 4.3.1
      fixed length, 4 octets
  Weight
    B2 4.3.9
      fixed length, 2 octets
  Beacon interval
    B2 4.3.2
      fixed length, 1 octet
  DTIM period
    B2 4.3.5
      fixed length , 1 octet
  continued...

## Slide 19
Probe contents (response)
  DTIM count
    B2 4.3.4
      fixed length, one octet
  Channel sync info
    Referenced in B2, but not fully defined.
      Hop sequence, where in sequence etc.
    Variable length structure
  ESS ID
    string
      variable length
      max size of 128 octets

## Slide 20
Association contents
Request / Response indicator
  Fixed length, Boolean
Request:
  Privacy Algorithm number
    fixed length, 2 octets
      length determined by 802.10
      value = current privacy algorithm in use

## Slide 21
Association contents
Response:
  Status value
    Boolean
    values:
      Successful
      Not successful
  Not Successful, followed by
    Error indication
      fixed length, one octet
      specific error codes TBD
  Successful, followed by
    SID
      B2 4.3.7
        fixed length, 2 octets
      item not included in msg in B2, required after Association as the SID is the index into a TIM

## Slide 22
Reassociation contents
Request / Response indicator
  Fixed length, Boolean
Request:
  Current AP address
    fixed length, 6 octets
  Privacy Algorithm number
    fixed length, 2 octets
      Length determined by 802.10
      value = current privacy algorithm in use

## Slide 23
Reassociation contents
Response:
  Status value
    Boolean
    values:
      Successful
      Not successful
  Not Successful, followed by
    Error indication
      fixed length, one octet
      specific error codes TBD
  Successful, followed by
    SID
      B2 4.3.7
        fixed length, 2 octets
      item not included in msg in B2, required after Association as the SID is the index into a TIM

## Slide 24
Disassociation contents
null
  all needed information in header
  msg from STA to AP
    “I'm disassociating”
    SA = STA disassociating
    DA = old AP
  msg from AP to STA
    “you're being disassociated”
    SA = old AP
    DA = STA being disassociated

## Slide 25
Privacy contents
Transaction sequence number
  Fixed length, 1 octet
  values: 1, 2

## Slide 26
Privacy contents
Transaction sequence = 1:
  Supported algorithm list
    variable length structure
    structure fields
      Number of algs supported
        fixed length, one octet
      Privacy Algorithm number
        fixed length, 2 octets
        one field for each alg supported

## Slide 27
Privacy contents
Transaction sequence = 2:
  Status value
    Boolean
    values:
      Successful
      Not successful
  Not Successful, followed by
    Error indication
      fixed length, one octet
      specific error codes TBD
  Successful, followed by
    Privacy Algorithm number
      fixed length, 2 octets
      Privacy algorithm selected

## Slide 28
Authentication contents
Transaction sequence number
  Fixed length, 1 octet
  values: 1, 2, 3, 4, 5, 6
Transaction is started by S1, to S2
  general for STA to STA
  For infrastructure S1 = STA, S2 = AP
Challenge response information notation
  3 structures
    authentication alg dependent contents
    variable length
    contained in authentication transaction msgs

## Slide 29
Authentication notation
  Challenge (by, of)
    by challenging STA, of STA being challenged.
    variable Length structure
      Len fixed, 2 octets
      rest = alg dependent challenge contents
  Challenge_Response (by, to)
    by STA that was challenged, to STA issued challenged
    variable length structure
      Len fixed, 2 octets
      rest = alg dependent response contents
  Challenge_Result (from, to)
    from STA challenging STA, to responding STA
    variable length structure
      Len fixed, 2 octets
      rest = alg dependent result contents

## Slide 30
Authentication contents
Transaction sequence = 1:
  Supported algorithm list
    variable length structure
    structure fields
      Number of algs supported
        fixed length, one octet
      Authentication Algorithm number
        fixed length, 2 octets
        one field for each alg supported

## Slide 31
Authentication contents
Transaction sequence = 2:
  Status value
    Boolean
    values:
      Successful
      Not successful
  Not Successful, followed by
    Error indication
      fixed length, one octet
      specific error codes TBD

## Slide 32
Authentication contents
  (Transaction 2 continued)
  Successful, followed by
    Identity assertion by S2
      not in frame body
      contained implicitly in msg header
        SA = S2
    Authentication Algorithm number
      fixed length, 2 octets
      Authentication algorithm selected
      determines how contents of subsequent frames parsed for rest of this authentication transaction sequence.

## Slide 33
Authentication contents
Transaction sequence = 3:
  Challenge ( by S1, of S2 )
  Identify assertion by S1
    implicitly in msg header
      SA = S1
Transaction sequence = 4:
  Challenge_Response ( from S2, to S1 )
  Challenge ( by S2, of S1 )

## Slide 34
Authentication contents
Transaction sequence = 5:
  Challenge_Result ( from S1, to S2 )
  Challenge_Response ( from S1, to S2 )
Transaction sequence = 6:
  Challenge_Result( from S2, to S1)

## Slide 35
Motion:
That the information contents of frames as described in 94/214a be adopted and that the draft be updated to reflect this.