## Slide 1
Proposed Revision to PHY_SAP Service Primitives
Authors:
Dean Kawaguchi, FH PHY co-editor, Symbol Technologies Inc.
Ed Geiger, FH PHY co-editor, Apple Computer Inc.
Tim Blaney, FH PHY co-editor, Xircom
Keith Furuya, FH PHY co-editor, Xircom
Paul Struhsaker, DS PHY editor, Aironet Wireless Communications, Inc.
Barry Dobyns, BB-IR PHY editor, Photonics

## Slide 2
Reason for Change
The PHY editors jointly propose to modify the PHY_SAP service primitives.
The current set of classes defined in section 8 are insufficient to support all PHYs or are not clearly defined.
  No means of indicating CCA channel busy or idle
  Transmit and receive interactions not clearly defined
  Data parameters for start and end classes not defined
  No means of indicating the end of a NAV timer

## Slide 3
PHY_DATA.request
PHY_DATA.request(class, data)
  class=Start_of_Data, data=TXVECTOR
    Starts the transmit state machine. TXVECTOR contains the packet length and other packet control information which are PHY dependent.
  class=Data, data=DATA
    One octet of MPDU data
  class=End_of_Data, data=NULL
    Indicates end of data to transmit.
  class=End_of_Activity, data=NULL
    Resets the PLCP CS/CCA assessment timers to the state appropriate for the end of a received packet. This is generated by the MAC at the end of a NAV timer. This request is used by some PHY implementations which may synchronize antenna diversity switching with the contention backoff timing. The use of this request in the PHY is optional.

## Slide 4
PHY_DATA.indicate
PHY_DATA.indicate(class, data)
  class=Start_of_Activity, data=NULL
    CS/CCA channel busy
  class=Start_of_Data, data=RXVECTOR
    Start of the MPDU portion of a packet following a valid SFD and PLCP Header. RXVECTOR contains the packet length and other packet information including RSSI. RXVECTOR is PHY dependent.
  class=Data, data=DATA
  class=End_of_Data, data=RXERROR
    End of a received packet. RXERROR contains the condition of the received packet with states including no_error, header_violation, format_violation, carrier_lost.
  class=End_of_Activity, data=NULL
    CS/CCA channel idle

## Slide 5
PHY_DATA.confirm
PHY_DATA.confirm
  After all PHY_DATA.request(Data, DATA), it indicates the PLCP is ready to receive another byte. After the PHY_DATA.request(End_of_Data, NULL), it indicates that transmission is complete.

## Slide 6
FH PLCP State Machines

## Slide 7
FH Transmit Timing

## Slide 8
FH Receive Timing

## Slide 9
FH CS/CCA Timing