## Slide 1
Extending B3 frame formats to include WDS support.
Revision 1.0
David Bagby
Bob O’Hara
Dave Roberts
Advanced Micro Devices
One AMD Place
Sunnyvale CA, 94088

## Slide 2
Summary of proposed changes.
Functionality:
  Connectivity combinations
Performance:
  Header lengths
  Duplicate detection / Miscorrelation
  Frame filtering
This presentation will comment on each of these subjects.

## Slide 3
Guidance from August 94 meeting:
Get functionality correct as highest priority.
Efficiency improvements follow functionality in priority.
Using this guideline, this paper analyzes functionality first, performance improvements second.

## Slide 4
Connectivity cases:
10 connectivity cases:
  5 cases from 236
  5 additional cases

## Slide 5
B3 Connectivity cases.
AP3
AP1
AP2
S1
S2
S3
S4
S5
1
2
4
3
5
Distribution System
6

## Slide 6
Additional cases
Committee discussion has been using loose terminology, resulting in less than optimum analysis.
Stricter terminology and attention to notational detail are required to correctly understand all the cases.
Therefore, the first step in the analysis is to establish more precise terminology...

## Slide 7
Terminology problems:
STAn has been used to describe both a station and a station’s address.
APs, and their address are described as APn.
  This obscures the fact that APs ARE Stations.
  This obscures the fact that APs straddle two logically different address spaces.
    The two address spaces could physically be the same.

## Slide 8
Terminology problems:
The loose english concepts of “within a BSS”, “within an ESS”, “a member of a BSS”, “associated” and “in the same physical volume” have been used interchangeably.
  This has caused much confusion among members.
  There are several of these cases depending on how the loose terms are interpreted.

## Slide 9
Let’s get more formal in terminology.
Maddr(sta) == 802.11 MAC address of a STA.
  This can only be a wireless medium address as that is the only address space used by 802.11.
  This notation is for 802.11 stations.
  This covers both STAs and APs, since APs are addressable STAs within the 802.11 MAC address space.
DSaddr(sta) == the DS address of an AP.
  This is the address used by the DS to address the DS side of an AP.
  The details of the DS address space are dependent on the DS implementation and outside the scope of 802.11.
  The single DS implementation that 802.11 impacts is when a DS is implemented using an 802.11 wireless medium.

## Slide 10
B3 notation:
B3 uses the following concepts:
SA = source address
DA = Destination address
VIA = the address of the (single) AP which is a member of a specific BSS.
  This name was changed to BSSID during the August meeting.
“To bit”: indicates if a frame was “to” an AP.
“From bit”: indicates if a frame was “from” an AP.

## Slide 11
The connectivity categories:
Infrastructure cases
Independent BSS (“Ad-Hoc”) cases
Wireless DS cases
Mixed terminology cases

## Slide 12
Infrastructure cases:
Case 1: STA to STA, via DS; first link
  Example: Frame from S1 destined to S2, entering DS via AP1
Case 2: STA to STA via DS; last link
  Example: Frame from S1 destined to S2, exiting DS via AP2
Case 3: STA to AP; frame destined for AP
  Example: Frame from S3 destined to AP3
Case 4: AP to STA; frame originated by AP
  Example: Frame from AP3 destined to S3

## Slide 13
Independent BSS (“Ad-Hoc”) cases:
Case 5: STA to STA direct.
  Example: Frame originated by S4 destined for S5.

## Slide 14
Wireless DS case:
Case 6: AP to AP, distributing (a case 1 or 2 frame) via the same (i.e. in-band) wireless medium as that used for either the first OR last link.

## Slide 15
Mixed terminology cases:
“Overlapping”, “within”, “when a member of” etc.
More later, after we have examined the concepts that are being intermixed...

## Slide 16
Separate overloaded concepts
Analysis of case 6 points out that we are still mixing concepts and overloading different concepts onto address fields.

## Slide 17
Architectural “transit points”:
Originator of a frame.
Terminator of a frame.
Transmitter of a frame.
Receiver of a frame.

## Slide 18
Architectural “transit points”:
The term “source” has been used to refer to both the Originator and the Transmitter of a frame.
The term “destination” has been used to refer to both the Destination and the Receiver of a frame.
Confusion occurs because we do not always mean the same thing by “source” and “destination” in all cases.
This is probably because our brains have been constrained by thinking about networks with zero levels of indirection.
The 802.11 architecture is a 1 indirection level system.

## Slide 19
Architectural “transit points”:
In the Ad-hoc cases:
  Originator = Transmitter = “source”
  Terminator = Receiver = “destination”
Infrastructure cases:
  The VIA concept in B3, is a recognition that in transiting an ESS, “receiver” does NOT always equal “terminator”.
  Case 6, also points out that if you have a WDS, “originator” does not always equal “transmitter”.
    This leads one to introduce the concept of “RA”.

## Slide 20
Let’s name these different addresses.
Let [ variable ] == the value of “variable”;
[SA] = Maddr (of the STA which originated the frame).
  This is consistent with the term SA as used in other 802 standards.
[DA] = Maddr (of the STA which is the final destination of the frame).
  This is consistent with the term DA as used in other 802 standards.
[RA] = Maddr (of the STA which is intended to receive the frame off the 802.11 wireless medium).
[TA] = Maddr (of the STA which placed the frame onto the 802.11 wireless medium).

## Slide 21
Frame direction wrt DS
802.11 has also found it necessary to specify the direction of a frame with respect to the DS.
This is done by bits in the FC field of the frame header.
“To bit” == Frame is entering the DS from the wireless medium via an AP.
“From bit” == Frame is exiting the DS via an AP onto the wireless medium.

## Slide 22
Frame direction wrt DS
The truth table for these bits is:
TO FROM Meaning
False False “Direct, not via a DS”
False True “Frame outbound from DS”
True False “Frame inbound to DS”
True True “Frame wirelessly distributed”
The concept is not to / from an AP.
The concept is to / from the DS.
We should correct the names of the bits:
  “To AP” is changed to “To DS”
  “From AP” is changed to “From DS”

## Slide 23
Consider cases concepts separated out...
Before optimizing the addressing needed for each case, we must clearly understand which address is needed for each case and why.
Note: A claim that four addresses are needed in every message is not going to be made.

## Slide 24
Independent BSS (“Ad-Hoc”) cases:
Case 5: STA to STA direct.
Example: Frame originated by S4 destined for S5.
  [SA] = Maddr(S4)
  [DA] = Maddr(S5)
  [TA] = Maddr(S4)
  [RA] = Maddr(S5)
  [To] = False
  [From] = False

## Slide 25
Infrastructure cases:
Case 1: STA to STA, via DS; first link
Example: Frame from S1 destined to S2, entering DS via AP1
  [SA] = Maddr(S1)
  [DA] = Maddr(S2)
  [TA] = Maddr(S1)
  [RA] = Maddr(AP1)
  [To] = True
    Frame is inbound to DS
  [From] = False

## Slide 26
Infrastructure cases:
Case 2: STA to STA via DS; last link
Example: Frame from S1 destined to S2, exiting DS via AP2
  [SA] = Maddr(S1)
  [DA] = Maddr(S2)
  [TA] = Maddr(AP2)
  [RA] = Maddr(S2)
  [To] = False
  [From] = True
    Frame is outbound from DS

## Slide 27
Infrastructure cases:
Case 3: STA to AP; frame destined for AP
Example: Frame from S3 destined to AP3
  [SA] = Maddr(S3)
  [DA] = Maddr(AP3)
  [TA] = Maddr(S3)
  [RA] = Maddr(AP3)
  [To] = False
    frame is NOT inbound to DS, it is destined to the AP.
  [From] = False
    frame is NOT outbound from DS

## Slide 28
Infrastructure cases:
Case 4: AP to STA; frame originated by AP
Example: Frame from AP3 destined to S3
  [SA] = Maddr(AP3)
  [DA] = Maddr(S3)
  [TA] = Maddr(AP3)
  [RA] = Maddr(S3)
  [To] = False
    frame is NOT inbound to DS
  [From] = False
    frame is NOT outbound from DS, it originated at the AP.

## Slide 29
Wireless DS cases

## Slide 30
Wireless DS general case
S1
S2
AP1
AP4
AP2
Case 1
Case 2
Case 6
Distribution System Medium
Wireless Medium
Logical Distribution Service /
Association Information
Additional WDS links

## Slide 31
Wireless DS case
Case 6: AP to AP, distributing a frame via the wireless medium.
Example: Frame from S1 destined to S2, transiting a wireless DS between AP1 and AP4
  [SA] = Maddr (S1)
  [DA] = Maddr (S2)
  [TA] = Maddr (AP1)
  [RA] = Maddr (AP4)
  [To] = True
    frame IS inbound to DS from the wireless medium
  [From] = True
    frame IS outbound from DS onto the wireless medium

## Slide 32
Wireless DS case
Note: with all four addresses, it is possible to handle an arbitrary number of WDS hops.
This provides a general solution for wireless distribution.

## Slide 33
Mixed terminology cases
Many loose terms causing confusion:
  “Overlapping”
  “within”
  “when a member of”
  “in the same volume as”
  “Associated with”
  etc...
The key concept is Overlapping coverage volumes.

## Slide 34
MIxed mode case analysis
The cases under discussion are those where a STA desires to both make use of the services of an ESS, and also be able to communicate directly with another STA.
There are 3 combinations which cover the permutations.
The key is to understand that the state of a STA (with respect to membership in an ESS) is orthogonal to the communication method used for any particular frame.

## Slide 35
Let’s Consider the mixed mode cases wrt SA, DA, RA, TA, To, & From...

## Slide 36
Mixed mode case diagram
AP1
S1
S7
Mixed mode cases A, B, C

## Slide 37
Mixed mode case A
S1 is a member of a BSS which contains AP1 and is Associated with AP1,
AND
S7 is not a member of the same BSS.
  [SA] = Maddr (S1)
  [DA] = Maddr (S7)
  [TA] = Maddr (S1)
  [RA] = Maddr (S7)
  [To] = False
    frame is NOT inbound to DS from the wireless medium
  [From] = False
    frame is NOT outbound from DS onto the wireless medium

## Slide 38
Mixed mode case B
S7 is a member of a BSS which contains AP1 and is Associated with AP1,
AND
S1 is not a member of the same BSS.
  [SA] = Maddr (S1)
  [DA] = Maddr (S7)
  [TA] = Maddr (S1)
  [RA] = Maddr (S7)
  [To] = False
    frame is NOT inbound to DS from the wireless medium
  [From] = False
    frame is NOT outbound from DS onto the wireless medium

## Slide 39
Mixed mode case C
S1 is a member of a BSS which contains AP1 and S1 is Associated with AP1,
AND
S7 is also a member of the BSS which contains AP1 and S7 is Associated with AP1.
  [SA] = Maddr (S1)
  [DA] = Maddr (S7)
  [TA] = Maddr (S1)
  [RA] = Maddr (S7)
  [To] = False
    frame is NOT inbound to DS from the wireless medium
  [From] = False
    frame is NOT outbound from DS onto the wireless medium

## Slide 40
All three of the mixed mode cases are the same.
Wrt SA, DA, RA, TA, To & From, all three mixed mode cases are identical.
All three mixed mode cases are also identical to case 5 (direct communication).
B3 contains confusion when it talks about the address of the BSS, within a ESS of which S1 is a member, and overload this concept with BSSID.
So let’s examine the concept of BSSID...

## Slide 41
BSSID vs mixed modes
It is desirable to have a BSSID so that receiving STAs can filter incoming msgs based on BSSID.
  In particular, there is interest in filtering Broadcast and Multicast msgs.
BSSID is substituting in our shared media environment for the concept of a “logically separate media”.

## Slide 42
BSSID vs mixed modes
The key question: What is the BSSID that should be used for mixed mode cases A, B and C?
Answer: The BSS that contains both S1 and S7.
This may or may not be the same BSS which contains AP1.
Lets look at each case closer...

## Slide 43
Mixed mode case A
AP1
S1
S7
Mixed mode case A
BSSID = Maddr(AP1)
BSSID = “Ad-Hoc A”

## Slide 44
Mixed mode Case A BSSID
For the frame going from S1 to S7:
BSSID must = “Ad-Hoc A”
This is the only piece of info common to both S1 and S7.

## Slide 45
Mixed mode case B
AP1
S1
S7
Mixed mode case B
BSSID = Maddr(AP1)
BSSID = “Ad-Hoc B”

## Slide 46
Mixed mode Case B BSSID
For the frame going from S1 to S7:
BSSID must = “Ad-Hoc B”
This is the only BSSID known to S1.
This is the only piece of info common to both S1 and S7.

## Slide 47
Mixed mode case C
AP1
S1
S7
Mixed mode case C
BSSID = Maddr(AP1)
BSSID = “Ad-Hoc C”

## Slide 48
Mixed mode Case C BSSID
For the frame going from S1 to S7:
There are two choices for BSSID:
  “Ad-Hoc C”
  Maddr(AP1)
Either will get the msg from the source to the destination without causing any problems at an AP.
  [To] = [From] = False, so APs will not attempt to process the frame.

## Slide 49
Direct communication BSSID conclusion
The BSSID must be that of a BSS of which both the Source and Destination stations are members.
  This allows both choices for Case C.
Such a BSS always exists for direct communication cases.
The choice of BSSID to use for mixed mode case C can be unspecified by 802.11 - either works from the MAC viewpoint.
  The choice of which to use and/or try first is not of significance to 802.11 MAC operation.

## Slide 50
Infrastructure BSSID values
For BSSs which are part of an ESS:
BSSID = Maddr(AP).

## Slide 51
Using ESSID to find BSSID
In an ESS, a STA learns about local APs.
What it learns is { ESSID, Maddr(AP) } pairs
  Contained in beacons etc
STAs wishing to join a particular administrative group, pick an AP by using the Maddr(AP) of an AP which belongs to the desired administrative group.

## Slide 52
Using Ad-Hoc admin group to find BSSID.
The BSSID of an IBSS = Maddr( the STA which initiated establishment of the BSS)
The same mechanism used by a STA to find BSSID from ESSID is sufficient.
A STA wishing to join an IBSS simply selects a Maddr which corresponds with the desired administrative grouping.

## Slide 53
Independent BSSID values
Conclusion: For Independent BSSs, BSSID = Maddr( the STA which initiated establishment of the BSS).
This supports as much differentiation between different IBSSs as desired.
Thus broadcast, multicast filtering by BSSID is provided.

## Slide 54
Mixed mode interaction conclusions:
At any given instant:
A STA may be a member of zero or 1 ESSs.
AND
A STA may be a member of as many IBSSs as it desires.
Since APs are STAs, this also applies to APs.

## Slide 55
WDS components

## Slide 56
Logically, IBSSs are used to build WDSs.
S1
S2
AP1
AP4
AP2
Case 1
Case 2
Case 6
Distribution System Medium
Wireless Medium
Logical Distribution Service /
Association Information
Additional WDS links
IBSS

## Slide 57
Logically, IBSSs are used to build WDSs.
Two APs must be in direct communication or they can not be used to wirelessly distribute a frame.
Interestingly, the BSSID of the logical IBSS is not required within the case 6 frame.
  See case 6 frame examples later in paper.
Only a DS need know how APs are related.
  (In order to figure out which APs to use to wirelessly distribute a frame).
  If were needed, the logically correct BSSID for a case 6 frame is the ID of the BSS which contains both AP1 AND AP4.
  Whether a DS actually does, or does not, set up the logical IBSSs is irrelevant to the 802.11 MAC.
  Mobile STAs neither need to know, nor care, about these logical BSSs.

## Slide 58
Observations about WDS case:
Case 6 is only required for wirelessly distributed DATA type frames.
Control frames never transit a DS.
  RTS, CTS, ACK, POLL
Management frames never transit a DS.
  They are always between directly communicating STAs
  STA to STA in a BBS
  STA to AP in an ESS
Only Data frames are ever Distributed and hence transit a DS.

## Slide 59
Observations about WDS case:
Case 6 (WDS) is the only case where all four logical addresses can actually have 4 distinct values.
In all case 6 “hops”, the logical Distribution Service, is invoked.
  Required in order to access the Association information to determine how to distribute the original frame from S1 to S2.
  Whether this functionality is implemented within a physical AP is not relevant.

## Slide 60
WDS Data frame support.
We should enable support of WDS.
Wirelessly distributed msgs are identified by [To] = [From] = true.
WDS link msgs use a WDS Data header.
  Provides support for WDS links.
  Only a small amount of additional information is needed (above a normal Data header) for specific msgs.
    One address
  Overhead cost is only paid for msgs that are actually wirelessly distributed.
  No other msgs have increased overhead.

## Slide 61
WDS Data header
B3 DATA header
Orig
SA
MSDU
Present IFF [To] = [From] = TRUE in FC field
WDS Data Header

## Slide 62
Impacts on frame headers:
Now that we have explored the previously overloaded concepts, lets look at what this means for frame headers...

## Slide 63
Header Address field contents for each msg type:
RTS
  all examples
    [ SA field ] = TA = Maddr( transmitting STA )
    [ DA field ] = RA = Maddr( receiving STA )
    [ To DS] = False
    [ From DS] = False
CTS
  all examples
    [ DA field ] = RA = Maddr( receiving STA )
    [ To DS] = False
    [ From DS] = False

## Slide 64
Header Address field contents for each msg type:
ACK
  all examples
    [ DA field ] = RA = Maddr( receiving STA )
    [ To DS] = False
    [ From DS] = False
POLL
  all examples
    [ SA field ] = TA = Maddr( transmitting STA )
    [ To DS] = False
    [ From DS] = False

## Slide 65
Header Address field contents for each msg type:
DATA & Mgt
  Case 1
    [ BSSID field ] = Maddr (AP1)
    [ SA field ] = Maddr (S1)
    [ DA field ] = Maddr (S2)
    [ To DS] = True
    [ From DS] = False

## Slide 66
Header Address field contents for each msg type:
DATA & Mgt
  Case 2
    [ BSSID field ] = Maddr (AP2)
    [ SA field ] = Maddr (S1)
    [ DA field ] = Maddr (S2)
    [ To DS] = False
    [ From DS] = True

## Slide 67
Header Address field contents for each msg type:
DATA & Mgt
  Case 3
    [ BSSID field ] = Maddr (AP3)
    [ SA field ] = Maddr (S3)
    [ DA field ] = Maddr (AP3)
    [ To DS] = False
    [ From DS] = False

## Slide 68
Header Address field contents for each msg type:
DATA & Mgt
  Case 4
    [ BSSID field ] = Maddr (AP3)
    [ SA field ] = Maddr (AP3)
    [ DA field ] = Maddr (S3)
    [ To DS] = False
    [ From DS] = False

## Slide 69
Header Address field contents for each msg type:
DATA & Mgt
  Cases 5, A & B:
      (case 5 example shown)
    [ BSSID field ] = Maddr (ad-hoc initiating STA)
    [ SA field ] = Maddr (S4)
    [ DA field ] = Maddr (S5)
    [ To DS] = False
    [ From DS] = False

## Slide 70
Header Address field contents for each msg type:
DATA & Mgt
  Case C
    [ BSSID field ] = Maddr (AP1) or Maddr (ad-hoc initiating STA)
    [ SA field ] = Maddr (S1)
    [ DA field ] = Maddr (S7)
    [ To DS] = False
    [ From DS] = False

## Slide 71
Header Address field contents for each msg type:
DATA (WDS DATA support frame)
  Case 6
(using 236/B3 field names)
    [ BSSID field ] = Maddr (AP4)
      Is actually RA field
    [ SA field ] = Maddr (AP1)
      Is actually TA field
    [ DA field ] = Maddr (S2)
      Is actually DA field
    [ Orig SA ] = Maddr (S1)
      Is actually SA field
    [ To DS ] = True
    [ From DS ] = True

## Slide 72
Header Address field contents for each msg type:
It is proposed that for the WDS Data header, the fields be renamed to accurately reflect their function.
The case 6 example would become:
DATA (WDS DATA support frame)
  Case 6
    [ RA ] = Maddr (AP4)
    [ TA ] = Maddr (AP1)
    [ DA ] = Maddr (S2)
    [ SA ] = Maddr (S1)
    [ To DS ] = True
    [ From DS ] = True

## Slide 73
Header Address field contents for each msg type:
WDS DATA header field names:
FC
RA
DA
TA
Seq #
Frag #
Dur
SA

## Slide 74
Extended B3 Headers
RTS
CTS
ACK
POLL
DATA / MGT
WDS DATA
FC
RA
DA
TA
Seq #
Frag #
Dur
SA
FC
BSSID
DA
SA
Seq #
Frag #
Dur
DA
Dur
FC
DA
SA
Dur
FC
DA
Dur
FC
FC
BSSID
SA

## Slide 75
Mixed mode case corrections to B3 section 2 text.

## Slide 76
B3 Section 2 State Diagram Corrections
Now that we understand the mixed mode cases it becomes clear that the transmitting station state diagram in sec 2.5 is incorrect and needs to be corrected.
The existing states described in B3 section 2 are still correct, but the division of services is not.
The correct dependency on STA state is sets of allowable transmit frames, not services.
Any frame can be received at any time, but if not in a correct state at the receiver (e.g authenticated), an error occurs.

## Slide 77
Station States
State 1:
  Initial start state, Unauthenticated, Unassociated.
State 2:
  Authenticated, not Associated
State 3:
  Authenticated and Associated.

## Slide 78
STA State vs frame types
State 1:
Unauthenticated,
Unassociated
State 2:
Authenticated,
Unassociated
State 3:
Authenticated
and Associated
Successful
Authentication
Class 1
Frames
Class 1 & 2
Frames
Class 1, 2 & 3
Frames
DeAuthentication
Time out
Successful
Association
Disassocaiation
Notification

## Slide 79
STA State vs frame types
Class 1 frames (anytime)
  Legal from within States 1, 2 and 3
  Control Frames
    RTS
    CTS
    ACK
    Poll
  Mgt Frames
    Probe R/R
    Beacon
    Authentication
      Success enables Class 2 frames.
      Failure leaves STA in State 1.

## Slide 80
STA State vs frame types
State 1 -> 2 transition
  Successful Authentication frames sequence transitions to state 2.

## Slide 81
STA State vs frame types
Class 2 frames (IFF Authenticated)
  Legal from within States 1, 2 and 3
  Data frames
    Async data
      Direct only NOT to/from DS
  Mgt frames
    ATIM
    Association R/R
      Success enables Class 3 frames.
      Failure leaves STA in state 2.

## Slide 82
STA State vs frame types
State 2 -> 3 transition frames
  Successful Association frames sequence transitions to state 3.

## Slide 83
STA State vs frame types
Class 3 frames (IFF Associated)
  Legal from within States 1, 2 and 3
  Data frames
    Async Data
      Direct and indirect allowed
  Mgt frames
    Privacy R/R
    Reassociation R/R
    Dissasociation
  continued...

## Slide 84
STA State vs frame types
Class 3 frames (IFF Associated)
  CF Frames
    CF Data frames
      CF DATA
      CF DATA + ACK
    CF Control frames
      CF END

## Slide 85
STA State vs frame types
State 3 -> 2 transition frames
  Dissasociation: STA now Unassociated, so back to state 2 and Class 2 frames.

## Slide 86
STA State vs frame types
State 2 or 3 -> 1 transition events
  Current draft assumes Authentication is aged during inactive periods.
  This can result in “disauthentication” as an error response.
  Disauthenticaion => Disassocaition, so is back to State 1 and Class 1 frames.
    (As shown in B3 state diagram.)

## Slide 87
Conclusions:
Motion: That in order to provide WDS support, the extensions and corrections to B3 contained in 94/248 and 94/248A be adopted and that the changes be incoroprated into draft B4.