## Slide 1
Selective Insertion: A Constrained Alternative to Elements
Michael Fischer and Wim Diepstraten Digital Ocean AT&T

## Slide 2
The Two Roles for Elements
Elements have been proposed for two, distinct purposes:
1. A mechanism for encoding management information that facilitates optional inclusion of information and incremental protocol extension.
2. A mechanism for piggybacking MAC management or control information in frames that lack fields for this information.
We have been confusing ourselves by trying to use one approach for both purposes.
  This proposal explicitly separates the two mechanisms and defines separate rules for each.

## Slide 3
Management Information Encoding
The benefits of “element” encoding for management information are:
  Fields are self-identifying. This permits new information fields to be added to management frames without requiring a new protocol version.
    A new protocol version requires preexisting stations to ignore the new frames.
    Self-identifying fields permit protocol analyzers to easily decode management information.
  Unnecessary fields can be omitted from particular instances of a given frame type without creating ambiguity.
    Fixed fields must always be present.
    Variable length fields also require the receiving station to scan the frame body to locate the successor field.

## Slide 4
Control Information Conveyance
Selective insertion of control information in other frames is a distinct application.
  This may be useful, but must be a very limited amount of information because length extension of CTS and ACK control frames can break the NAV mechanism.
  There are potential uses, such as TX power control, administrative compliance, and selective CRC coverage designation; but no mandatory purposes have yet been identified.
A mechanism to allow for possible use in the future is to add a MIB variable that controls the number of octets (even, 0-8) added to the end of all headers. An abbreviated type representation is then used to identify the inserted information.

## Slide 5
Formats
Element Format
SCode
Link
1
5
3
Octets Specific
to Element
bits:
Link (3 bits): number of subsequent octets
SCode: Selective Insertion Code (0:31)
Element Type
Link
Octets Specific
to Element
More bit M
=1: More Elements Follow
=0: Last Element
Link: 8-bit number of subsequent 2-octet groups (0-255 for 0-510 octets)
Element Type: 7 bits (0:127)
Link
(0 to 7)
(even, 0 to 510)
M
bits:
7
Selective Insertion Format

## Slide 6
Usage Rules
A. Elements shall be used strictly in Management frames, and shall be used for all fields in the payloads of such frames.
B. Elements within the payload of any particular Management frame shall be ordered by increasing element type code value.
C. Stations encountering an element type they do not understand shall ignore that element.
D. Element type codes and selective insertion codes not explicitly defined in the standard are reserved, and shall not appear in any frames.
E. Selective insertion shall apply to all frames, with the NAV settings adjusted to protect these longer frames.

## Slide 7
MOTIONS
1. To adopt the management information encoding mechanism and usage rules proposed in document 94/255.
2. To adopt the selective insertion mechanism and usage rules proposed in document 94/255.