## Slide 1
Type dependent (Smart) DIFS.
By: Wim Diepstraten

## Slide 2
History:
Basic assumption was:
  DIFS is approx. one slot longer then the PIFS.
A number of problems have been identified based on the above assumption:
  Ack may be clobbered by a “Hidden node”.
  Ack for subsequent fragments may be clobbered by a “Hidden node” when Data is send at a Extended rate.
  Ack will be clobered by a “Hidden node” when active priority signalling is used to support DTBS.
  “Hidden nodes” will not be properly synchronized for an priority resolution, causing “leakage” between priority levels.
A single longer DIFS will not resolve all identified problems.

## Slide 3
Problem Description:

## Slide 4
Hidden node problem effects:
Hidden Stations may affect the Ack integrity unless DIFS > 2*IFS + Ack length (Safe DIFS).
  Ack can be overjammed by a station that is Hidden from the Ack generating station.
    This can happen on frames not send with RTS / CTS (like all frames shorter then RTS_Threshold).
    When fragmented data is send at an extended rate.
    When RTS collides (in part of the network), so that not all stations can decode the RTS duration.
Hidden station problem will also affect the Active priority signalling synchronization.
  This will result in “Leakage” between priority levels”
  Needs long DIFS to prevent consistent Ack failure due to jamming by the PaS signal.

## Slide 5
Long DIFS effects:
A Long DIFS will prevent the Ack overlap.
  DIFS > 2*SIFS + Ack length.
  This reduces the medium efficiency.
    Actual IFS could be much shorter after an Ack.
  It does not resolve the PaS synchronization mismatch in the Active priority mechanism.
Solution:
  A more intelligent DIFS specification is needed.
  The DIFS length should be dependent on the Type of the preseding frame.

## Slide 6
Type dependent DIFS specification:
DIFS definitions:
  DIFS-1 = 2*SIFS + Ack duration
  DIFS-2 = PIFS + Slot time
Proposed Algorithm:
  If preceding frame is identified as an Ack then
DIFS = DIFS-2, else DIFS=DIFS-1.

## Slide 7
Mechanisms to identify an Ack:
If within “Data detection” range and CRC is correct:
  Type field will identify the frame as an Ack
If outside “Data detection” range (CRC error) but within CCA detection range.
  Monitor the length of !CCA (Busy medium), and identify the type by monitoring the Busy medium duration.

## Slide 8
Example:
Type dependent DIFS length assures proper Ack protection against hidden node effects.
  Improves efficiency, otherwise DIFS-1 would be always needed.
  Nodes waking up in the middle of a Data frame will likely wait the appropriate long time.
  End of frame reference is indicated by !CCA drop.

## Slide 9
Conclusion:
Type dependent DIFS is highly preferred.
It resolves Ack vulnerability issue in an efficient way.
  Only Long DIFS needed when in Hidden Station situation.
  Also effective if Data rate was not supported by the receive station (CRC error).
It resolves the synchronization mismatch due to the same hidden Station problem during active priority signalling.
  Reduces / eliminates the priority leackage problem.
It also works for the situation where the “Defer range” is beyond the “Data Range”, and when there are CRC errors.

## Slide 10
State Machine changes needed:
{Extra slide to show the state Machine changes}

## Slide 11
Motion:
Move:
To adopt the Smart DIFS mechanism as described in this contribution.