## Slide 1
`
DTBS Standard Specification Details
By: Wim Diepstraten

## Slide 2
Assumptions:
DTBS Service support is optional.
  But all stations need to provide “DTBS-Coexistance” provisions.
Not all Phy’s need to specify DTBS capability support.
A Single State Machine in the MAC can support multiple mechanisms:
  A passive access priority mechanism
  An active access priority mechanism
  No operational access priority mechanism
A given PHY standard shall specify only one access priority mechanism.

## Slide 3
DTBS Support levels:
The DTBS service is optional.
  But coexistence mechanisms need to be implemented in every node to assure proper operation in the presence of stations that do implement the service.
DTBS support levels can be classified in two different levels:
  The DTBS coexistence mechanisms
    This is the access priority mechanism. A part of this needs to be included in all stations to assure coexistance with the DTBS service, even when it is not implemented.
  The DTBS Service interface and priority mapping
    This is the definition of the LLC interface, and its control by means of the QoS parameter, and the translation of this to the priority levels.
    In non-DTBS capable stations a fixed priority mapping is to be assigned.

## Slide 4
DTBS implementation options:
Only minimum coexistance mechanism is to be included in all implementations.

## Slide 5
Coverage of this proposal:
This proposal will only cover the “Access Priority “ mechanism.
  Describes a MAC State Machine to support the full Access Priority mechanism.
  Identifies the minimum coexistance provisions needed.
  Defines the MIB attributes needed.
Discusses AP versus Station relative priority characteristics.
Other DTBS support specifications in particular the LLC interface and Service specifications are documented in doc 94/196, but are not covered by this proposal.

## Slide 6
DTBS Generic priority mechanism:
Extend contention resolution phase with a “Priority resolution Phase”.
If “Medium Free Condition” is met at initial access attempt, then transmission can start immediately without any priority or contention resolution.
  The MFC can be priority level dependent.

## Slide 7
Generic Priority resolution mechanism:
Mechanism can support both active and passive priority resolution method.
Basic (coexistance) Algorithm:
  If “Busy Medium” is detected during PDP period, then defer untill the next Priority Resolution Window (PRW).

## Slide 8
Single State Machine support both mechanisms:
Specified by the PDP and PAS parameters.
  A set of parameters are needed per priority.

## Slide 9
Active Priority example:
Ack is not shown in example.
LP traffic does not contend with HP traffic.

## Slide 10
Priority_Set examples:
"Active priority set" example for a 2 priority system:
  Low priority: PDP = 2 slots, PAS = 0 slots.
  High priority: PDP = 0 slots, PAS = 2 slots.
"Passive priority set" example for a 2 priority system:
  Low priority: PDP = 16 slots, PAS = 0 slots.
  High priority: PDP = 0 slots, PAS = 0 slots.
Assume MFC = DIFS + PDP + PAS.
In a non-DTBS supporting station the default Access Priority setting should be: Low Priority.

## Slide 11
MIB variables:
aNumber_of_Priorities:
  This indicates the number of different priority levels supported by the Phy. A “1” indicates that no priority mechanism is supported.
aPAS_Duration: Determines the duration of the PAS.
Per priority the following parameter sets are required:
  aPDPx: Specifies the PDP duration in usec for priority x.
  aPASx: Specifies the PAS duration in usec for priority x.
Where x indicates the priority level (1 is highest).
Other MIB variables:
  aBusyFilt: Specifies the “Busy medium” condition under which the Backoff algorithm will be exit, to defer untill the next PRW.
MFC can be derived per priority level.

## Slide 12
Basic Transmitter State Machine:
Only needed when
DTBS supported

## Slide 13
Requirements on the Phy:
A new Class definition is needed to allow a Phy independent PAS signal generation.
  Ph-DATA.request(SEND_PAS, param)
  The parameters can be the same as for the START_OF_ACTIVITY class.
The Phy can choose to use the same modulation as used in the PLCP header, with the length determined by the aPAS_Duration MIB variable.
  Other modulation suitable for detection by the CCA detection mechanism can be specified.
The !CCA detection mechanism should be suitable to signal the detection of a PAS signal modulation.

## Slide 14
Draft standard updates needed:
Only needed when
DTBS supported

## Slide 15
Howmany priorities needed:
MAC service maps to:
  Queueing priority
  Access Priority
At least two hierarchical independent priority levels needed to support the main services:
  Asynchronous service Low priority
  Distributed TBS (optional) High priority
Quality of Service (QoS) should map to priority and Queuing priority.

## Slide 16
Additional Priority specification:
Additional relative priorities possible within a service level using Contention Window size differences.
Relative Priority difference between AP and station makes sense.
  Most traffic will be via the AP.
  So AP would generate close to 50% of frames.
  Use of separate hierarchical independent levels for AP is not optimum.
    So in a Multi-priority environment, the AP should not be given a seperate level.
Higher relative Priority settings should only be allowed for an AP.
  Suggest AP_CWmin = STA-CWmin / 2

## Slide 17
DTBS status
Priority mechanism presented to the combined MAC/PHY meeting on Tuesday
  This mechanism was accepted in the MAC group in the September meeting (with a sligth modification).
  The 20B3 draft changes have been distributed.
This MAC will not only need to support the current Phy’s.
  but also the future Phy’s.
  and possibly higher speed extensions of the current Phy’s.
Therefore this mechanism can serve different Phy’s:
  Phy’s that do not support a priority mechanism.
  Phy’s that can support a passive priority mechanism.
  Phy’s that can support an active priority mechanism.

## Slide 18
Motion-1:
Move:
That not all Phy standards need to support the coexistance mechanism for the optional DTBS service provisions. 7/37/15 fails
to add: Each phy will specify if it supports this or not as part of its standard Dave/Leon 8/37/17

## Slide 19
Motion-2
Move:
That the MAC should implement the Access priority mechanism as described in this proposal as documented in document 94_258x. 7/35/18.