## Slide 1
Transmit Power control Provisions
in the MAC
By: Wim Diepstraten

## Slide 2
Why Tx-Power Control:
The Wireless Medium is a scarce resource:
  Only limited bandwidth available per a given Three dimensional area.
  Medium must be reused as much as possible.
  Speed increase will limit the number of useable orthogonal channels also in future bands.
In practice (loaded) systems will be interference limited rather then noise limited.
  Co-Channel interference is the limiting factor.
Reducing the Tx-Power to the “Needed Level” will significantly reduce the co-channel interference level generated.
  This will increase the available bandwidth and so throughput.

## Slide 3
Prior work:
Previous proposals indicate huge benefits:
  Doc 92/76: “The potential of Dynamic Power Control”
    Shows simulation results of Multiple networks with and without Tx-Power Control.
    Significant medium re-use potential between a factor 2 and 8 was demonstrated (92/76).
  Doc 94/59: “Protocol elements needed for Tx-Power Control”
Purpose is Medium re-use efficiency improvement, not a Power consumption saving.
The current Phy’s specify multiple Tx-Level settings associated with a related CCA sensitivity threshold.

## Slide 4
Approach:
Use a transmit level that is suitable to achieve the required SIR at the receiver.
  Do not transmit more then “Needed”.
  This does not mean; “Lower power so that reception is at the minimum sensitivity level”.
Transmitter needs to know the average attenuation to a given destination, to make an informed decision on the Tx-Power Level needed.
If a lower Tx-Level is needed, then this will reduce the interference level in the surroundings.
  This means that we can also reduce the “Defer area”.
The Transmit level can dynamically be REDUCED from its nominal specified level.

## Slide 5
What is the basic mechanism:
A mechanism is needed to measure the attenuation between transmitter and remote receiver.
  Tx knows (controls) its own Tx-Level.
  Rx to put measured RSSI in the returning response (CTS or Ack).
  Tx can calculate the experienced attenuation.
  This knowledge can be maintained per applicable destination.
A Tx-based algorithm can calculate a more appropriate Tx-Level.
If Tx-Level is reduced, then also the “Defer Threshold” can be made less sensitive.
  Result: Lower Tx-Level then less stations to defer for, resulting in a higher throughput per unit area.

## Slide 6
Reduce Power, Increase Throughput:
Transmitters control their Power level from the nominal level DOWN.
Interferers can be closer, so Defer threshold can be less sensitive.

## Slide 7
Minimum MAC Functions needed:
MAC to specify a RSSI field in the CTS and Ack frame.
  Specify 8 bit field with 1 dBm resolution.
  Note that this does not imply a PHY accuracy, but just a range and resolution that the MAC can signal.
MAC needs to be able to adjust the Tx-Level per frame.
MAC needs to be able to modify the CCA-Threshold prior to each access attempt.
The Tx-Level Control algorithm does not need to be specified.
  Only the mechanism to acquire the necessary information.
  And the Phy Control mechanism.

## Slide 8
Gather attenuation information:
Transmitter can determine the attenuation.
  It knows its own ouput power, and receives the RSSI in the Ack.
  The transmitter can adjust its Transmit Power for subsequent transmissions to that same destination.
Phy needs to deliver RSSI type information anyway.

## Slide 9
What is needed in the MAC Standard:
Assumption: Include the minimum requirement in the MAC to allow the Attenuation calculation.
Level-1 provisions:
Specify a fixed field in the CTS and Ack frame.
  8 bits field, assume 1 dB resolution.
  Additional spare 8 bits available if we want word bounded fields (could contain “Background Level’ or a Quality indication).

## Slide 10
Level-2 Provisions:
Level-2 provisions:
Specify a way to allow Phy parameter control independent of a Tx activity which can be issued when the MAC starts monitoring the medium prior to an actual access.
  Add a Transmit_Enable parameter to the
Ph-DATA.request(START_OF_ACTIVITY,params), so that parameters can be changed independent of Transmit activity.
  Specify a separate class
Ph-DATA.request(Set_Param,params), to allow change of the defer threshold.
Include Tx-Power_level and CCA_threshold parameters in the MAC / PHY interface.
State Machine change may not be needed.

## Slide 11
Conclusion:
Lets prepare the frame formats to support the implementation of this important medium sharing function.
  Its use can be optional.
  This is possible because a mix of stations that do and don’t implement Tx-Power Control can work together without any problem.
A next level of support would be to specify the necessary provisions to control the Tx-Power_Level and CCA_Threshold.
  Currently no mechanism is available to change the Phy parameters per frame, but independent of transmit activity.

## Slide 12
Motion:
Move:
To add a fixed field to the CTS and Ack frame to report the received RSSI level. 14/38/13 fails.
Move:
To specify a Transmit_Enable parameter to the basic Ph-DATA.request(START_OF_ACTIVITY,params) parameters, so that they can be changed independent of Transmission activity.