## Slide 1
Analysis of B3 vs. MID
Revision 1.0
David Bagby
Bob O’Hara
Dave Roberts
Advanced Micro Devices
One AMD Place
Sunnyvale CA, 94088

## Slide 2
Common Ground
There was a lot of concensus reached around B3 functionality
Alteration of NID to unique address
FC field definitions
Uniform 32-bit CRC
Textual ESSID representation

## Slide 3
Disagreement Surrounds WDS Support
All believe that WDS is important
Two solutions: 94/248 vs. MID
Argument could be characteriszed as: stablility vs. efficiency

## Slide 4
B3 Summary Description
B3 uses directed addressing for all frames in a transmission “dialog”
RTS carries return address for CTS, Data carries return address for ACK

## Slide 5
Issue with B3
Problem results in wireless distribution system because 4 addresses are needed to be carried in a data frame: immediate transmitter, immediate receiver, original source, and final destination
B3 only specified that 3 addresses be carried in a data frame
Result was that second AP in forwarding sequence could not send ACK for Data frame to first AP

## Slide 6
MID Summary Description
MID attempts to remedy situation by making CTS and ACK non-directed
A token (MID) is used to match a CTS with an RTS and an ACK with Data
Transmitter “randomly” picks a MID value from 11-bit space (2048 choices)
MID is included with RTS and Data and returned with CTS and ACK
MID uses the bits B3 used for sequence number, plus a couple more, and so is also used for MPDU duplicate detection

## Slide 7
Problem with MID
The problem with the MID is the same problem MPDUID originally had
Two stations in close proximity can choose the same MID value and frames in a dialog can become miscorrelated
This can lead to errored frames not being retried and dropped

## Slide 8
Example of Miscorrelation
STA 1
STA 2
AP 1
AP 2
RTS/Data,
MID = x,
STA 1 finds
bad CRC
RTS/Data,
MID = x
AP1 hears STA 2’s
response and thinks
it’s from STA 1
CTS/ACK,
MID = x

## Slide 9
MID Answers to Miscorrellation Problem
It’s unlikely
It’s only a problem if the frames are the same size
Therefore, it’s not a problem

## Slide 10
“It’s Unlikely...”
We have an 11-bit token
MID proponents claim random number means stations are highly unlikely to choose the same token
  1 in 2048 chance of choosing any particular value
MID proponents claim that even if they do, it probably won’t happen twice
  i.e., probability is 1/(2048)^2 = very small

## Slide 11
A Look At “Random” Numbers
“Random” numbers are generated using an algorithm operating on a seed value
  Linear Congruential
  LFSR
They are “random” at a macroscopic scale (spectral test, etc.) but not at a microscopic scale
Same seed value always generates same output
Seed value for next choice is the output of previous choice
  Rn = F(Rn-1)
PRNG results in a sequence of numbers

## Slide 12
Example PRNG
A 3-bit linear congruential
  F(n) = (5n + 3) mod 8
  RN(n) = F(RN(n-1))
This produces the sequence:
  0, 3, 2, 5, 4, 7, 6, 1, 0, 3, ...
The last RNG generated is used as the seed to generate the next random number, also known as the state of the generator
Generators that cycle through all possible states before repeating are called maximal length generators
  We want this property for a MID for duplicate detection

## Slide 13
PRNG/MID Implications
Given a particular state value, the PRNG “picks” the next value in sequence with P=1. It picks all other numbers from set with P=0
Note that for the purposes of correlating frames in a dialog, we don’t care what the MID value is. 13 is just as good a 1238.
Note also that a simple counter has the same property as above. A PRNG is just a strange counter
Since we don’t care what the value of the PRNG output is, a counter is just as good as a PRN.
The MID might as well be a simple counter!

## Slide 14
Stations Can Become “In Sync”
Even if stations start out (at powerup) with different positions in the “random” sequence, traffic patterns can cause them to reach the same position
Once they reach the same position, the probabily gets very high that they will collide
  One station’s position will “crossover” the other station’s
This becomes much more likely the more stations you have
If outbound traffic patterns are similar, then stations will tend to stay in sync for a while
  It may take them a long to reach this point, but it will also take them a long time to get out of it

## Slide 15
Introducing More Randomness
Use a larger seed
  E.g., use low order bits of larger seed as PRN
  Breaks maximal length property
Generating a new MID for Data/ACK than that used for RTS/CTS doesn’t help
  You’ll generate the same value!
  You’ll use duplicate detection tags more quickly, leading problems
In general, doing anything breaks duplicate detection needs

## Slide 16
Randomness Conclusions
“Random” numbers aren’t as random as you might think
They are really no better than a sequence number
Once stations become sync’d, the probability is quite high that collisions will occur
  Probability of stations becoming sync’d increases greatly with increase in number of stations
Trying to change this breaks duplicate detection properties
  Maximal lenght property no longer exists which increases the probability of a duplicate detection failure

## Slide 17
“It’s Only A Problem With Frames Of Equal Size...”
False: It’s a problem with all frames that end at the same time
AND, frames of equal size are actually very likely

## Slide 18
Problem Window
The problem occurs when a transmitter waits for a reply and sees what it thinks is a valid response
This occurs if a false ACK or CTS is returned within a SIFS after the transmitter stops
Different start times are acceptable as long as stop times are within a SIFS of each other

## Slide 19
CCA Doesn’t Necessarily Help
STA 1
STA 2
AP 1
AP 2
AP 1’s CCA can’t detect AP2
so it may start a shorter transmission
after AP 2 has already started

## Slide 20
Probability of STAs Choosing Same Size Is High
Frame sizes are not randomly distributed
  I measured the sizes of 1236 TCP/IP frames
  There were 25 different sizes
Of 1236 frames, 800 were 576 bytes (65%)
Assuming random choosing (false), then with 5 nodes the probability that any two choose 576-byte frames is 94%
  See following graph
Reality is that frame sizes are not “chosen” randomly, which makes things worse
  Station doing file transfer outbound will send all large frames (the data)
  Station doing file transfer inbound will send all short frames (network layer acknowledgements)

## Slide 21
Probability of Two Nodes Choosing 576-Byte Frames
Prob
# of Nodes
Individual Probability
Of Choosing a 576-byte
Frame

## Slide 22
MID Conclusions
“Random” numbers aren’t random
  PRN is no better than sequence # for MID purposes
MID collision is more probable than first glance might suggest
  Stations can get in sync and stay in sync for quite a while
  Problem can occur many times in succession
Frame sizes cluster and probability that two stations choose same frame size is high with only moderate number of nodes
All probabilities increase with larger number of nodes (and increase is non-linear, as in case of two stations choosing same size frame)
This IS a problem!

## Slide 23
Arguments Against 94/248
Efficiency
Simplicity

## Slide 24
Efficiency
Some say MID is more efficient than B3
Using MID results in dramatic reduction in frame header overhead
Frames B3 MID Delta
RTS/CTS/Data/ACK 60 48 -20%
Data/ACK 34 30 -11.8%
Yes, but this is a meaningless measurement!

## Slide 25
Throughput Delta
The only meaningful measurement is change in throughput
  Users don’t care how big the frame headers are!
AMD created a spreadsheet to calculate throughput based on total dialog exchange parameters (PHY preamble, SIFS/DIFS time, realistic payload sizes, etc).
  We even figured in the decrease in throughput caused by retrys caused by increase in frame error rate caused by more bits being transmitted
  This spreadsheet was distributed to the email reflector

## Slide 26
Throughput Delta Results
Payload size RTS/CTS MID/B3 Diff
585 Y 1.59%
585 N 0.59%
39 Y 5.75%*
39 N 2.92%
585-byte payload represents 576-byte IP or IPX packet with 9-byte LLC/SNAP
39-byte payload represents 30-byte minimum size IPX packet with 9-byte LLC/SNAP
* Don’t do this! But we already knew that.

## Slide 27
Further Throughput Results
Largest deltas occur when payload is small
  As expected...
But throughput is bad at this point anyway...
  Headers and IFS times dominate in any case
Expected throughput for B3 at 39-byte payload w/o RTS/CTS is only 284.5 Kbps
Using a MID rather than B3 increases throughput to only 293 Kbps
Using a MID isn’t going to increase user satisfaction any...

## Slide 28
Simplicity
MID Proponents claim that MID results in easier state machine design
This is true
  Receiver copies MID unconditionally to the CTS or ACK
But this is putting the cart before the horse
The MID scheme doesn’t work reliably!

## Slide 29
Overall Conclusions
The MID is unreliable
Its proponents admit this but claim that the probability of failure is low
BUT they haven’t put forth the detailed analysis to show this!
We’ve shown that the probability can be quite high under reasonable loading conditions and station count
Although B3 directed frames result in a small decrease in throughput (<3%), B3 doesn’t rely on probabalistic arguement to show that it works