## Slide 1
Nov ‘94 MAC group Report
MAC
PHY
LLC

## Slide 2
Misc Subjects
August MAC minutes approved

## Slide 3
Papers / subjects / motions

## Slide 4
August papers
None

## Slide 5
WDS
248: B3 extension for WDS
  no motions made
254: Frame header improvements
  no motions made

## Slide 6
WDS
Discusion of 248, 254, resulted in a joint proposal (290r1) for WDS support.
270: Direct addressing vs MIDs.
  Presenrtation skipped due to compromise motion w/o objection of authors.

## Slide 7
WDS
290: A compromise Proposal for Revision to the MAC Frame Formats to Support WDS.
  One revision to 290 to reflect desired header field order.
  290 and 290R1 major points:
    248 base
    Reorg fields within headers like 254.
    EP bit included
    Wim’s data (re MID miscorrelation) to be considered on merits when avail.

## Slide 8
WDS
290R1 Motion:
  Moved: To adopt 290R1 as presented.
  MAC vote: 27-1-6 Passed
  Plenary Vote:

## Slide 9
WDS
248 B3 Section 2 corrections:
  Motion: that the corrections to B3 sec 2 contained in slides 77 thru 86 of 94/248A be adopted and incorporated into the next draft (the text / diagram needed is contained in those slides).
  MAC vote: 19-0-7 Passed
  Plenary Vote:

## Slide 10
Elements
240: elements for bss sync.
  moved: to adopt the changes from page 4 of 94/240 - w/o bottom sentence.
  MAC vote: 21-1-6 Passed
  Plenary vote:

## Slide 11
Elements
282: Elements encodings.
  Motion: to adopt the changes proposed in 94/282.
  MAC vote: 10-14-4 Failed

## Slide 12
Elements
255: Selective Insertion, a constrained alternative to elements.
  Motion: to adopt usage rules A thru D from slide 6 doc 94/255A and the element format picture from slide 5 from 94/255a.
  Amended: remove the phrase “and selective insertion codes” from bullet D on slide 6 of 94/255A and change bullet A to “... and shall be used after any fixed fields in the payloads of such frames.”
  MAC vote: 16-4-4 Passed
  Plenary Vote:

## Slide 13
Misc MAC specs
285 - mac specification issues.
  motion: That timing synchrounization be mantained in a ad-hoc network, by adjusting a syncrounized sation timing reference to be the average of itself and any time-stamp recieved from anouther station in that network.
    MAC vote: 20-0-3 Passed
    Plenary vote:

## Slide 14
Misc MAC specs
285 - mac specification issues.
  motion: that the estimated power saving state of another station be based on the power mgt info xmitted by that station and additional info available locally (such as history of failed transmission attempts) which may be deemed relevant.
    MAC vote: 21-0-2 passed
    Plenary vote:

## Slide 15
Misc MAC specs
285 - mac specification issues.
  motion 3: That in a network there shall be al least one node that is awake any given time to respond to probes. In an ad-hoc network probe responses shall be sent by the station that sent the last beacon. Stations do not need to cancel a pending probe response transmission if they observe a successful probe response from another sta in the same network.
  MAC Vote: 17-1-9 Passed
  Plenary Vote:

## Slide 16
Security
249: Wired Equiv Privacy
  Adopted with modification that:
  The specific PRNG algorithm used within the proposal shall be unspecified in the draft at this time (and the issues referred to be left open). Reviewers are encouraged to comment in letter ballot responses on appropriate PRNG algorithms for consideration. The “WEP algorithm specification” section of doc 94/249, when transfered into the draft, shall be replaced with the text: “Reviewers are encouraged to comment on appropriate PRNG algorithms for adoption by 802.11.”
  Original MAC adoption vote: 23-2-2 Passed
  Modification adoption MAC vote: 19-3-8 Passed
  Plenary vote:
    (To accept proposal including modifications)
802.10 Liason action:
  Ask 802.10 for magic number.

## Slide 17
State machines
253: Updated MAC state machines
  Paper did not arrive at mtg.

## Slide 18
DTBS
258: DTBS draft text
  Some discussion, paper handled in Joint M/P session.

## Slide 19
Multi-rates
247: Multirate Provisions in the MAC
  Some discussion, paper handled in Joint M/P session.

## Slide 20
MAC frame check sequence
245: Need for partial MAC frame check sequence checking.
  802.2 liasion not present at mtg, no one to present paper, paper not discussed.

## Slide 21
B3 comments
251: Comments on B3
  Points important to authors:
    mobility
    Authentication
    compression
    privacy in ad-hoc
    DTBS channel access mechanism missing.
  no actions asked for by the authors, just informative before LB comments.

## Slide 22
More Function
283 - Liberating the more funciton.
  Motion 1: To permit Stations, as well a APs, to use the More indication when additional buffered frames are present.
    Mac vote: 26-0-3 Passed
    Plenary vote:

## Slide 23
More Function
283 - Liberating the more funciton.
  Motion 2: To combine the Sequence numer and Fragment number fields into a 16-bit field, while reducing the size of the Fragment number sub-field to 4 bits with a corresponding increase in the size of the Sequence Number sub-field.
    MAC vote: 24-1-5 Passed
    Plenary vote:

## Slide 24
More Function
283 - Liberating the more funciton.
  Motion 3: To adpot the frame header changes affecting the More, Power management, Fragment Number, and Sequence Number fields described in submission 94/283A.
    MAC vote: 26-1-3 Passed
    Plenary vote:

## Slide 25
WLAN requirements
284: Boeing paper re req for wlan
  no author present
  No paper avail for mac group
  not discussed.

## Slide 26
TX power control
259: MAC TX power control
  Discussed, handling moved to joint M/P session.

## Slide 27
PCF Based TBS
269: PCF TBS
  Motion: to adopt paper 269v2 into draft std w/o the last 2 lines from page 3 of 269v2.
  MAC Vote: 15-1-8 Passed
  Plenary vote:

## Slide 28
Type dependent DIFS
257: Type Dependent DIFS
  No motion made by author.

## Slide 29
CF-Async simplified.
252: Simplified Contention Free
  Motion:To adopt the changes to contention free async operation, including frame types / subtypes, usage rules, IFS duration, etc. as defined in doc 94/252 and to modify the updates to section 4.1.2.1.2 to designate the “reserved” frame type (type code = 11) as “time bounded” frame type.
  MAC vote:18-2-12
  Plenary vote:

## Slide 30
MIB
293 MIB results from mon ad-hoc mtg
  Motion: to adopt MIB changes recommended from Monday ad-hoc MIB mtg.
  MAC vote: 28-0-6 Passed
  Plenary Vote:

## Slide 31
Pushed Off schedule:
None!

## Slide 32
Goals for January 95
Need guidance from 802.11 chair:
  Subject limitations resulting from the open LB during the mtg?
  Other work required?
    Conformance / test?
Motion: resolved that the mac group recommends that the January mtg be:
  1) Held as scheduled: 22
  2) Canceled. 3
  3) Abstain. 8

## Slide 33
MAC group report
That’s all folks...