## Slide 1
Liberating The “More” Function
  Michael Fischer Digital Ocean, Inc.

## Slide 2
Reasons to modify the More function
1. The use of the More FC-bit is unnecessarily restricted in draft 20b3.
  A class of potential benefits are precluded.
2. The More indication can merge into the Power Management FC–bits with no loss of functionality.
  This groups together indicators primarily relevant to power conservation management.
  A bit position in the FC field becomes available for other usage.
3. By vacating the More FC bit position, the Last Frag (F) bit can be relocated to the FC field.
  The F–bit logically belongs in the FC field.
  Removing the F–bit from the Fragment Number field permits a longer dialog token or sequence number.

## Slide 3
Removing the unnecessary restriction
  20b3 restricts the More function to indicate that additional frames are queued at an AP.
    Stations are explicitly required to set More =0 (page 48, lines 16-19).
    There is no functional benefit from this restriction.
  Stations with >1 queued frame for the same wireless recipient should be allowed (not required) to set More =1. Benefits include:
    A PCF could give a station with more queued frames additional transmission opportunities during a given CF-period.
    The sender of an ATIM could indicate additional queued frames to the same recipient.

## Slide 4
Merging More into Power Management
  The Power Management bits can encode Power Save Mode + More:
00 = Active (CAM/TAM), no More frames 01 = Power Save Polling (PSP) 10 = Power Save No-Polling (PSNP) 11 = Active (CAM/TAM), More frames
  TAM and CAM differ in the need for AP buffering.
    This can be indicated as part of association/reassociation.
  The dynamic indication is “Active” vs. “PSxx”
    The transition to Active from PSP or PSNP is the call for the AP to send buffered frames.
    The transition from Active to PSP or PSNP is the signal for the AP to resume buffering frames.
    The duration of “temporary” activity is controlled by the station

## Slide 5
Relocating F-bit into FC-field
  The “Last Fragment” bit moves to the FC–bit vacated by More.
    This indicator is a frame control function.
    This is presently the only 1–bit header subfield outside the FC–field.
  The Sequence Number and Fragment Number fields are combined as a 16–bit field with a 12–bit Dialog Token or Sequence Number and a 4–bit Fragment Number.
    16 fragments are plenty for 2304–byte MSDUs.
    A 12–bit uniqueness value reduces the risk of discarding a new frame as a duplicate.
    A 12–bit Dialog Token is available (for proposal 94/254) without giving up the reserved FC–bit.
Dialog Token or Sequence Number
Fragment

## Slide 6
MOTION #1
1. To permit stations, as well as APs, to use the More indication when additional buffered frames are present.

## Slide 7
MOTION #2
2. To combine the Sequence Number and Fragment Number fields into a 16–bit field, while reducing the size of the Fragment Number sub–field to 4 bits with a corresponding increase in the size of the Sequence Number sub–field.

## Slide 8
MOTION #3
3. To adopt the frame header changes affecting the More, Power Management, Fragment Number, and Sequence Number fields described in submission 94/283.