## Slide 1
How to specify the IFS timing in the Standard
By: Wim Diepstraten

## Slide 2
Approach:
The xIFS’s specifications are PHY specific.
The xIFS’s can only be measured on the medium.
So the specifications apply to time gaps on the medium.
The reference for these timings are the end of a frame on the medium.
MIB parameters need to be specified to allow a single MAC to run on multiple PHY’s.
Specification should be such to allow time slotted implementations.

## Slide 3
Detailed delay components:

## Slide 4
Basic parameters:
SIFS:
  Time it takes a MAC to decide to react on the frame received, and to turnaround the transceiver, until Transmit energy is put on the medium, OR the Tx/Rx turnaround, whichever is larger.
Slot_Time:
  Time between a MAC decision to turn the transmitter on, untill all stations are aware that the medium is occupied.
  This relates to the meaning of Slot_Time in the CSMA/CA mechanism.
The PIFS and DIFS are derived from the basic parameters SIFS and Slot_Time by:
  PIFS = SIFS + Slot_Time
  DIFS = SIFS + 2* Slot_Time
Tolerance specification: (Assume nominal +/- Tolerance)

## Slide 5
Medium and MAC xIFS relation:
Slot Boundary definitions are different for MAC and PHY, but they are all referenced to the end of the last frame (end of last bit?).

## Slide 6
What MAC evaluation delay is needed:
There are two basic decision types for a MAC.
  1: Interpret frame correctness before start transmission.
  2: Sense CCA/NAV and Transmit if medium is available.
Decision type-1: Applies to SIFS only:
    Reaction of Ack to a Data frame
    Reaction of CTS to a RTS frame
    Reaction of Data following CTS
    Reaction of Data following Ack (fragmentation)
    Reaction of Point Coordinator to received frame.
  Needs a minimum MAC delay to allow MAC level processing.
    Need at least CRC validation before Tx-goahead.
    We need to fix a time for this.
Decision type-2:
  Applies to PIFS/DIFS and transmissions after backoff.
  MAC delay associated with this is assumed minimum, close to zero.

## Slide 7
Need MIB specifications to support it:
Ed Geigers approach in doc 95/039 is a good starting point, but we need to use events on the medium as a reference.
  Specify nominal values in the standard.
  Specify MIB variables containing the implementation deviation.
The MIB needs to specify those parameters that allow a MAC to calculate:
  Tx_SIFS
  Tx_PIFS
  Tx_DIFS and subsequent slots

## Slide 8
Timing references:
There are two different timing references for the MAC.
  1: The end of an incomming frame.
  2: The end of a previous transmission.
    This applies to any subsequent transmission, but requires to execute backoff, in which case it only affects slotting.
    This applies to SIFS gaps in fragmented Broadcast frames.
TX_SIFS timing in the MAC:
  TX_SIFS-1 = SIFS - Rx_Delay - Tx_Delay. Rx as reference
  TX_SIFS-2 = SIFS. Tx as reference

## Slide 9
MIB parameters needed:
PHY dependent MIB parameters:
  Slot_Time
  Rx_Delay
  Rx_Delay_Delta
  Tx_Delay
  Tx_Delay_Delta
MAC dependent MIB parameter.
  MAC_Delay-1; MAC_Delay-2 as needed
Resulting: SIFS = Rx_Delay+MAC_Delay+Tx_Delay (on medium)
  This time should be such that Tx/Rx_turnaround time is such that the next frame can be successfully received.
Basic Equations:
  TX_SIFS = SIFS - Rx_Delay + Rx_Delay_Delta - Tx_Delay + Tx_Delay_Delta.
  TX_PIFS = TX_SIFS + Slot_Time.
  TX_DIFS= TX_IFS + 2*Slot_Time

## Slide 10
Conclusion-1:
Motion:
To accept the specifications of SIFS, PIFS and DIFS, according to this document to be:
SIFS = Rx_Delay+MAC_Delay+Tx_Delay (PHY specific)
PIFS = SIFS + Slot_Time
DIFS = SIFS + 2 * Slot_Time
As measured on the medium, with:
Slot_Time:
  Time between a MAC decision to turn the transmitter on, untill all stations are aware that the medium is occupied.
Text to reflect this decision to be specified in section 5.2.13 (DCF Timing relations).

## Slide 11
Conclusion-2:
Motion:
To specify in the standard the MIB parameters and the equations needed to allow the MAC to generate the necessary timing gaps (SIFS, PIFS, DIFS).
PHY dependent MIB parameters:
  Slot_Time
  Rx_Delay
  Rx_Delay_Delta
  Tx_Delay
  Tx_Delay_Delta
MAC dependent MIB parameter.
  MAC_Delay-1; MAC_Delay-2 as needed
Basic Equations:
  TX_SIFS = SIFS - Rx_Delay + Rx_Delay_Delta - Tx_Delay + Tx_Delay_Delta.
  TX_PIFS = TX_SIFS + Slot_Time.
  TX_DIFS= TX_IFS + 2*Slot_Time

## Slide 13
MAC Timing reference issues:
There are two different timing references for the MAC.
  1: The end of an incomming frame.
  2: The end of a previous transmission.
    This applies to any subsequent transmission, but requires to execute backoff, in which case it only affects slotting.
    This applies to SIFS gaps in fragmented Broadcast frames.
It should be clear what signalling provides the MAC timing reference:
  1: The CCA indication.
    How is it derived by the PHY:
      For a valid reception?
      For a reception with failing PLCP CRC check?
  2: The last bit transmitted:

## Slide 14
Other related parameters:
Ack_Timeout:
  The time after which a MAC can decide whether an expected Ack has failed to return.
T3?:
  The time following a RTS frame after which a MAC can decide whether subsequent Data has followed a sucessfull RTS / CTS exchange.
Retry Limits:

## Slide 15
Ack Timeout specification:
Max Medium delay (for Ack response) = 5 usec.
  not the medium delay assumed in Time Slot.