## Slide 1
Inter Access Point Protocol
Prepared by:
Aironet & Lucent Technologies
Presented By: Wim Diepstraten
Mike Trompower
Notes: 1

## Slide 2
Agenda
Introduction
Goals
History
Requirements
Architecture
Specifications
Conclusion
Notes: 2

## Slide 3
Introduction
Wireless Networks introduce new concepts
  Medium is unbounded, but range is limited.
  End nodes can be mobile.
IEEE 802.11 is developing a Wireless LAN standard.
  Standard is in final stage, expected to go to Sponsor Ballot.
  802.11 defines MAC and PHY specifications, “Air Interface” only.
  Provides basic primitives to support mobility.
IEEE 802.11 extends its coverage beyond the range of its PHY through a Distribution System.
  Distribution System connects multiple AP to form an ESS.
  However, the Distribution System is not specified.
  This represents an interoperability issue at the system level.
Notes: 3

## Slide 4
IEEE 802.11 architecture
IEEE 802.11 defines the “over the air” protocol.
Notes: 4

## Slide 5
IEEE 802.11 architecture
IEEE 802.11 defines the “over the air” protocol.
Range extension through use of a Distribution System.
Notes: 5

## Slide 6
IEEE 802.11 architecture
IEEE 802.11 defines the “over the air” protocol.
Range extension through use of Distribution System.
AP to AP protocol is not defined by 802.11.
?
Notes: 6

## Slide 7
The Missing Link
A standard protocol for Access Point communication.
Notes: 7

## Slide 8
The Missing Link
A standard protocol for Access Point communication.
A particular Distribution System Medium.
  based on existing LAN standards
Notes: 8

## Slide 9
Goals of this initiative
Specify the “missing link” for Wireless LAN systems interoperability.
  to support mobility of end nodes
Enable multivendor Distribution Systems.
  based on existing network standards
  by specifying IAPP, the protocol between Access Points
Aironet , Digital Ocean and Lucent Technologies have developed an initial specification.
  It is published as an “open voluntary standard”.
  To solicit feedback by interested parties
Notes: 9

## Slide 10
History
IEEE 802.11 started work in 1990.
  Its PAR specifies support for range extension and mobility.
  802.11 decided early on not to specify the Distribution System.
    it is beyond IEEE 802 MAC level authority
    Distribution System requires Network and Transport layer functionality
  802.11 specifies the services the Distribution System must provide
There were a number of attempts to specify interoperability functions on the Distribution System.
  The term IAPP was introduced in IEEE P802.11-94/17.
  IEEE P802.11-95/188 by Michael Fischer proposed a limited Distribution System by introduction of the MESS.
Aironet, Digital Ocean and Lucent Technologies provide an initial specification of the IAPP.
Notes: 10

## Slide 11
General IAPP requirements
Build upon specified 802.11 functionality.
Use existing networks to serve as the Distribution System Medium.
  Existing 802 wired Networks
  802.11 Wireless LANs
Support a wide range of Network transfer protocols.
  Support MAC level Bridge based Data Link level implementations
  Support Router based Network layer implementations
    Allow multi-segment IAPP
    Not intended to solve addressing issues for Network layer mobility.
Allow for different network Management topologies.
Provide mechanisms to allow APs to communicate with each other.
The IAPP should be flexible and extendable.
  allow proprietary extensions
Notes: 11

## Slide 12
Architecture background
The 802.11 architecture is designed to allow diverse Distribution System implementations:
  The DS may be created from different technologies including but not limited to current 802.x wired LANs.
  It is not constrained to either Data Link or Network layer.
  Its addressing space can be separate from the addressing space used in the DS or integrated wired LAN.
This IAPP initiative focuses on a set of solutions representing a typical case.
  Distribution Systems based on existing 802.x wired LANs.
    The Distribution Medium (DM) can be an existing LAN with stations connected.
    With 802.11 and DM using the same MAC level address space.
Notes: 12

## Slide 13
IAPP Architecture
IAPP defines a communication mechanism between APs.
  to allow for coordination between APs
  to exchange channel or hop sequence information
IAPP allows AP MAC Management entities to communicate.
  to enable a station to disassociate from the “Old AP”
  to redirect the Distribution System filtering functions
Two transfer protocols will be implemented.
  UDP/IP
    used whenever an IP address is present in the AP
  802.2 Sub-Network Access Protocol (SNAP)
    for simpler systems when no IP Address is present
Notes: 13

## Slide 14
IAPP Architecture
Distribution System Medium can be built from existing networks
  including 802.11 wireless LANs
802.11 MAC
or
IAPP Handler
UDP
IP
IAPP-
SNAP
MAC
Management
interface
other network(s)
Access Point Management
Bridge
MAC
MAC
Router
802.11 MAC
or
IAPP Handler
UDP
IP
IAPP-
SNAP
MAC
Management
interface
Access Point Management
other network(s)
DSM
DLC
DLC
Notes: 14

## Slide 15
General IAPP Message Format
Protocol Header: SNAP or UDP/IP protocol Header.
Ver#: IAPP Version number.
PDU-Type: Identifies Specific PDU.
n * PDU element: PDU data element fields.
Following 802.11 element format
  Element-ID: Element identification
  Length: Length of element data field in octets.
  Data: Data of the element.
Messages can be specifically addressed to one AP, or group addressed to all APs.
Notes: 15

## Slide 16
Basic IAPP protocol functions
IAPP Announce Protocol
  to facilitate AP awareness and coordination
  to support the formation of Wireless Distribution Systems
IAPP Handover Protocol
  to extend the 802.11 Re-Association MAC management function across the distribution system
Notes: 16

## Slide 17
IAPP Announce Protocol
IAPP Announce protocol:
  Inform other APs and/or network management functions that a new AP has become active.
  Inform other APs and/or network management functions of the continued operation of that AP.
  Allow APs to communicate their configuration.
  Allow for network Management function to provide AP coordination.
Associated PDU Types:
    Announce.Request
    Announce.Response
Supports centralized or distributed AP coordination, and allows autonomous operation in uncoordinated environments.
Provides a means for Wireless APs to “Register” with other APs.
  enables creation of a Wireless Distribution System
Notes: 17

## Slide 18
AP management topologies
Topologies supported:
  Uncoordinated APs
  Centralized AP Management
  Distributed AP Management
Provides for “Management level AP awareness”
  Needed to configure wireless Distribution Systems.
  This is not covered by 802.11.
Notes: 18

## Slide 19
Uncoordinated APs
New AP generates Announce.response.
  sent as a general Broadcast
Allows AP to identify itself and its operational status.
Uncoordinated AP
Notes: 19

## Slide 20
Centralized AP Management
Announce.request generated by new AP.
  AP manager will respond (with Master bit set).
AP manager can query AP’s by sending Announce.requests.
  with “Response desired” enabled
New AP announces to AP manager
AP Manager query of all APs
Notes: 20

## Slide 21
Distributed Control
New AP generates Announce.request
  with “Response desired” enabled.
Other APs send Announce.response
New AP generates Announce.response
  Indicating its operational status.
APs can generate Announce.response messages periodically as an “Alive indication”.
Distributed Control
Notes: 21

## Slide 22
IAPP Handover Protocol
IAPP Handover Protocol:
  Inform the “old AP” that a station has associated with a new AP.
    To release resources assigned to that station by the old AP.
    To allow optional frame forwarding of buffered frames,
    or discard them.
  Update filter tables of intermediate MAC layer Bridges.
    By using the “Mobile Station Source address” as the SA of the handover request message.
Associated PDU Types:
    Handover.Request
    Handover.Response.
Notes: 22

## Slide 23
Handover procedure
Relationship between 802.11 reassociation and IAPP handover.
802.11
IAPP
Notes: 23

## Slide 24
PDU Elements
ESSID as in 802.11
BSSID as in 802.11
Old BSSID as in 802.11
MS-Address Mobile Station address
IAPP capability/Status
Announce interval in Kusec
Handover Timeout in Kusec
PHY type identify 802.11 PHY
Regulatory Domain as in 802.11 MIB
Channel PHY dependent
Beacon Interval as in 802.11
OUI Company identifier Precedes block of proprietary elements.
  Proprietary elements Following OUI Company ID only.
Notes: 24

## Slide 25
Element Usage
Element use per PDU type:
  fixed elements are specified
  other elements are optional
Proprietary elements are allowed.
  receivers ignore elements they don’t understand
OUI Company ID precedes block of proprietary elements.
  This prevents Element ID conflicts.
    (OUI, Element ID) tuple will be unique
Notes: 25

## Slide 26
Conclusion
IAPP provides the “missing link” in Wireless networking.
  interoperability between multiple vendor AP implementations
IAPP is compatible with IEEE 802.11.
  it builds upon the 802.11 functionality
IAPP enables a multitude of AP management schemes.
  with support across Bridges and Routers
IAPP is scalable for the future.
  element structure allows for migratable extensions
  proprietary extensions are allowed
Notes: 26

## Slide 27
How to continue
Short term
  Comments on the IAPP are solicited from all interested parties.
  Specification is maintained by Aironet and Lucent Technologies.
  New versions are distributed via:
    IEEE Email reflector
    Web sites
  Aironet, Digital Ocean and Lucent Technologies agree to implement IAPP in their 802.11 products
Long term: Consensus of the meeting:
  A lot of interest to move forward with this proposal.
  Proposal to present it to 802.1 Technical plenary to see where it should belong.
    Do this in November, to prevent impact on 802.11 Sponsor ballot
    Would be very useful as informative annex to 802.11, but not now.
Notes: 27