## Slide 1
IEEE 802.11 DSSS PHY
Characteristics:
2.4 GHz ISM band (FCC 15.247)
1 and 2 Mbit/s datarate (DBPSK and DQPSK modulation)
> 10 dB processing gain
spreading sequence 11 chip Barker sequence

## Slide 2
Operating frequency range
2.4 to 2.4835 GHz
11 overlapping channels with centerfrequencies from 2412 MHz to 2462 MHz with 5 MHz spacing

## Slide 3
Spreading sequence
Each symbol is spreaded with 11 chip Barker sequence
+1, -1, +1, +1, -1, +1, +1, +1, -1, -1, -1
chipping rate 11 MHz
Chipping rate of 11 MHz over 1 MHz symbols gives a processing gain of theoretical 10.4 dB

## Slide 4
Datarates and Modulation
1 Mbit/s Differential Binary Phase Shift Keying
2 Mbit/s Differential Quadrature Phase Shift Keying
Symbol rate is 1 MHz.

## Slide 5
Encoding tables

## Slide 6
Scrambler
All bits are being scrambled with:

## Slide 7
Transmit Power level
The maximum allowable output power is 1000mW according to FCC 15.247

## Slide 8
Transmit Spectrum Mask

## Slide 9
Spurious Emissions
The DSSS PHY shall conform with in-band and out of band spurious emissions as set by regulatory bodies
For USA: refer to FCC 15.247, FCC 15.205 and FCC 15.209

## Slide 10
Antenna Gain
Not defined in standard, but should be conform FCC 15.247

## Slide 11
Carrier suppression
Carrier suppresion shall be at least 15 dB below the peak sin(x)/x power spectrum