## Slide 1
Introduction of IEEE P802.11
Prepared by Vic Hayes, Chair, AT&T
Utrecht, the Netherlands

## Slide 2
Representation
For the Frequency Hopping medium
  Peter Chadwick, G3RZP
    GEC Plessey Semiconductors, Inc
    Wiltshire, United Kingdom
  Naftali Chayat
    BreezeCom
    Tel Aviv, Israel
For the Direct Sequence medium
  Don Sloan
    Aironet Wireless Communications Inc.
    Akron, Ohio

## Slide 3
Outline
Organization
  IEEE P802
  IEEE P802.11
Functional requirements
Physical layers
Medium AccessControl

## Slide 4
IEEE PROJECT 802
Local and Metropolitan Standards Committee (LMSC)
Formed in 1980
Sponsored by the Computer Society
  Largest of 35 Societies
Local Area Networks (LANs)
  The only LAN standards development organization
8 Standards adopted as International Standard by ISO/IEC
  International Standards Organization and International Electrical Committee
Metropolitan Area Networks
Over 450 Voting Members, over 600 Observers
11 Working Groups, 2 Technical Advisory Groups 802.1 through 802.14
Notes: Updated April 9 to reflect the new working group for 100 Mbit/s Unshielded Twisted Pair standard.
The working group in IEEE is an open forum, anyone can attend the meetings, participation in the discussions may be restricted by the chairman to members. Membership of the working group is granted to individuals that have a satisfactory attendance record.

## Slide 5
IEEE PROJECT 802
Local Area Network - Definition
  Moderate to high signalling rate
    > 1 Mbit/s
  Moderately sized geographic area
    Room to campus size
  Generally owned, used and operated by single user
    In contrast to wide area networks
  Common shared medium

## Slide 6
IEEE Project 802.11
Wireless Local Area Networks Standards Working Group
Established July 1990
Membership
  79 voting members, 28 aspirant voting members
  Membership is by individual, not by company
  Complete mailing list with over 180 addresses
    USA, Canada, Europe, Israel, Japan, Korea, Taiwan
  Manufacturers
    Computers
    Micro-electronics
    Infra-red
    Radio equipment
  Users
    Government
    Manufacturers
Notes: Updated January 19 to reflect the membercount

## Slide 7
802.11 Functional requirements
Requirements study showed two types of networking needs:
  asynchronous, that is bursty traffic, but when something to send: need for very fast delivery
  isochronous, that is regular traffic, in small amounts at a time, but at a constant pace
Therefore 802.11 adopted the following requirements:
  Asynchronous MSDU delivery on all stations
    MSDU is the MAC Service Data Unit
  Optionally "time-bound MSDU delivery service"
Pedestrian speed and vehicular speed
  premises environment
Security: first review 802.10 provisions
Common MAC to support various PHYs
  regulation dependency
Notes: The pedestrian speed is agreed to be a few miles per hour
The vehicular speed is not fixed. It came from the industrial users. Depending on the politics this speed may be up to 30 mile per hour.

## Slide 8
Computer Architecture

## Slide 9
Multiple PHYs
MAC
PHY
802.3
10BASE2
10BASE5
10BROAD36
1BASE5
10BASE-T
10BASE-F
10BASE-FP
10BASE-FL
10BASE-FB
all Ethernet, but not inter-operable on the medium
802.11
DSSS
FHSS
IR
possibly all 802.11, but not inter-operable on the medium
wired
wireless

## Slide 10
802.11, MAC: Basics
“Distributed Medium Access Control Protocol” using an Ethernet like CSMA/CA + Ack scheme.
  Collision “Avoidance” rather then a “Detection” scheme.
    Effectiveness demonstrated in Wavelan product.
  Allows MAC level recovery of “Lost Packet” using a retransmission algorithm.
  Includes provisions to deal with “Hidden Nodes”.

## Slide 11
802.11, MAC: Performance
Efficient and stable throughput.
  Example: Based on 2 Mbps Wavelan speed.

## Slide 12
802.11, MAC: Other Functions
Roaming through the Wireless Infrastructure
  Maintain Continuous connectivity
  Station will “Re-Associate” with Access Points based on “Signal / Link Quality”.
  Support multi channel roaming.
  “Distribution System” will adapt to logical location changes of the station.
Provisions to use minimum Battery Power
  Strategy: Switch nodes off as much as possible, while maintaining network configuration.
  Traffic buffering functions are included in the Access Point to support this.
“Wired Equivalent Privacy” encryption algorithm is included.

## Slide 13
802.11, PHY, Radio
Concentrate radio work on the 2.4 GHz band (ISM)
  Most promising globally Spread Spectrum required
Also allowed to start work in 1.9, 5.2 and 5.8 GHz bands
  no activity yet
Notes: Updated April 7, 1994 to reflect March meeting results
Updated in Nov 93 to reflect the OQPSK decision for DS in Nov mtng,
(Personal opinion: this will erode away later) the channel modelling data format and the other band decision.

## Slide 14
Direct Sequence Spread Spectrum
Direct Sequence uses an 11 chip Barker Sequence to multiply the transmitted data
Receiver divides received signal by same Sequence to recover the data
  narrow band interference deminished
  implementations can resolve multipath in the correlation
modulation of 2 Mbit/s in DQPSK (Differential Quaternary Phase Shift Keying)
fall back modulation of 1 Mbit/s in DBPSK (Differential Binary PSK)
    3 channel pairs for USA
    3 channel pairs for Europe (1 pair with single channel)
    1 channel for Japan

## Slide 15
Frequency Hopping Spread Spectrum
Frequency Hopping uses one of out 79 channels at a time
hops from one frequency channel to the next at a 2.5 hops/s
  3 sets of 22 hop sequences defined
modulation for 1 Mbit/s in 2 level GFSK (Gaussian Frequency Shift Keying)
modulation for 2 Mbit/s in 4 level GFSK, channel permitting

## Slide 16
802.11, PHY, Infra-Red
Modulation for 1 Mbit/s (basic rate) in 16-PPM (Pulse Position Modulation)
Modulation for 2 Mbit/s (enhanced rate) in 4 -PPM
Transmitter illuminates the ceiling with a diffuse
Notes: Updated April 7 to reflect March 1994 meeting result

## Slide 17
Status
Second draft ballot conducted
47.5 % approval (75 % required, unanimous preferred)
  31 (17) approving
  33 (66) disapproving
  5 (11) abstaining
Resolving negative votes at November/January meeting
Second draft sent to ISO annexed to a Proposed New Work Item
Notes: New on April 7, 194

## Slide 18
IEEE P802.11 schedule
WG Confirmation ballot Jan/Feb 1995
Resolve issues at March 1996 meeting
Sponsor Ballot Mar/Apr1996
Resolve issues at May 1996 meeting
Sponsor Confirmation ballot Jun 1996
Resolve issues at July 1996 meeting
Standards Board meeting September 17-18, 1996
Notes: This plan has been updated to represent the schedule established at the January 1994 meeting.