## Slide 1
1
Frequency Hopping Spread Spectrum subpart of the 802.11 Wireless LAN Standard
FCC - 802.11 meeting, Jan. 5, 1996
Naftali Chayat
Chief Scientist
Notes: 1
1

## Slide 2
2
802.11-FCC Meeting Objectives
To inform FCC about the 802.11 WLAN Standard and its status
To avoid situation in which 802.11 standard is not acceptable by FCC
To get better understanding of what FCC does permit, in order to produce a better standard
Notes: 2
2

## Slide 3
3
Collision Avoidance
The Physical layer (PHY) is able to provide Carrier Detect indication, when not transmitting.
Randomized Inter-Frame Space (IFS) for reducing collision probability
Exponential Backoff is used to stabilize the network when collisions occur
Notes: 3
3

## Slide 4
4
Virtual Carrier Sense mechanism
In radio network, some stations may not hear a transmission from a certain station and therefore collide with it
The RTS-CTS exchange contains timing information that signals other stations for how long the medium will be busy
Virtual Carier Sense mechanism is implemented in the MAC layer
Notes: 4
4

## Slide 5
5
Frequency Hopping Sp.Sp.
Operates according to FCC 15.247 ruling:
  max 1 MHz bandwidth at -20 dB PSD
  hopping over 79 frequencies in a pseudo-random manner
  max 1 Watt power and 36 dBm EIRP
Notes: 5
5

## Slide 6
6
802.11 FHSS Modulation Objectives
Achieving at least 1 Mbit/sec rate
Low cost/familiar technology - FSK
  Constant Envelope- Saturated Amplifiers
  Limiter-Discriminator detection
Multichannel operation -shaping to reduce adjacent channel interference
Multiple rates - taking advantage of short range scenarios to increase rate
Notes: 6
6

## Slide 7
7
802.11 FHSS Modulation
Gaussian shaped FSK (GFSK)
  1 Msymbol/sec
  NRZ data is filtered with BT=0.5 Gaussian filter
1 or 2 Mbit/sec with multilevel GFSK
  1 Mbit/sec: 2 level GFSK h2=0.34
  2 Mbit/sec: 4 level GFSK h4=0.45h2=0.15
  Preamble and Header always at 1 Mbit/sec; Data at 1 or 2 Mbit/sec
Notes: 7
7

## Slide 8
8
GFSK vs GMSK comparison
GMSK is popular with cellular telephony
GMSK is a binary GFSK with h2=0.5
802.11 GFSK is h2=0.34 due to both
  1 Mb/s objective
  1 MHz 20 dB bandwidth 15.247 ruling
Results:
  Sensitivity reduced by 4-5 dB
  Increased first adjacent channel interference
Notes: 8
8

## Slide 9
9
802.11 FHSS Frame Format
PHY header indicates payload rate and length; CRC16 protected
Data is formatted to limit DC offset variations, for PLL based implementations
80 bits
16 bits
80 bits
16 bits
16 bits
variable lengyh 2 level data
16 bits
80 bits
16 bits
16 bits
variable lengyh 4 level data
ramp up 010 timing sync pattern frame sync PHY header leader CRC Payload Data ramp down
Notes: 9
9

## Slide 10
10
FHSS Modulation Specifications
Deviation:
  Upper bounded by FCC requirements
  Lower bounded to maintain sensitivity
Shape accuracy:
  Zero crossing instants accuracy
  Level accuracy
Center Frequency accuracy - 60 KHz
Notes: 10
10

## Slide 11
11
Receiver Performance
Notes: 11
11

## Slide 12
12
CCA- Clear Channel Assessment
CCA is used to:
  Initiate frame reception
  Avoid transmitting when the channel is busy
CCA Sensitivity:
  -80 dBm for PT<20 dBm, reduced by 0.5 dB for each dB of power increase
  Detection during 0101 pattern within 20 usec with 95% probability
Notes: 12
12

## Slide 13
13
Frequency Hopping Sequences
Design Criteria:
  Assured minimum hop distance for multipath diversity performance
  Minimizing hits and adjacent channel hits between different hopping patterns
  Minimizing consecutive hits between different hopping patterns
FCC 15.247 requirement: Pseudorandomly ordered frequency list
Notes: 13
13

## Slide 14
14
Previous Hopping Sequences
Previous 802.11 hopping sequences were based on constant frequency increment (mod 79).
Had better worst case hit, adjacent hit and consecutive hit performance
Were rejected by FCC as insufficiently pseudorandom (due to constant frequency increment)
Notes: 14
14

## Slide 15
15
New Frequency Hopping Sequences
Passed FCC approval for BreezeNet
Predesigned computer generated pseudorandom list of 79 frequencies
Minimum hop distance of 6 channels
Additional hopping sequences derived from the base predesigned sequence.
78 hopping patterns organized in 3 sets of 26 patterns each.
Notes: 15
15

## Slide 16
16
New Frequency Hopping Sequences- cont.
Denote frequency as 2402+b[i], b[i] is the base sequence in range 0.. 78.
k-th sequence is formed from the base sequence as 2402+(b[i]+k) mod 79
Example:
  Base seq: 2402, 2456, 2472, 2447, ...
  30-th seq: 2432, 2407, 2423, 2477, ...
Notes: 16
16