## Slide 1
Direct Sequence Spread Spectrum Physical Layer Specification IEEE 802.11
Prepared by Jan Boer, Chair DS PHY
Lucent Technologies WCND Utrecht

## Slide 2
What is DSSS?
Signal symbol is spreaded with a sequence
Wider Bandwidth
Less power density

## Slide 3
11 chip BARKER sequence
Good autocorrelation properties
Minimal sequence allowed by FCC
Coding gain 10.4 dB

## Slide 4
DSSS benefits
10 dB coding gain:
  Robust against interferers and noise (10 dB suppression)
Robust against time delay spread
  Resolution of echoes

## Slide 5
IEEE 802.11 DSSS PHY characteristics
2.4 GHz ISM band (FCC 15.247)
1 and 2 Mb/s datarate (DBPSK and DQPSK modulation)
Symbolrate 1MHz
Chipping rate 11 MHz with 11 chip Barker sequence
Multiple channels in 2.4 to 2.4835 GHz band

## Slide 6
PLCP Frame Format
Preamble and Header always at 1Mb/s DBPSK

## Slide 7
PLCP synchronization
128 scrambled 1 bits
needed for o.a.
  gain setting
  energy detection
  antenna selection
  frequency offset compensation

## Slide 8
Start Frame Delimiter
16 bit field (hF3A0)
used for
  bit synchronization

## Slide 9
Signal Field
Rate indication
  h0A 1Mb/s DBPSK
  h14 2Mb/s DQPSK
Other values reserved for future use (100 kb/s quantities)

## Slide 10
Service Field
Reserved for future use
h00 signifies 802.11 compliant

## Slide 11
Length Field
Indicates number of octets to be transmitted in MPDU
Used for
  End of frame detection
  MPDU CRC sync

## Slide 12
CRC field
CCITT CRC-16
Protects Signal, Service and Length Field

## Slide 13
Data Scrambler
ALL bits transmitted by the DSSS Phy are scrambled
Purpose
  Whithening the spectrum
  DC blocking (Barker sequnce is asymetric)

## Slide 14
DBPSK Modulation

## Slide 15
DQPSK Modulation

## Slide 16
Transmit Spectrum Mask

## Slide 17
DSSS Channels

## Slide 18
Clear Channel Assessment
Three methods:
  CCA mode 1: Energy above threshold
  CCA mode 2: Carrier sense only
  CCA mode 3: Carrier sense with energy above threshold
Energy detection function of TX power
  Tx power > 100 mW: -80 dBm
  Tx power > 50mW : -76 dBm
  Tx power < = 50mW: -70 dBm
Energy detect time : 15 μs
Correct PLCP header --> CCA busy for full (intended) duration of of frame as indicated by PLCP Length field

## Slide 19
DSSS Specification Summary
Slottime 20 μs
TX to Rx turnaround time 10 μs
Rx to Tx turnaround time 5 μs
Operating temperature range
        type 1: 0 - 40 °C
        type 2: -30 - 70 °C
Tx Power Levels
        1000 mW USA
        100 mW Europe
        10 mW/MHz Japan
Minimum Transmitted Power 1 mW
Tx power level control required above 100 mW

## Slide 20
DSSS Specification Summary (cont)
Tx Center Frequency Tolerance +/- 25 ppm
Chip Clock Frequency Tolerance +/- 25 ppm
Tx Power On Ramp 2 μs
Tx Power Down Ramp 2 μs
RF Carrier suppression 15 dB
Transmit modulation accuracy test procedure
Rx sensitivity -80 dB
@ 0.08FER (1024 Bytes)
Rx max input level -4 dB
Rx adjacent channel rejection >35 dB
@ > 30 MHz separation
between channels

## Slide 21
PLCP Transmit Procedure

## Slide 22
PLCP Receive Procedure