## Slide 1
802.11 Architecture
Notes: 1

## Slide 2
What is unique about wireless?
Difficult media
  interference and noise
  quality varies over space and time
  shared with “unwanted” 802.11 devices
  shared with non-802 devices (unlicensed spectrum, microwave ovens)
Full connectivity cannot be assumed
  “hidden node” problem
Multiple international regulatory requirements
Notes: 2

## Slide 3
Medium Variations
Notes: 3

## Slide 4
Uniqueness of Wireless (continued)
Mobility
  variation in link reliability
  battery usage: requires power management
  want “seamless” connections
Security
  no physical boundaries
  overlapping LANs
Notes: 4

## Slide 5
Requirements
Single MAC to support multiple PHYs.
  Support single and multiple channel PHYs.
  PHYs with different “Medium Sense” characteristics.
Should allow overlap of multiple networks in the same area and channel space.
Need to be “Robust for Interference”.
  Microwave, other non-802.11 interferers.
  Co-channel interference.
Need mechanisms to deal with “Hidden Nodes”.
Need provisions for Time Bounded Services.
Notes: 5

## Slide 6
Architecture Overview
One MAC supporting multiple PHYs
  currently Frequency Hopping, Direct Sequence and Infrared PHYs
Two configurations
  “Independent” (ad hoc) and “Infrastructure”
CSMA/CA (collision avoidance) with optional “point coordination”
Notes: 6

## Slide 7
802.11 Protocol Entities
MAC Sublayer
PLCP Sublayer
PMD Sublayer
MAC Layer
Management
PHY Layer
Management
Station
Management
LLC
MAC
PHY
Notes: 7

## Slide 8
802.11 Protocol Architecture
MAC Entity
  basic access mechanism
  fragmentation
  encryption
MAC Layer Management Entity
  synchronization
  power management
  roaming
  MAC MIB
Physical Layer Convergence Protocol (PLCP)
  PHY-specific, supports common PHY SAP
  provides Clear Channel Assessment signal (carrier sense)
Notes: 8

## Slide 9
802.11 Protocol Architecture (cont.)
Physical Medium Dependent Sublayer (PMD)
  modulation and encoding
PHY Layer Management
  channel tuning
  PHY MIB
Station Management
  interacts with both MAC Management and PHY Management
Notes: 9

## Slide 10
802.11 Configurations - Independent
Independent
  one “Basic Service Set”, BSS
  “Ad Hoc” network
  direct communication
  limited coverage area
Station
AH3
Station
Station
AH1
AH2
Ad Hoc Network
Notes: 10

## Slide 11
802.11 Configurations - Infrastructure
Infrastructure
  Access Points and stations
Distribution System interconnects Multiple Cells via Access Points to form a single Network.
  extends wireless coverage area
Station
Station
Station
Station
A1
A2
B1
B2
BSS-A
BSS-B
A
AP
AP
B
Server
DISTRIBUTION SYSTEM
Notes: 11

## Slide 12
Distribution System
Used to interconnect wireless cells
  multiple BSS connected together form an ESS, Extended Service Set
  Allows mobile stations to access fixed resources
Not part of 802.11 standard
  could be bridged IEEE LANs, wireless, other networks …
  Distribution System Services are defined
Notes: 12

## Slide 13
Access Points
Stations select an AP and “associate” with it
Support roaming
Provide other functions
  time synchronization (beaconing)
  power management support
  point coordination function
Traffic typically (but not always) flows through AP
  direct communication possible
Notes: 13

## Slide 14
802.11 Defines the Airwaves IF
The airwaves interface between stations (including that between station and AP) is standardized
  PHY and MAC
No exposed MAC/PHY interface specified
No exposed interface to Distribution System
  required DS services are defined
Internals of Distribution System not defined
Notes: 14

## Slide 15
MAC Services
Asynchronous MSDU Data Delivery
  provided to LLC (2304 octet maximum)
Time Bounded Services
  optional point coordination function
Security Services
  confidentiality, authentication, access control
Management Services
  scanning, joining, power management
Notes: 15

## Slide 16
MAC Functionality
Independent and Infrastructure configuration support
  Each BSS has a unique 48 bit address
  Each ESS has a variable length address
CSMA with collision avoidance
  MAC-level acknowledgment
  allows for RTS/CTS exchanges
    hidden node protection
  MSDU fragmentation
  “Point Coordination” option
    AP polling
Notes: 16

## Slide 17
MAC Functionality (continued)
Roaming support within an ESS
  station scans for APs, association handshakes
Power management support
  stations may power themselves down
  AP buffering, distributed approach for IBSS
Authentication and privacy
  Optional support of “Wired Equivalent Privacy” (WEP)
  Authentication handshakes defined
Notes: 17

## Slide 18
PHY Layer Services
PHY_DATA transfers
  multiple rates
Clear Channel Assessment (CCA)
  carrier sense
PHY Management
  channel tuning
Notes: 18

## Slide 19
Three PHYs
Frequency Hop Spread Spectrum
  2.4 GHz band, 1 and 2 Mbps transmission
  2GFSK, 4GFSK
  hop over 79 channels (North America)
Direct Sequence Spread Spectrum
  2.4 GHz band, 1 and 2 Mbps transmission
  DBPSK, DQPSK
  11 chip Barker sequence
Baseband IR
  Diffuse infrared
  1 and 2 Mbps transmission, 16-PPM and 4-PPM
Notes: 19