## Slide 1
802.11 Tutorial
802.11 MAC Entity:
MAC Basic Access Mechanism
Privacy and Access Control
Notes: 1

## Slide 2
802.11 Protocol Entities
MAC Sublayer
PLCP Sublayer
PMD Sublayer
MAC Layer
Management
PHY Layer
Management
Station
Management
LLC
MAC
PHY
Notes: 2

## Slide 3
Main Requirements
Single MAC to support multiple PHYs.
  Support single and multiple channel PHYs.
  and PHYs with different Medium Sense characteristics
Should allow overlap of multiple networks in the same area and channel space.
  Need to be able to share the medium.
  Allow re-use of the same medium.
Need to be Robust for Interference.
  Microwave interferers
  Other un-licensed spectrum users
  Co-channel interference
Need mechanisms to deal with Hidden Nodes.
Need provisions for Time Bounded Services.
Need provisions for Privacy and Access Control.
Notes: 3

## Slide 4
Basic Access Protocol Features
Use Distributed Coordination Function (DCF) for efficient medium sharing without overlap restrictions.
  Use CSMA with Collision Avoidance derivative.
  Based on Carrier Sense function in PHY called Clear Channel Assessment (CCA).
Robust for interference.
  CSMA/CA + ACK for unicast frames, with MAC level recovery.
  CSMA/CA for Broadcast frames.
Parameterized use of RTS / CTS to provide a Virtual Carrier Sense function to protect against Hidden Nodes.
  Duration information is distributed by both transmitter and receiver through separate RTS and CTS Control Frames.
Includes fragmentation to cope with different PHY characteristics.
Frame formats to support the access scheme
  For Infrastructure and Ad-Hoc Network support
  and Wireless Distribution System.
Notes: 4

## Slide 5
CSMA/CA Explained
DIFS
Contention Window
Slot time
Defer Access
Backoff-Window
Next Frame
Select Slot and Decrement Backoff as long as medium is idle.
SIFS
PIFS
DIFS
Free access when medium
is free longer than DIFS
Busy Medium
Reduce collision probability where mostly needed.
  Stations are waiting for medium to become free.
  Select Random Backoff after a Defer, resolving contention to avoid collisions.
Efficient Backoff algorithm stable at high loads.
  Exponential Backoff window increases for retransmissions.
  Backoff timer elapses only when medium is idle.
Implement different fixed priority levels.
  To allow immediate responses and PCF coexistence.
Notes: 5

## Slide 6
CSMA/CA + ACK protocol
Defer access based on Carrier Sense.
  CCA from PHY and Virtual Carrier Sense state.
Direct access when medium is sensed free longer then DIFS, otherwise defer and backoff.
Receiver of directed frames to return an ACK immediately when CRC correct.
  When no ACK received then retransmit frame after a random backoff (up to maximum limit).
Ack
Data
Next MPDU
Src
Dest
Other
Contention Window
Defer Access
Backoff after Defer
DIFS
SIFS
DIFS
Notes: 6

## Slide 7
Throughput Efficiency
Efficient and stable throughput.
  Stable throughput at overload conditions.
  To support “Bursty Traffic” characteristics.
Notes: 7

## Slide 8
Transmitters contending for the medium may not “Hear each other” as shown below.
Separate Control frame exchange (RTS / CTS) between transmitter and receiver will Reserve the Medium for subsequent data access.
  Duration is distributed around both Tx and Rx station.
“Hidden Node” Problem
AP
STA
STA
CTS-Range
RTS-Range
STA
AP
RTS
CTS
Data
Ack
Stations do not hear each other
But they hear the AP.
Notes: 8

## Slide 9
“Hidden Node” Provisions
Duration field in RTS and CTS frames distribute Medium Reservation information which is stored in a Net Allocation Vector (NAV).
Defer on either NAV or "CCA" indicating Medium Busy.
Use of RTS / CTS is optional but must be implemented.
Use is controlled by a RTS_Threshold parameter per station.
  To limit overhead for short frames.
RTS
CTS
Ack
Data
NAV
Next MPDU
Src
Dest
Other
CW
Defer Access
Backoff after Defer
NAV
(RTS)
(CTS)
DIFS
Notes: 9

## Slide 10
RTS/CTS Overhead Impact
Good mixed Throughput (long inbound frames) efficiency.
60% Short, 40% Long Frames
Notes: 10

## Slide 11
Optional Point Coordination Function (PCF)
Contention Free Service uses Point Coordination Function (PCF) on a DCF Foundation.
  PCF can provide lower transfer delay variations to support Time Bounded Services.
  Async Data, Voice or mixed implementations possible.
  Point Coordinator resides in AP.
Coexistence between Contention and optional Contention Free does not burden the implementation.
(CSMA/CA )
Contention
Service
Service
PHY
MAC
PCF
Optional
DCF
Contention Free
Async
Time Bounded / Async
Notes: 11

## Slide 12
Contention Free operation
Alternating Contention Free and Contention operation under PCF control.
NAV prevents Contention traffic until reset by the last PCF transfer.
  So variable length Contention Free period per interval.
Both PCF and DCF defer to each other causing PCF Burst start variations.
Contention Free Period
Contention Period
CFP repetition interval
Variable Length
PCF Defers for Busy Medium
CF-Burst
Busy medium
PCF
DCF
(Optional)
Defer
NAV
Async traffic Defer
PCF
"Reset NAV"
CFP repetition interval
Notes: 12

## Slide 13
PCF Burst
CF-Burst by Polling bit in CF-Down frame.
Immediate response by Station on a CF_Poll.
Stations to maintain NAV to protect CF-traffic.
Responses can be variable length.
“Reset NAV” by last (CF_End) frame from AP.
"ACK Previous Frame" bit in Header.
CFP repetition interval
D1
U1
U2
D2
D3
D4
U4
NAV
Reset NAV
No Up
Contention Period
Contention Free Burst
Dx = AP-Frame
Ux = Station-Frame
CF_End
Min Contention Period
Busy Medium
PIFS
SIFS
Notes: 13

## Slide 14
Fragmentation
Burst of Fragments which are individually acknowledged.
  For Unicast frames only.
Random backoff and retransmission of failing fragment when no ACK is returned.
Duration information in data fragments and Ack frames causes NAV to be set, for medium reservation mechanism.
Fragment 0
ACK 0
Src
Dest
CTS
SIFS
RTS
NAV (RTS)
NAV (CTS)
Other
PIFS
DIFS
Backoff-Window
ACK 1
Fragment 1
NAV (Fragment 0)
NAV (ACK 0)
SIFS
Notes: 14

## Slide 15
Frame Formats
MAC Header format differs per Type:
  Control Frames (several fields are omitted)
  Management Frames
  Data Frames
Includes Sequence Control Field for filtering of duplicate caused by ACK mechanism.
Frame
Control
Duration
ID
Addr 1
Addr 2
Addr 3
Addr 4
Sequence
Control
CRC
Frame
Body
2
2
6
6
6
6
2
0-2312
4
802.11 MAC Header
Bytes:
Protocol
Version
Type
SubType
To
DS
Retry
Pwr
Mgt
More
Data
WEP
Rsvd
Frame Control Field
Bits: 2
2
4
1
1
1
1
1
1
1
1
DS
From
More
Frag
Notes: 15

## Slide 16
Address Field Description
Addr 1 = All stations filter on this address.
Addr 2 = Transmitter Address (TA)
  Identifies transmitter to address the ACK frame to.
Addr 3 = Dependent on To and From DS bits.
Addr 4 = Only needed to identify the original source of WDS (Wireless Distribution System) frames.
Notes: 16

## Slide 17
Privacy and Access Control
Goal of 802.11 is to provide “Wired Equivalent Privacy” (WEP)
  Usable worldwide
802.11 provides for an Authentication mechanism
  To aid in access control.
  Has provisions for “OPEN”, “Shared Key” or proprietary authentication extensions.
Optional (WEP) Privacy mechanism defined by 802.11.
  Limited for Station-to-Station traffic, so not “end to end”.
    Embedded in the MAC entity.
  Only implements “Confidentiality” function.
  Uses RC4 PRNG algorithm based on:
    a 40 bit secret key (No Key distribution standardized)
    and a 24 bit IV that is send with the data.
    includes an ICV to allow integrity check.
  Only payload of Data frames are encrypted.
    Encryption on per MPDU basis.
Notes: 17

## Slide 18
Privacy Mechanism
WEP bit in Frame Control Field indicates WEP used.
  Each frame can have a new IV, or IV can be reused for a limited time.
  If integrity check fails then frame is ACKed but discarded.
WEP
PRNG
IV
IV
Secret Key
Integrity Alg
+
Ciphertext
ICV
WEP
PRNG
IV
+
Secret Key
Ciphertext
ICV
Integrity Alg
Plaintext
ICV'=ICV?
Plaintext
TX
Preamble
PLCP Header
MAC Header
CRC
Payload
Encrypted
IV (4)
ICV (4)
Cyphertext
K-ID
Notes: 18

## Slide 19
Support for Mobility
MAC Sublayer
PLCP Sublayer
PMD Sublayer
MAC Layer
Management
PHY Layer
Management
Station
Management
LLC
MAC
PHY
Notes: 19

## Slide 20
MAC Management Layer
Synchronization
  finding and staying with a WLAN
  Synchronization functions
    TSF Timer, Beacon Generation
Power Management
  sleeping without missing any messages
  Power Management functions
    periodic sleep, frame buffering, Traffic Indication Map
Association and Reassociation
  Joining a network
  Roaming, moving from one AP to another
  Scanning
Management Information Base

## Slide 21
Synchronization in 802.11
Timing Synchronization Function (TSF)
Used for Power Management
  Beacons sent at well known intervals
  All station timers in BSS are synchronized
Used for Point Coordination Timing
  TSF Timer used to predict start of Contention Free burst
Used for Hop Timing for FH PHY
  TSF Timer used to time Dwell Interval
  All Stations are synchronized, so they hop at same time.
Notes: 21

## Slide 22
All stations maintain a local timer.
Timing Synchronization Function
  keeps timers from all stations in synch
  AP controls timing in infrastructure networks
  distributed function for Independent BSS
Timing conveyed by periodic Beacon transmissions
  Beacons contain Timestamp for the entire BSS
  Timestamp from Beacons used to calibrate local clocks
  not required to hear every Beacon to stay in synch
  Beacons contain other management information
    also used for Power Management, Roaming
Synchronization Approach
Notes: 22

## Slide 23
Infrastructure Beacon Generation
APs send Beacons in infrastructure networks.
Beacons scheduled at Beacon Interval.
Transmission may be delayed by CSMA deferral.
  subsequent transmissions at expected Beacon Interval
  not relative to last Beacon transmission
  next Beacon sent at Target Beacon Transmission Time
Timestamp contains timer value at transmit time.
Time Axis
Beacon Interval
X
X
X
X
"Actual time" stamp in Beacon
Beacon
Busy Medium
Notes: 23

## Slide 24
Power Management
Mobile devices are battery powered.
  Power Management is important for mobility.
Current LAN protocols assume stations are always ready to receive.
  Idle receive state dominates LAN adapter power consumption over time.
How can we power off during idle periods, yet maintain an active session?
802.11 Power Management Protocol:
  allows transceiver to be off as much as possible
  is transparent to existing protocols
  is flexible to support different applications
    possible to trade off throughput for battery life
Notes: 24

## Slide 25
Power Management Approach
Allow idle stations to go to sleep
  station’s power save mode stored in AP
APs buffer packets for sleeping stations.
  AP announces which stations have frames buffered
  Traffic Indication Map (TIM) sent with every Beacon
Power Saving stations wake up periodically
  listen for Beacons
TSF assures AP and Power Save stations are synchronized
  stations will wake up to hear a Beacon
  TSF timer keeps running when stations are sleeping
  synchronization allows extreme low power operation
Independent BSS also have Power Management
  similar in concept, distributed approach
Notes: 25

## Slide 26
Infrastructure Power Management
Broadcast frames are also buffered in AP.
  all broadcasts/multicasts are buffered
  broadcasts/multicasts are only sent after DTIM
  DTIM interval is a multiple of TIM interval
TIM
TIM-Interval
Time-axis
Busy Medium
AP activity
TIM
TIM
TIM
DTIM
DTIM
DTIM interval
Broadcast
Broadcast
Notes: 26

## Slide 27
Infrastructure Power Management
Broadcast frames are also buffered in AP.
  all broadcasts/multicasts are buffered
  broadcasts/multicasts are only sent after DTIM
  DTIM interval is a multiple of TIM interval
Stations wake up prior to an expected (D)TIM.
TIM
TIM-Interval
Time-axis
Busy Medium
AP activity
TIM
TIM
TIM
DTIM
DTIM
DTIM interval
PS Station
Broadcast
Broadcast
Notes: 27

## Slide 28
Infrastructure Power Management
Broadcast frames are also buffered in AP.
  all broadcasts/multicasts are buffered
  broadcasts/multicasts are only sent after DTIM
  DTIM interval is a multiple of TIM interval
Stations wake up prior to an expected (D)TIM.
If TIM indicates frame buffered
  station sends PS-Poll and stays awake to receive data
  else station sleeps again
TIM
TIM-Interval
Time-axis
Busy Medium
Tx operation
AP activity
TIM
TIM
TIM
DTIM
DTIM
DTIM interval
PS Station
Broadcast
PS-Poll
Broadcast
Notes: 28

## Slide 29
Wireless LAN Infrastructure Network
Access Point A
Access Point B
Station 4
Access Point C
Station 1
Station 2
Station 3
Station 5
Station 6
Station 7
Each Station is Associated with a particular AP
  Stations 1, 2, and 3 are associated with Access Point A
  Stations 4 and 5 are associated with Access Point B
  Stations 6 and 7 are associated with Access Point C
Notes: 29

## Slide 30
Roaming
Access Point A
Access Point B
Station 4
Access Point C
Station 1
Station 2
Station 3
Station 5
Station 6
Station 7
Mobile stations may move…
Notes: 30

## Slide 31
Roaming
Access Point A
Access Point B
Station 4
Access Point C
Station 1
Station 2
Station 3
Station 5
Station 6
Station 7
Mobile stations may move…
  beyond the coverage area of their Access Point
Notes: 31

## Slide 32
Roaming
Access Point A
Access Point B
Station 4
Access Point C
Station 1
Station 2
Station 3
Station 5
Station 6
Station 7
Mobile stations may move…
  beyond the coverage area of their Access Point
  but within range of another Access Point
Notes: 32

## Slide 33
Roaming
Access Point A
Access Point B
Station 4
Access Point C
Station 1
Station 2
Station 3
Station 5
Station 6
Station 7
Mobile stations may move…
  beyond the coverage area of their Access Point
  but within range of another Access Point
Reassociation allows station to continue operation
Notes: 33

## Slide 34
Roaming Approach
Station decides that link to its current AP is poor
Station uses scanning function to find another AP
  or uses information from previous scans
Station sends Reassociation Request to new AP
If Reassociation Response is successful
  then station has roamed to the new AP
  else station scans for another AP
If AP accepts Reassociation Request
  AP indicates Reassociation to the Distribution System
  Distribution System information is updated
  normally old AP is notified through Distribution System
Notes: 34

## Slide 35
Scanning
Scanning required for many functions.
  finding and joining a network
  finding a new AP while roaming
  initializing an Independent BSS (ad hoc) network
802.11 MAC uses a common mechanism for all PHY.
  single or multi channel
  passive or active scanning
Passive Scanning
  Find networks simply by listening for Beacons
Active Scanning
  On each channel
    Send a Probe, Wait for a Probe Response
Beacon or Probe Response contains information necessary to join new network.
Notes: 35

## Slide 36
Active Scanning Example
Steps to Association:
Station sends Probe.
Initial connection to an Access Point
Access Point C
Access Point A
Notes: 36

## Slide 37
Active Scanning Example
Steps to Association:
Station sends Probe.
APs send Probe Response.
Initial connection to an Access Point
Access Point C
Access Point A
Notes: 37

## Slide 38
Active Scanning Example
Steps to Association:
Station sends Probe.
APs send Probe Response.
Station selects best AP.
Initial connection to an Access Point
Access Point C
Access Point A
Notes: 38

## Slide 39
Active Scanning Example
Steps to Association:
Station sends Probe.
APs send Probe Response.
Station selects best AP.
Station sends Association
Request to selected AP.
Initial connection to an Access Point
Access Point C
Access Point A
Notes: 39

## Slide 40
Active Scanning Example
Steps to Association:
Station sends Probe.
APs send Probe Response.
Station selects best AP.
Station sends Association
Request to selected AP.
AP sends Association
Response.
Initial connection to an Access Point
Access Point C
Access Point A
Notes: 40

## Slide 41
Active Scanning Example
Steps to Association:
Station sends Probe.
APs send Probe Response.
Station selects best AP.
Station sends Association
Request to selected AP.
AP sends Association
Response.
Initial connection to an Access Point
- ReAssociation follows a similar process
Access Point C
Access Point A
Notes: 41

## Slide 42
MAC Management Frames
Beacon
  Timestamp, Beacon Interval, Capabilities, ESSID, Supported Rates, parameters
  Traffic Indication Map
Probe
  ESSID, Capabilities, Supported Rates
Probe Response
  Timestamp, Beacon Interval, Capabilities, ESSID, Supported Rates, parameters
  same for Beacon except for TIM
Association Request
  Capability, Listen Interval, ESSID, Supported Rates
Association Response
  Capability, Status Code, Station ID, Supported Rates
Notes: 42

## Slide 43
More MAC Management Frames
Reassociation Request
  Capability, Listen Interval, ESSID, Supported Rates, Current AP Address
Reassociation Response
  Capability, Status Code, Station ID, Supported Rates
Disassociation
  Reason code
Authentication
  Algorithm, Sequence, Status, Challenge Text
Deauthentication
  Reason
Notes: 43

## Slide 44
802.11 MAC
the end…
Notes: 44