## Slide 1
Tutorial on 802.11 to 802
Prepared by Vic Hayes, Chair IEEE P802.11
One of the founders and chair from the beginning (September 1990)
Lucent Technologies

## Slide 2
Outline (1)
Requirements
MAC
  Wireless Architecture and MAC architecture overview
  Basic Access mechanism and Frame formats
  MAC Management and mobility provisions
PHY
  Spectrum selection
  Frequency Hopping PHY
  Direct Sequence PHY
  Infrared PHY

## Slide 3
Requirements
PAR
Study the environment and applications
Functional Requirements

## Slide 4
Requirements (PAR)
Project Authorization Request (PAR)
  Title: Standard for Wireless Medium Access Method (MAC) and Physical Layer (PHY) Specifications
  To develop a Medium Access Control (MAC) and Physical Layer (PHY) specification for wireless connectivity for fixed, portable and moving stations within a local area.
  To provide wireless connectivity to automatic machinery, equipment or, stations that require rapid deployment, which may be portable, or hand-held or which may be mounted on moving vehicles within a local area.
  To offer a standard for use by regulatory bodies to standardize access to one or more radio frequency bands for the purpose of local area communication.

## Slide 5
Requirements (802.11)
Type of medium
  The goal is that the MAC shall support PHYs using electromagnetic waves through the air (i.e.. radio waves as well as infra-red or visible light).
  PHY layer suitable for use with the electromagnetic frequency spectrum as described in the following paragraph will be defined with this standard. If evidence of need and sufficient interest exists other PHY layers will be considered at a later time.
Supported Stations
  The standard shall support stationary stations, movable stations, and mobile stations moving at pedestrian and vehicular (local premises environment) speeds. This is to be implemented with one PHY if feasible.

## Slide 6
Requirements (802.11)
Environment
  Because the range of wireless transmission / reception may be smaller than the physical coverage area desired, a distribution system designed to provide range extensibility will be addressed as part of this standard.
  The standard will include support of the following:
    Basic Service Area (BSA) in which each station can communicate with any other station in the BSA.
    Extended Service Area (ESA) in which each station can communicate with any other station via the defined and managed Distribution System.
  Stations which interoperate in both BSA and ESA shall be defined if feasible.

## Slide 7
Requirements (802.11)
Possible target environments include:
  in buildings and other premises such as offices, financial institutions, shops, malls, small and large industry, hospitals and residences,
  outdoor areas such as parking lots, campuses, building complexes and outdoor plants and storages.
  Note: The definition of performance classes within a PHY may be necessary to support environments with benign or hostile characteristics.
Supported service
  The Wireless MAC shall support both connectionless service as defined in the MAC Service definition at rates between 1 and 20 Mbit/s as well as a service supporting packetized voice.

## Slide 8
Requirements (802.11)
Compatibility requirements
  The specification shall meet the following standards and documents:
    the IEEE P802 Functional Requirements including section 5.6.1 (in version 6.5) as defined below:
    "5.6.1 The MAC Service Data Unit (MSDU) loss rate shall be less than 4*10E-5 for an MSDU length of 512 octets.".
  A minimally conformant IEEE P802.11 network will meet all of the P802 requirements except that 5.6.1 will be met at least 99.9 % of the time on a daily basis, in 99.9 % of the total geography of the service area.
  IEEE P802.11 will define approaches to allow a minimally conformant network to achieve full conformance over the total geography of the service area.

## Slide 9
Requirements (802.11)
Data Service Types:
  802.11 will provide two classes of MSDU delivery service:
    1) An Asynchronous MSDU delivery service.
    2) A Time-bounded MSDU delivery service.
  All 802.11 implementations will support the Asynchronous class service.
  Stations using the Asynchronous and/or Time-bounded service must coexist within the same BSS.
MAC / PHY interface:
  A single MAC will be used to support multiple PHYs.

## Slide 10
Requirements (802.11)
Note: To make this purpose feasible, this PAR also authorizes IEEE P802 to petition or provide comments to regulatory bodies worldwide (e.g.. the FCC in the USA, the Department of Communications in Canada, the RF agency of the Department of Trade and Industry in the UK and the Radio Frequency Commission of the CEPT of Europe)

## Slide 11
MAC
Wireless Architecture and MAC architecture overview
  Greg Ennis, consultant to Symbol Technologies
  member since May 1993
document 96/49B

## Slide 12
MAC (2)
Basic Access mechanism and Frame formats
  Wim Diepstraten, Lucent Technologies
  member since November 1991
MAC Management and mobility provisions
  Phil Belanger, Aironet
  member since July 1992
document 96/49C

## Slide 13
PHY Introduction
Current draft supports 3 PHY specifications
  2 for radio
  1 for Infrared

## Slide 14
Radio Regulations
Radio spectrum is a scarce resource and needs to be regulated
Responsibility of local Administration
International Regulations are the responsibility of the International Telecommunications Union, Radiocommunication Sector
  Old name is CCIR (International Radio Consultative Committee)
  Membership by Administration (or through administration)
Main decisions made in the Radiocommunication Assemblies
  Old name World Administrative Radio Conference (WARC)
    Last one held in 1992
    next one planned for 1995
The ITU divides the world in three Regions for the allocation of frequencies in the Radio Regulations
Notes: The members of the CCIR are the administrations of the nations around the world. Participation is therefore limited to organisations that are member through the national delegation of their country.
The CCIR Plenary Assemblies were held 5 yearly. The are now held every two years, and are called World Radio Assemblies.
World Radio Conferences are held every two years also, coinciding with and after the World Radio Assemblies.
November 93 there will be a WRC for setting the agenda for the WRC 95.

## Slide 15
Region 1
Europe is part of Region 1
CEPT responsible for harmonization in Europe
1 foot
3 cm
3 mm
UHF
cm waves
mm waves
Notes: The yellow or large boundary is the Region 1 boundary
The pink ellipse is the part CEPT is active in the European harmonization
Note that the eastern European countries are rapidly becoming members of CEPT thus, in principle, accepting the Recommendations

## Slide 16
Region 1
Allocation for DECT, 1.880 - 1.900 GHz
  Digital European Cordless T(elephone)elecommunications
Allocation for RLANs of 100 MHz in the 2.45 GHz band, T/R 10-01
  top part (2.4835 - 2.500 GHz) may be withdrawn for satellite service
Allocation for HIPERLAN, 100 + 50 MHz in 5.2 GHz area and 200 MHz in 17 GHz area, T/R 22-06
  High Performance European radio LAN
Allocation for RLANs in 61.0 - 61.5 GHz, T/R 22-03
915 MHz band has been allocated to GSM (Groupe Speciale Mobile)
Some persons thinking about spectrum auctions as in USA
Notes: Correction made on November 30 1993 (remark about satellite service was on wrong place)
The sequence is in frequency
The timing is roughly as follows:
1. 60 GHz
2 DECT
3 2.4
4 HIPERLAN

## Slide 17
Region 2
USA is part of Region 2
FCC is the agency for regulation in USA
Notes: The yellow line is the region 2 area
The small ellipse is the USA area

## Slide 18
Region 2
FCC Part 15 rules allow for use of Spread Spectrum devices:
  902 - 928 MHz also in Canada and Mexico
  2.4 - 2.4835 GHz also in Canada
  5.725 - 5.875 GHz
Unlicensed PCS, 1.910 - 1.930 GHz
  10 MHz for voice applications (1.920-1.930 GHz)
  10 MHz for data applications (1.910-1.920 GHz)
  needs to be cleared first
  relocation to be paid by new users
    definition of users unclear for non-licensed applications
    conditionally designated to UTAM, Unlicensed (ad-hoc committee) for 2 GHz microwave Transition And Management
Unlicensed PCS, 2.390 - 2.400 GHz
Notes: Sequence by frequency
Timing :
1 ISM band s
2 Licensed 19 GHz allocation
3 The PCS band allocation is very recent, Report and order expected on October 22, 1993

## Slide 19
Region 2
Notice of Proposed Rulemaking for above 40 GHz allocation
  8.5 GHz for unlicensed services
    includes LANs, vehicle radar systems to avoid collisions
    5 GHz in a single band: 59-64 GHz
    additional 3.5 GHz in 7 bands between 71 and 153 GHz
  7.3 GHz for licensed services
    3 GHz in two bands, 40.5 - 42.5 GHz and 47.2 - 48.2 GHz
    4.3 GHz in 7 bands between 71 and 153 GHz
Licensed band for data communications, 18.8 - 19.2 GHz

## Slide 20
Region 3
Japan is part of Region 3
Notes: The yellow line is the region 3 boundary
Japan is indicated by the small ellipse

## Slide 21
Region 3
Allocation in Japan for RLANs 2.471 - 2.497 GHz
Many other countries in Region 3 adopting the 2.4 - 2.5 GHz allocation for RLANs
Allocations expected in the area of 17 - 19 GHz
Notes: The allocations in the 17 - 19 GHz area are mainly driven by Motorola, Some are in the 17-18 GHz others are in the 18-19 GHz band

## Slide 22
Global View
915 MHz band is only available in Region 2
1.9 GHz allocations in US and Europe differ in ruling:
  US
    spectrum etiquette (co-existence standard)
    needs to be cleared from Microwave point-to-point links
    clearing will be done area by area
    cost of clearing will be charged to devices (US$ 20)
    nationwide clearing will take apr. 5 years
    peer-to-peer devices not allowed before nationwide clearance
  Europe
    DECT standard(interoperability standard
Notes: I am not sure whether DECT, with some modifications to adhere to the etiquette, could be used in the USA

## Slide 23
Global View
2.4 GHz
  available in many countries around the globe
  IEEE P802.11 working on an interoperability standard for 1 and 2 Mbit/s datarate
  disadvantages:
    secondary status
    microwave ovens
HIPERLAN band
  only in European part of Region 1
Notes: I am not sure whether DECT, with some modifications to adhere to the etiquette, could be used in the USA

## Slide 24
Global View
5.8 GHz band(ISM)
  only available in the USA
HIPERLAN
  please turn to prior slide
some channels in the 18.8 - 19.2 GHz band
  only in the USA
  subject to licensing
17 - 19 GHz band
  only in Japan, rules unknown
Notes: I am not sure whether DECT, with some modifications to adhere to the etiquette, could be used in the USA

## Slide 25
Global View
61.0 - 61.5 GHz band
  technology is too expensive yet
  line of sight required due to properties of waves at this frequency
  is in the Oxygen absorption band
    limits coverage area
Notes: I am not sure whether DECT, with some modifications to adhere to the etiquette, could be used in the USA

## Slide 26
Availability of the 2.4 GHz band
Austria Belgium
Denmark Finland
France Germany
Iceland Ireland
Italy Netherlands Norway
Portugal Spain
Sweden Switzerland UK
Czech Republic (*)
Estonia
Hungary
Latvia (*)
Lithuania (*)
Poland (*)
Russia
Ukraine (*)
US Canada
Australia
China (*) Hong Kong
Indonesia (*) Japan
Korea Malaysia New Zealand
Philippines (*) Singapore Taiwan (*) Thailand
Abu Dhabi (*)
Cyprus
Israel
Morocco (*) Saudi Arabia South Africa
Turkey (*)
2.4 GHz
(*) Certification in progress

## Slide 27
PHY Frequency Hopping
Frequency Hopping PHY
  Naftali Chayat, Breezecom
  member since September 1993
document 96/49D

## Slide 28
PHY Frequency Hopping
Direct Sequence PHY
  Jan Boer , Lucent Technologies
  member since July 1992
document 96/49E

## Slide 29
Infrared PHY
No expert available at this meeting
Nearly visible light
  850 nanometer to 950 nanometer range
“Diffuse Infrared” transmission
  the receiver and transmitter do not have to be aimed at each other and do not need a clear line-of-sight
  range up to about ten meters
  only in-building

## Slide 30
Infrared PHY
Frame Format
  SFD, start frame delimiter
  DR, data rate
  DCLA, DC level adjustment

## Slide 31
Infrared PHY
Basic Access Rate is based on 1 Mbit/s 16-PPM modulation
Enhanced Access Rate is based on 2 Mbit/s 4-PPM

## Slide 32
Tutorial on 802.11 to 802
  the end