## Slide 1
Frequency Hopping Spread Spectrum PHY of the 802.11 Wireless LAN Standard
Presentation to IEEE 802
March 11, 1996
Naftali Chayat
BreezeCom
Copyright ©1996 IEEE, All rights reserved. This contains parts from an unapproved draft, subject to change

## Slide 2
Why Frequency Hopping?
Frequency Hopping is one of the variants of Spread Spectrum- a technique which enables coexistence of multiple networks (or other devices) in same area
FCC recognizes Frequency Hopping as one of the techniques withstanding “fairness” requirements for unlicensed operation in the ISM bands.
802.11 Frequency Hopping PHY uses 79 nonoverlapping frequency channels with 1 MHz channel spacing.
FH enables operation of up to 26 collocated networks, enabling therefore high aggregate throughput.
Frequency Hopping is resistant to multipath fading through the inherent frequency diversity mechanism

## Slide 3
Regulatory requirements for FH
North America (CFR47, Parts 15.247, 15.205, 15.209):
  Frequency band: 2400-2483.5 MHz
  At most 1 MHz bandwidth (at -20 dB re peak)
  At least 75 hopping channels, pseudorandom hopping pattern
  At most 1 W transmit power and 4 W EIRP (including antenna)
Europe (ETS 300-328, ETS 300-339):
  Frequency band: 2400-2483.5 MHz
  At least 20 hopping channels
  At most 100 mW EIRP
Japan (RCR STD-33A):
  Frequency band: 2471-2497 MHz
  At least 10 hopping channels

## Slide 4
802.11 FH PHY vs. Regulations
1 MHz Bandwidth
79 hopping channels in North America and Europe; pseudorandom hopping pattern.
23 hopping channels in Japan.
At most 1 W power; devices capable of more than 100 mW have to support at least one power level not exceeding 100 mW.

## Slide 5
802.11 FHSS Modulation Objectives
Achieving at least 1 Mbit/sec rate
Familiar, field proven, low cost technology - FSK
  Constant Envelope- Saturated Amplifiers
  Limiter-Discriminator detection
Multichannel operation -transmit signal shaping to reduce adjacent channel interference
Multiple rates - medium use optimization by taking advantage of short-range/good-propagation scenarios to increase rate

## Slide 6
802.11 FHSS Modulation
Gaussian shaped FSK (GFSK) at Fclk = 1 Msymbol/sec
  NRZ data is filtered with BT=0.5 low-pass Gaussian filter (500 KHz bandwidth at 3 dB) and then FM modulates a carrier
1 or 2 Mbit/sec with multilevel GFSK
  1 Mbit/sec: 2 level GFSK h2=0.34
  2 Mbit/sec: 4 level GFSK h4=0.45h2=0.15
1 Mbit/sec operation mandatory; 2 Mbit/sec- optional
  facilitates production of interoperable lower-rate/lower-cost and higher-rate/higher-cost equipment

## Slide 7
802.11 FHSS Frame Format
PHY header indicates payload rate and length; CRC16 protected
Data is whitened by a synchronous scrambler and formatted to limit DC offset variations
Preamble and Header always at 1 Mbit/sec; Data at 1 or 2 Mbit/sec

## Slide 8
PLCP Preamble
PLCP preamble starts with 80 bits of 0101 sync pattern, used to
  detect presence of signal
  to resolve antenna diversity
  to acquire symbol timing
Follows 16 bit Start Frame Delimiter (SFD)
  the pattern is 0000 1100 1011 1101 (left bit transmitted first)
  the SFD provides symbol-level frame synchronization
  the SFD pattern is designed to optimize autocorrelation properties in conjunction with the 0101 pattern in front of it
  the SFD pattern is balanced

## Slide 9
PLCP Header
A 32 bit PLCP header consists of PLW (PLCP_PDU Length Word), PSF (PLCP Signaling Field) and 16 bit HEC (Header Error Check)
  PLW (PLCP_PDU Length Word) is 12 bit field indicating the length of PLCP_PDU in octets, including the 32 bit CRC at the PLCP_PDU end, in the range 0 .. 4095
  PSF (PLCP Signaling Field) is 4 bit field, of which currently 3 are reserved and the fourth is used to signal the PLCP_PDU data rate (1 or 2 Mbit/s)
  HEC is a 16 bit CRC with CCITT generator polynomial G(x)=x16+x12+x5+1
The PLCP header is always transmitted at 1 Mbit/sec.

## Slide 10
PLCP_PDU Formatting
Delineating data octets into serial stream, LSB first
Scrambling: the data is XORed with periodic 127 bit LFSR sequence generated by a 1+x4+x7 feedback polynomial
Dividing serial bit stream into symbols:
  at 1 Mbit/s, each bit is converted into 2FSK symbol
  at 2 Mbit/s, each 2 bits are encoded into 4FSK symbol using Gray mapping
DC offset control:
  A polarity indication symbol is inserted in front of each 32 symbol block
  The 33 symbol block is either inverted or not, as to maintain lower cumulative DC bias
  DC offset control is important in PLL-based transmitters

## Slide 11
FH PHY Scrambler
Scrambling is applied just to PLCP_PDU, not to PLCP header
Scrambling is performed by a bitwise XOR with LFSR sequence with 127 bit period, with 1+x4+x7 feedback polynomial
Same method is used for scrambling and descrambling

## Slide 12
Bits to Symbol Mapping
1 bit (with 2GFSK) or 2 bits with (4GFSK) are mapped to a symbol
at 2 bits/symbol Gray coded mapping is used, as customary with multilevel modulations.
2GFSK and 4GFSK have same RMS frequency deviation

## Slide 13
DC Bias Control
The DC offset control is instrumental in reducing "baseline wander" in PLL based implementations (problem similar to transformer coupling in wired networks)
Polarity indication symbol is added in front of each 32 symbol block - "0" for 2GFSK, "00" for 4GFSK (the symbol with most negative frequency offset)
The sign of DC offset contribution of the 33 symbol block is compared to sign of previous accumulated DC offset; if same sign, the block is inverted (frequency deviation reversed at each symbol).
At receive side, the polarity of the first (indication) symbol is tested- if positive, next 32 symbols are inverted.

## Slide 14
Transmit Ramp Up and Ramp Down
The gradual Ramp Up and Ramp Down are required to reduce the splatter (spikes) in adjacent channels at start and ending of the packet.
Up to 8 microseconds of the PLCP idle pattern and 8 microseconds following the last symbol of the PLCP_PDU are allocated to gradual increase and decrease of transmit power
The minimal ramp time is dictated by adjacent channel interference specifications, and is not specified directly in the standard

## Slide 15
Indoor Environment - Multipath Fading
Multiple propagation paths, interfering with each other, create a frequency selective fading.
The fades are correlated at adjacent frequencies and get decorrelated after few megahertz in an indoor environment

## Slide 16
Frequency Hopping Sequences- Reqts.
Design Criteria:
  Assured minimum hop distance for multipath diversity performance
  Minimizing hits and adjacent channel hits between different hopping patterns
  Minimizing consecutive hits between different hopping patterns
FCC 15.247 requirement: Pseudorandomly ordered frequency list

## Slide 17
Frequency Hopping Sequences
Predesigned computer generated pseudorandom list of 79 frequencies
Minimum hop distance of 6 channels
Additional hopping sequences derived by modulo 79 frequency offset
78 hopping patterns organized in 3 sets of 26 patterns each.
  Sequences from same set collide 3 times on average, 5 times worst case, over a hopping pattern cycle, including hits and adjacent channel hits.
Aggregate throughput continues to increase up to about 15 collocated networks, at high load conditions.

## Slide 18
Frequency Hopping Sequences- cont.
Denote frequency as 2402+b[i], b[i] is the base sequence in range 0.. 78.
k-th sequence is formed from the base sequence as 2402+(b[i]+k) mod 79
Example:
  Base seq: 2402, 2456, 2472, 2447, ...
  30-th seq: 2432, 2407, 2423, 2477, ...
Notes: 16
16

## Slide 19
FHSS Transmitter Specifications
Deviation:
  Upper bounded by FCC requirements
  Lower bounded to +/-110 KHz in order to maintain sensitivity
Shape accuracy:
  Zero crossing instants accuracy - <+/- 1/8 symbol (at 2GFSK)
  Level accuracy
Center Frequency accuracy - 60 KHz (25 PPM)
Symbol rate - 1 MHz +/- 50 ppm
Hop Time- transmitter has to settle within 224 microseconds to within 60 KHz off nominal center frequency after

## Slide 20
Receiver Performance Specifications
Parameter 1 Mb/s 2 Mb/s
Sensitivity -80 dBm -75 dBm
Desensitization
@ 2 Mhz offset 30 dB 40 dB
@ 3 Mhz or more 20 dB 30 dB
Intermodulation Protection 30 dB 25 dB

## Slide 21
CCA- Clear Channel Assessment
CCA is used to:
  Initiate frame reception
  Avoid transmitting when the channel is busy
The Backoff Slot width for FHSS PHY is 50 microseconds. The CCA should detect a signal which started up to 16 microseconds before end of the slot
CCA Sensitivity:
  -85 dBm for PT<20 dBm, reduced by 0.5 dB for each dB of power increase
  Detection during 0101 pattern within 20 microseconds with 90% probability