## Slide 1
1
High Rate DS PHY
IEEE 802.11 High data rate PHY extensions
Introduction
Definition
Technical Approach
Performance Predictions
Notes: 1
This paper address the PAR topic of Higher Speed PHY extensions to the 802.11 Standard. This proposal is submitted by Harris Semiconductor for the purposes of suggesting a suitable DS extension that will smoothly integrate with the existing PHY definition. The DS PHY can operate at higher rates with comparative ease due the the FCC rules that cover the operation at 2.4 GHz for DSSS modulation.
This paper will outline the essence of the Harris proposal.

## Slide 2
2
Tradeoffs
The 802.11 PHY group has identified a need for higher data rates
For higher data rates, we need a new DSSS waveform that has:
  good power efficiency (range)
  "10 dB PG", i.e. will pass FCC CW jammer test
  acceptable multipath performance
  Low to moderate amplitude modulation
  low implementation cost
It would be desirable to use the existing preamble and PLCP header, so it would be interoperable with lower rate stations.
Notes: 2
At the November, 1996 meeting, the Higher Speed PHY PARs Study Group met and suggested that a PAR be issued to address the needs for higher data rates. This group did not want to disturb the ongoing standards acceptance process, so it held its suggestion to a new PAR. Additionally, the existing 802.11 PAR is due to run out this year, so to do ongoing extension work, we will need a new PAR.
The market potential for higher data rates is obvious but will depend on the availability of a suitable implementation that meets some basic requirements for range, performance and rate. most notably, the DS PHY needs a new waveform that achieves good modulation efficiency for adequate range. This is tightly coupled with good multipath performance which is one of the primary limitations to achieving acceptable packet error rates at ranges that satisfy the user. Schemes that require heroic processing to achieve this performance will price themselves out of the market even if they achieve the higher rates.
Another performance need is to meet the FCC's rules for processing gain.
Additionally, it would be nice to make it backwards compatible.

## Slide 3
3
Modulation Options
There are several options for increasing the data rate
  Multiple bits per symbol
    M-Ary Orthagonal Keying
    Cyclic Code Shift Keying
    M-QAM with 11 MCps spreading
  M parallel carriers
    Orthogonal Frequency Division Multiplex (OFDM)
    M parallel orthogonal Spread signals
  Others
Higher spread rate not considered, it reduces number of available channels too much
Notes: 3
The schemes that have been considered for the higher rate modulation are variations on the DS architecture where more complex modulations are used in place of the BPSK and QPSK of the standard. Of these, various forms of M-Ary Orthagonal keying and QAM have been suggested. Multiple parallel channels of FDMA or CDMA carriers are also on the plate for consideration. These must be traded off to find the one with the best combination of properties.
We do not want to consider simply making the spread rate higher since that reduces the number of available channels for separate networks and the number is already very low. That might work for the 5 GHz bands, but it raises interoperability questions.

## Slide 4
4
Pick One
of 8 spread
Functions
MUX
1:8
3
3
DATA
IN
I OUT
Q OUT
1.375 MHz
11 MHz
1
1
Data Rate = 8 bits/symbol * 1.375 MSps = 11 MBps
Pick One
of 8 spread
Functions
Scrambler
1
1
MOK Modulation Approach for 11 MBps
Notes: 4
M-ary orthogonal keying has been known for many decades, and indeed, can be shown to be a generalization of many standard waveforms such as FSK. In this scheme, the spread function is picked from a set of M orthogonal vectors by the data word. Since the I and Q channels can be considered independent when coherently processed, both can be modulated this way. That allows us to pack 8 bits into each symbol. The most well known orthogonal vector set is the Walsh function set. It is available for 8 and 16 chip vectors and has true orthogonality. Unfortunately, 11 chip vectors are not available in an orthogonal set although cyclic rotations of the Barker word are nearly orthogonal.
To make the modulation have the same bandwidth as the existing 802.11 DS modulation, the symbol rate is increased to 1.375 MSps while the spread rate is kept at 11 MCps. This makes the overall bit rate 11 MBps.

## Slide 5
5
MOK properties
This modulation is most power efficient
The spectrum is like the 802.11 DSSS
Multipath performance is nominal for the SNR
Requires coherent processing
Moderate implementation complexity
Notes: 5
March 1997 doc: IEEE P802.11-97/25
____________________________________________________________________________
Submission: High Rate DS PHY Carl Andren, Harris
03/21/97
5
MOK modulation has been shown to have slightly better Eb/N0 performance than BPSK due to embedded coding properties. This makes the waveform the most power efficient of the candidates. This allows the modulation to tolerate more interference than other waveforms. Since there are more bits per symbol with this modulation, it naturally requires more Es/N0 than BPSK, but the increase is minimized.
The spectrum of this waveform is sinx/x, which is the same as the 802.11 waveform now, but without some of the little blips that the 11 bit sequence causes.
The multipath performance will depend on the Eb/N0 and phase distortion tolerance of the waveform. We have shown through simulation, that this signal will have an adequate performance in the indoor environment. It is obviously worse than the 1 MBps case which can tolerate an SNR of 0 dB.
While this, and any other waveforms need to exhibit 10 dB processing gain, the FCC is liberal in its interpretation of the specification and allows Es/N0 to be used for the SNR in the CW jammer test for processing gain. With this interpretation and with the right implementation, the FCC’s needs can be satisfied.

## Slide 6
6
Pick One
of 8 Cyclic
Shifts
MUX
1:8
3
3
DATA
IN
I OUT
Q OUT
1.375 MHz
11 MHz
1
1
Data Rate = 8 bits/symbol * 1.375 MSps = 11 MBps
Pick One
of 8 Cyclic
Shifts
Scrambler
1
1
CCSK Modulation Approach for 11 MBps
Notes: 6
The MOK theme can be also done with Cyclic Code Shift Keying. This variant is simpler to demodulate since only one sequence needs to be correlated for. We can do CCSK with an 11 bit Barker sequence at 1 MSps, if desired. This, however, would not achieve the 10+ MBps desired since the number of bits per symbol is not great enough.

## Slide 7
7
CCSK properties
The CCSK modulation symbols are not orthogonal, so they do not achieve as high an efficiency as MOK.
The CCSK symbols are susceptible to long range multipath.
Requires the least hardware to implement.
Notes: 7
The CCSK modulation technique is not quite as efficient as MOK since the symbols are not entirely orthogonal. cyclically shifted Barker words are reasonable good, however, and achieve almost the same Eb/N0 as MOK.
The main problem is that the cyclically shifted symbols are multipath susceptible when the multipath delay spread gets to be more than a chip's length. Therefore, long (for indoors) multipath will defeat this method.
The CCSK scheme is quite simple to demodulate and requires very little added hardware over the basic 802.11 waveform.

## Slide 8
8
QAM approach
1024 QAM
Modulator
11 MCps
PN
Generator
I
Q
DATA
10 bits/symbol * 1 MSps = 10 MBps
Notes: 8
One way to get bandwidth efficiency while still spreading (an oxymoron) is to use QAM for the data modulation. QAM is relative easy to spread and achieve a spreading bandwidth ratio of 10 or greater.

## Slide 9
9
QAM properties
1024 QAM is very sensitive to distortion and would need an equalizer to even be considered.
Does not achieve a good Eb/N0
Notes: 9
While this modulation will fill the bill, it is very sensitive to multipath, since 1024 QAM requires a very lean, undistorted signal. The Eb/No performance of QAM is not as good as MOK since it has both phase and amplitude components. This sensitivity to distortion implies the use of an equalizer which is undesirable on two counts. First, it requires a training sequence which will increase the length of the preamble. Second, it will increase the cost to add the equalizer.

## Slide 10
10
Parallel Spread Channels Approach
DATA
MUX
BPSK
SPREAD
BPSK
SPREAD
SUM
10 MBps
16 SPREAD CHANNELS AT 0.68 kBps = 10 MBps
Orthogonal Code Division Multiplex (OCDM)
Notes: 10
This technique has been announced by Sharp for their 10 MBps modem. They use CCSK Barker words for the 'orthogonal' PN spread channels. Basically, this technique uses multiple CDMA channels to send more data. Basically, 16 parallel channels of 16 chip orthogonal symbols are BPSK modulated and summed in an analog sense. This provides 16 parallel channels of data at a modest symbol rate. It could be said to have a 12 dB processing gain.

## Slide 11
11
OCDM Properties
Multiple summed orthogonal signals produce a high degree of incidental amplitude modulation.
Good Eb/N0 (power efficiency)
Same spectrum as 802.11 currently
Moderate implementation complexity
Notes: 11
The Orthagonal Code Division Multiplex scheme produces a high degree of amplitude modulation as it sums 16 independent channels. This is undesirable in that it then needs a very linear PA to meet the spectral mask.
This technique has good Eb/N0 and a sinx/x spectrum. The processing needed to demodulate it is about the same as the MOK scheme.

## Slide 12
12
OFDM Approach
DATA
MUX
BPSK
Channel 2
BPSK
Channel 1
SUM
10 MBps
16 FREQUENCY CHANNELS AT 0.68 kBps * 1 bit/channel = 10 MBps
Orthogonal Frequency Division Multiplex (OFDM)
Notes: 12
Orthagonal Frequency Division Multiplex has been adopted by one or more announced 10 MBps suppliers. It takes the approach of multiple frequency channels at regular spacing with each one modulated by PSK. MIL-STD 188C has used this technique for decades in wireline and radio modems. It is commonly radiated over Single Sideband Radios since it is very tolerant of spectral notches due to multipath. Diversity is necessary to make it work in this environment since a narrowband fade can remove one or more of the carriers. By spreading symbol energy over multiple frequencies, a robust link can be made.

## Slide 13
13
OFDM Properties
Best use of the spectrum with flat characteristic.
Large degree of amplitude modulation.
  Means that a very linear power amplifier is required
Complex processing (FFT)
  More cost and power consumption
Good spectrum and power efficiency in waveform
Can use differential, non-coherent processing
Notes: 13
This modulation makes best use of the spectrum with the channel filled edge to edge uniformly. This makes for the least interference to other users with the most noise like spectrum.
The summing of 16 independent carriers can produce large amplitude modulation which makes the transmitter difficult. It also rules out limiting in the receiver.
The processing of OFDM is traditionally done with FFTs and inverse FFTs. These are generally more complex and power hungry that the techniques used for the other waveforms.
Each of the BPSK or QPSK modulated carriers can employ differential coding to make the baseband processing somewhat simpler.

## Slide 14
14
Trade Table
Lower is better
Notes: 14
The trade table above will make for much controversy. Many will argue with the even weighting used and others will pick on the judgments of the relative merits of the waveforms. Nonetheless, some trade table such as this is necessary to put all the factors on the table and get ready to discuss them.
The table shows the MOK scheme as having the lowest score and QAM the highest.

## Slide 15
15
Standard Definition Issues
Lack of 10+ MBps Physical Layer standard
  Provide backwards compatibility to IEEE 802.11 at 1&2 MBps
Limited bandwidth available in the ISM bands
  Maximize bits/Hz
  Need at least 3 channels
Meet FCC requirements for ISM bands
  Preliminary review is encouraging
  FCC is comfortable with any solution that passes CW test
Interoperate with 1&2 MBps equipment
Notes: 15
The factors we need to address in the choice of an extension to the standard are:
Bandwidth occupied. We could up the spread rate, but the existing scheme is already down to 3 or 4 channels in the ISM band. Fewer channels is undesirable.
We have sought guidance from the FCC and have gotten the following: If you can pass the CW jamming test, they have no problem with your waveform. For the purposes of the test, SNR can be defined as your theoretical Es/N0.
It is highly desirable to tie the existing standard into the loop. We have studied the question and concluded that the new rates can be incorporated along with the existing rates at the expense of retaining the PLCP header as is. This saddles the high rate system with an overly long preamble, but it makes the systems interoperable. This is very good in that the user can add high rate nodes as needed and use the lower rates to fill coverage gaps in the high rate system. The interleaved rate system will be well behaved and defer the medium for the appropriate length of time as desired. The low rate preamble will reach further than the message, but the power density will be the same.

## Slide 16
16
High Rate 802.11 Features
Provide 10+ MBps wireless LAN data rates while maintaining interoperability with 1 & 2 MBps WLANs
Increase data rate by at least 5x with no increase in the transmit bandwidth requirement
Rate switching during packets is supported already
Notes: 16
The benefits of a good high rate waveform are an increased longevity in the marketplace and no obsolescence of the early entries. By making the units interoperable, they can be introduced seamlessly into the market.
The new methods shown are benign in that they do not increase the current occupied bandwidth. Up to 5.5 times higher data rates are achieved.
The mechanism for rate switching has already been incorporated and the new rates fit with the definitions already established.
The increase in complexity of the high rate system is still within the realm of fitting into a PCMCIA package now.

## Slide 17
17
Modifications to Standard
To get high rate use more complex modulation at same spread rate.
Use standard PLCP preamble and header to establish carrier phase and frequency lock.
Notes: 17
The 802.11 standard can be easily modified to accommodate the new waveform. The basic modifications are to the sections covering the DSSS PHY layer. The only modifications are to the actual modulation and resulting performance parameters. The current sections on DSSS contain separate sections on 1 and 2 MBps and this can b extended to cover the new rates. Some overall changes to the spread function also need to be addressed.
The PLCP header only needs to have the new rates added to the `list of acceptable rates.
A note in the modulation section to have the phase reference defined has to be added.