High Speed Study Group PAR Proposal for 3 Mbit/s extension of 802.11 FH PHY in 2.4 GHz band

Naftali Chayat,Naftali Chayat, SG Chair BreezeCom    Johnny Zweig, Netwave    Keith Amundsen, Raytheon

Following is a proposition for a separate PAR for the FH high-speed extension. Although the speed increase is relatively small, the preparedness of the material and the fast expected completion schedule give this PAR a significant chance of being approved by the ExecCom. The workload on the 802.11 group resulting from this project is negligible, as the text for inclusion already exists (802.11-96/80). We propose that the High Speed Study Group will issue a separate PAR for 3 Mbit/s FH PHY extension, as described below.

What follows is a proposal for a PAR, with the following revision history:

Revision 1:	As finalized during the meetings of the study group meetings during 11-13 March 1997

Revision 2:	By the Study Group on 14 March, 1997, after remarks from an interim plenary on 13 March 1997.

Revision 3:	By Naftali Chayat, according to remarks by Pat Thaler (member of Executive Committee)

IEEE STANDARDS PAR FORM

(1/96)

Fill in the answers to the questions in the bracket provided. A Hard Copy of this document must be printed, signed with the appropriate signatures and mailed or faxed to the Standards Department for submission to NesCom.

1.  Sponsor Date of Request _______________________

2.  Assigned Project Number (confer with staff) _______________________

3.  PAR Approval Date (leave blank) ________________________

4.  Project Title, Copyright Agreement and Working

Group Chair for This Project

I will write/revise a Standards Publication with the following TITLE (Spell out all acronyms)

[X] Standard [for] (Document stressing the verb "SHALL."), or

[  ] Recommended Practice for (Document stressing the verb

"SHOULD.") or

[  ] Guide for (Document stressing the verb "MAY.")

TITLE:

[

Standard for Wireless Medium Access Method (MAC) and Physical Layer (PHY) Specifications - SupplementStandard for 3 Mbit/s Physical Layer (PHY) extension for the Frequency Hopping (FH) Physical Layer (PHY) for High Speed Wireless Local Area Networks (LAN) in the 2.45 GHz band  ]

I hereby acknowledge my appointment as Official Reporter (usually the W.G. Chair) to the (Name of Working Group)

[Vic Hayes, Chair  P802.11  802.11

Working Group for Wireless Local Area Networks ]

In consideration of my appointment and the publication of the Standards Publication identifying me, at my option, as an Official Reporter, I agree to avoid knowingly incorporating in the Standards Publication any copyrighted or proprietary material of another without such other's consent and acknowledge that the Standards Publication shall constitute a "work made for hire" as defined by the Copyright Act, and, that as to any work defined, I agree to and do hereby transfer any right or interest I may have in the copyright to said Standards Publication to IEEE.

Signature of Official Reporter ______________________________________________

Name				Vic Hayes

Date				xx-xxx-1997

Title				802.11 Chair

Company			Lucent Technology

Address				Zadelstede 1-10

City				Nieuweigen

State				Netherlands

Zip				3431 JZ

IEEE Member Number

Telephone

Fax

E-Mail

Name				[ Vic Hayes ]

Date				[ xx-xxx-1997 ]

Title				[ 802.11 Chair ]

Company			[ Lucent Technologies WCND B.V. ]

Address				[ Zadelstede 1-10 ]

City				[ Nieuwegein ]

State				[ Netherlands ]

Zip				[ 3431 JZ ]

IEEE Member Number		[ 01550144 ]

Telephone			[ +31 30 609 7528 ]

Fax				[ +31 30 609 7556 ]

E-Mail				[ vichayes@lucent.com ]

5.  Describe this project:  (Choose ONE from each group below)

a.	[  ] Update an existing PAR

[  ]Yes or [X]No

If YES, project number/approval date)_______________________

Is this in ballot now?  [  ]Yes or [  ]No

b.	[  ] New Standard

[  ]Yes or [  ]No

[  ] Revision of an existing standard.

[  ]Yes standard number/year______________________ or [  ]No

[X] Supplement to an existing standard

[X  ]Yes standard number/year    802.11-1997      ______________________ or [  ]No

c.	[X] Full Use (5-year life cycle)

[  ] Trial Use (2-year life cycle)

d.	Fill in target completion date for submittal to

IEEE Standards Review Committee (RevCom).

[   31 June 1998July 1999  ]

6.  Scope of Proposed Project (What is being done including the

technical boundaries of the project?)

[   To incorporate the developed 3 Mbit/s  a High Speed (about 20 Mbit/s)extension to 802.11 Frequency Hopping PHYPHY  in 2.4 GHz band for use in fixed, moving or portable Wireless Local Area Networks. The PHY will be used in conjunction with the 802.11 Medium Access Control (MAC). ]

7.  Purpose of Proposed Project [Why is it being done,

including the intended user(s) and benefits to that user(s)]

[To extend the performance and the range of applications of the 802.11 compatible Frequency Hopping networks in the 2.4 GHz band by increasing the achievable data rate.To create a high speed wireless access technology suitable for data, voice and image information services. This technology should be beneficial for improved access  to the Global Information Infrastructure and wired LANs, as well as creation of high performance ad hoc networks.

The project will focus on communication techniques which use the spectrum efficiently and enable a high aggregate throughput, as well as high speed for an individual network. ]

8.  Sponsor (Give full name; spell out all acronyms) Society/Committee:

[  Computer Society - LMSC  ]

9(a.1) [NO  ] Are you aware of any patents relevant to this project?

(If YES, attach explanation, or No)

NO. In the field of modem technology  there are patents, but according to IEEE 802 policy an attempt will be made to avoid use of patented techniques, unless significant advantage is proven.

9(a.2) [NO  ] Are you aware of any copyrights relevant to this project?

(If YES, attach explanation, or No)

NO

9(a.3) [NO  ] Are you aware of any trademarks relevant to this project?

(If YES, attach explanation, or No)

NO

9b. [NOX] Are you aware of any other standards or projects with a similar scope?

(If YES, attach explanation, or No)

YES

European HIPERLAN Type 1, developed by ETSI

European HIPERLAN Type 2,3 (Wireless ATM oriented) being developed by ETSI

The “Magic Wand”, a Wireless ATM demo being developed by a consortium of European companies under the auspices of ACTS (Adv. Comm. Tech. ????)

9c. [YES  ] Is this standard intended to form the basis of an international standard?

(Yes, or if  NO, attach explanation, or Do Not Know)

YES

9d. [NO  ] Is this project intended to focus on health, safety or environmental issues?

(If YES, attach explanation, or No, or Do Not Know))

NO

10. Proposed Coordination/Recommended Method of Coordination (Coordination

is accomplished in any of the following three ways:

Circulation of Drafts or Liaison Membership or Common Membership.)

US TAG 			(Circulation of Drafts)

ETSI - RES10 	(Circulation of Drafts, Common Membership)

10a. Mandatory Coordination

SCC 10 (IEEE Dictionary) 			Circulation of Drafts

IEEE Staff Editorial Review			Circulation of Drafts

SCC 14 (Quantities, Units, and Letter Symbols) 	Circulation of Drafts

10b. IEEE Coordination requested by Sponsor:

(Use additional page if necessary).  If you believe your project

will require a Registration Authority, please list IEEE RAC

(refer to Working Guide).

[    US TAG to JTC-1 SC6					(Circulation of Drafts)     ]

If coordination is not required, please attach an explanation.

10c. Additional Coordination Requested by Others.  (Leave blank.  This will be completed by the Standards Staff).

11. Submitted by: (This MUST be the Sponsor Chair or the Sponsor's Liaison Representative to the IEEE Standards Board)

Signature of Submitter_________________________

Name			[ Jim Carlo (802 chair) ]

Title			[ IEEE 802 LMSC Sponsor Chairetc. ]

Date			[ xx-xxx-1997 ]

Company		[ Texas Instruments ]

Address			[ 9208 Heatherdale Drive ]

City			[ Dallas ]

State			[ Texas ]

Zip			[ 76243 - 6332 ]

IEEE Member Number	[ 05572953 ]

Telephone		[ +1-214-480-2524 ]

Fax			[ +1-214-480-2611 ]

E-Mail			[ jcarlo@ti.com ]

[

Supplement to a “Higher Speed Wireless LAN  PHY in 2.4 GHz band” PAR

Scope of the Project

The 802.11 MAC defines a mechanism for operation of stations supporting different data rates in same area. The current 802.11 standard already defines two rates - 1 Mbit/s and 2 Mbit/s  for both Frequency Hopping (FH) and Direct Sequence (DS) PHYs. The two rates are supported by having same header for both rates with length and rate information passed in the header at the lowest (“basic”) rate; then the body of the packet is transmitted at the rate chosen and with corresponding modulation method. The header structure of the two PHYs already supports passing rate information up to 4.5 Mbit/s (in 0.5 Mbit/s increments) for FH and up to 25.5 Mbit/s (in 0.1 Mbit/s increments) for DS. The 802.11 MAC already incorporates interpretation of this information and computation of expected packet duration even if it the specific station does not support the rate at which the packet was sent.

The proposed 3 Mbit/s extension of the 802.11 standard was reviewed by an ad hoc group high-speed study group of the FH PHY working group of 802.11. The proposed extension is compatible with the existing 802.11 PHY’s on a header level and is able to take advantage of the multirate mechanisms supported by 802.11 MAC. The scope of the proposed project is to incorporate the 3 Mbit/s extension into the standard.

To develop a High Speed (about 20 Mbit/s) PHY for use in fixed, moving or portable Wireless Local Area Networks. The PHY will be used in conjunction with the 802.11 Medium Access Control (MAC)

Radio Spectrum

Currently 802.11 supports rates of 1 and 2 Mbit/s rates in the 2.4 GHz ISM band. Since the inception of 802.11 things have changed both in a regulatory arena and regarding the needs for higher transfer rates.

Specifically, in the US, FCC released 300 MHz in three 100 MHz subbands in the 5 GHz region (ET Docket 96-102) for an unlicensed use with high speed Local Area Network communication services. The structure of the new regulations encourages communication at speeds of about 20 Mbit/s. These rulemakings are evidenced by subpart E - Unlicensed National Information Devices in Part 15.4xx.

Given the regulatory changes (as opposed to 15.247 which was the basis for 802.11’s work), it becomes feasible to develop efficient high speed modulation methods to address the 20 Mbit/s speed range. The scope of the proposed PAR is to propose such modem technology and methods as to take advantage of the new regulations. The modem technology will be examined with respect to propagation impairments typical of both indoor and reasonable range outdoor environments.

In order for the developed standard to be applicable geographically as widely as possible, the committee will be authorized to correspond with regulatory bodies worldwide.

Compatibility with 802.11 MAC

The 802.11 PAR mentions that the MAC will be capable of operation in the 1-20 Mbit/s range. The intent of the effort of this PAR is to examine rates beyond the 20 Mbit/s range. The 802.11 MAC will be reviewed for it’s capability to support such rates. In addition, the MAC will be reviewed to examine its capability to support the data, voice and image services intended in the rulemaking.

The Clear Channel Assessment (CCA) mechanism in the Physical Layer will be developed to operate with 802.11 MAC. In addition, the CCA will be developed to  ensure fairness with respect to participating stations and ensure operation in presence of other types of radio devices operating in the environment, according to the spirit of the FCC rulemaking.

The proposed PHY with 802.11 MAC will meet Quality of Service as detailed in 802.11 PAR.

]

Five Criteria

Broad Market Potential

The market potential of the 3 Mbit/s FH PHY is synergistic with the market potential of the 802.11 itself. The 3 Mbit/s FH 802.11 products will enable the upgrade of existing networks to a higher speed for selected users or in selected areas. The existence of such possibility will also have a positive effect  on the confidence of the public in 802.11 standard.

The 3 Mbit/s extension, relative to the current 2 Mbit/s data rate, may look insignigicant. Yet, we may look at the difference between 33.6 Kbit/s telephone modems versus 28.8 Kbit/s modems in which the relatively small difference in performance creates a more positive public image of the technology.

To support the claim for the broad need for high speed wireless networking, let us quote the FCC ET 96-102 Docket, which expands on the potential uses of such a technology. Applications such as education, medical, business,  consumer, telecommunication extensions and community Internet access are mentioned.

The applications today tend to be more graphically intensive and include voice and video. The volumes of data involved in medical image transfer are tremendous.

The trend in both the networking and the telecommunication industry to increase the speed of their products and the services they provide creates a market need for the wireless LAN to  match the throughput capabilities of the WAN.

US government actively supports wireless access to information, as is reflected by issuing the FCC Report and Order on January 9, 1997, for Docket 96-102. The large potential of the US market alone is reflected in the over 50 commentors’ market assessments contained in the responses to the FCC’s Notice of Proposed Rule Making. The frequency band allocated in the FCC Docket overlaps with a 5.2 GHz band allocated in western Europe for high speed local networking (the HIPERLAN project). Coordination with worldwide regulatory bodies will be attempted to ensure even wider market potential for the technology to be developed in this Project.

High degree of interest expressed by multiple vendors and the history of active participation of multiple vendors in 802.11 PHY standardization process promise that the standard will be accessible to multiple vendors. In addition, semiconductor manufacturers are expected to provide solutions for the emerging standard, making the technology available to multiple system manufacturers.

The 5 GHz radio component technology  is starting to develop and we believe that the U-NII rulemaking will give a boost to availability of such components.

The modem component technology needed to support 20 Mbit/s operation is of a scale comparable to cable modems or satellite Direct Video Broadcasting. This makes it reasonable to believe that components will be available from several vendors to implement the PHY resulting from the proposed Project.

We believe that the cost of the PHY resulting from this project will be comparable to the cost of wireless LAN adapters based on current 802.11 technology. The complexity of the PHY operating at 20 Mbit/s should be a few times higher than a solution for the current Direct Sequence Spread Spectrum PHY specification operating at 11 Mchip/s, but taking into account the progress in semiconductor device density the cost should be comparable, once appropriate ASICs are developed.

Compatibility with IEEE Standard 802

The compatibility with IEEE 802 requirements will result from the use of 802.11 standard as a basisMAC, which itself was developed to be compatible with those requirements.

Distinct Identity

The proposed Project is a straightforwardhigher-data-rate extension of the existing 802.11 Project. It might be argued that such an extension should be dealt within a framework of 802.11 maintenance, but it should probably be dealt within a separate Project framework.

distinct from the present 802.11 Project in that it is not restricted by CFR47 15.247 rules. As a result, usage of spread spectrum techniques in no longer required, and wider bandwidths are allowed. These factors enable significantly higher data rates.

This proposed PHY standard will provide for high performance (circa 20 Mbit/s) asynchronous wireless data communications in a local area network utilizing distributed coordination. In addition, time bounded services are implemented utilizing a centrally coordinated function. Both of these provisions are supported in the 802.11 MAC. In addition, this PHY layer standard will extend the 802.11 wireless LAN specification.

Technical Feasibility

Modulation Methods: The 3 Mbit/s modulation method was reviewed by an ad hoc study group of the FH PHY working group. This modulation method is incorporated as a proprietary extension in a product which has operated in the field since 1995. The product in which the proposed modulation method is incorporated passed the FCC licensing procedure.

Radio Technology:The technical feasibility of the radio part is already proven by existing 5.7 GHz products. The 3 Mbit/s extension uses same radio technology as 1 Mbit/s and 2 Mbit/s modulationsrequirements of a High Speed PHY are not significantly different from today’s ISM systems. Somewhat tighter specifications may be required for some components.

The increased processing requirements of the digital modem part are in line with the progress in ASIC technology. There are demonstrations of modem technologies which we believe to be of comparable complexity, such as XDSL, cable modems, satellite DVB modems,  etc.

Range and Cell Size: The tenfold increased in data rates will need to be traded for shorter range. , compared to 2 Mbps ISM device, is expected to reduce the cell radius by an estimated 40% (assuming fourth power propagation law). In addition, the 5 GHz band does not experience interference from microwave ovens.

Economic Feasibility

The economic feasibility of the proposed Project draws on the feasibility of 5 GHz radio technology available today and of our expectations of modem complexity. Once 5 GHz MMICs proliferate, the cost is expected to drop to that comparable to today’s 2.4 GHz technology. Some cost penalty may be incurred by tighter filtering requirements at the band edges, as FCC requires. Test equipment for higher frequency range may cost more, incurring some additional penalty on product cost. The architecture required to support the 3 Mbit/s extension is idntical to that required for 2 Mbit/s support. Therefore the cost of such product is only marginally higher than of a 2 Mbit/s product. The slight cost increase may be associated with higher accuracy modem ASICs requirements on the radio.will be somewhat more expensive than current 2.4 GHz modems. The overall cost of a 5 GHz high speed LAN adapter should be marginally higher than the current 802.11 adapter.

The installation of extended 5 GHz devices is same as regular 802.11 devicesat the stations is not different from a 2.4 GHz LAN, and has almost no associated cost. The infrastructure cost (Access Points) is expected to be almost the same with the exception of cost incurred by somewhat higher, due to smaller cell size than with lower rate 2.4 GHz equipment. Taking into account the higher rate of the proposed PHY, the overall cost/performance ratio should improve over ISM type network.Upgrading an existing network to a higher speed can be performed selectively in areas with a demand for higher instantaneous rate.

# Comments

Comment made by Pat: I think it is appropriate to add comments about the availability of this spectrum for this use outside the US since it is my underdtanding thatt that is one of the advantages of this band.

Comment made by Pat: Rather than this predictive statement (I am not sure who will be authorizing this and if it is already authorized, I do not know how you can make this statement)  I suggest the following:

IEEE P802.11 has actively corresponded with regulatory bodies worldwide in order to encourage spectrum allocatins to allow its standards to be applicable geographically as widely as possible and plans to continue these activities.

The scope and purpose statements do not indicate such intent! The purpose specifically mentioned 20 Mbit/s and Physical layer.  If MAC extentions are planned, you need to say it in scope!

Pat does not know what CCA is, she wrote: What is Clear Channel Assessment?  How can a Physical layer, yet undefined contain a mechanism?  You need to set context.  Or do you mean to say you will be requiring any proposal to have a CCA?

Indent or use quotes so people can tell where the quotes start and ends.