## Slide 1
HIPERLAN MAC Overview For IEEE 802
Tim Phipps, Symbionics
tgcp@symbionics.co.uk

## Slide 2
MAC Service Definition
Service definition is based on ISO 15 802-1
  To a higher layer the HIPERLAN MAC service interface looks very much like an “ordinary” MAC layer
  IEEE 48 bit addresses
  Quality of Service (QoS)
    User Priority (0 or 1)
    MAC SDU Lifetime (in milli-seconds)

## Slide 3
HIPERLAN Architecture
All nodes are equal
  Peer-to-peer communication
  No central controller, or “hub”
A node may bridge to a wired network
  Acts as an “access point”
  It does not have any other “special” functions just because it is a bridge

## Slide 4
Distributed MAC Architecture
Unlike 802.11 there is no centralised PCF
  HIPERLAN only has a few channels available and so different systems may have to share the same channel “fairly”
  QoS can be supported in non-centralised manner
Can bridge to a wired network
  Bridges learn the location of MAC entities and copy data from input to output port if appropriate
  HIPERLAN MAC layer and wired MAC layer can bridge data between themselves
    HIPERLAN can be used for broadband radio access to an infrastructure network
  This Access Point (AP) has no other special functions
All functions are distributed
  For example: Channel Access Control, Power Saving, Generating lookup confirm PDUs

## Slide 5
HIPERLAN Differentiation
Two HIPERLANs may occupy the same channel and location
  Differentiation is by HIPERLAN identifier (and name)

## Slide 6
Differentiation
HIPERLAN differentiation
  How to differentiate logical groups of nodes (HIPERLANs) ?
  A string, the HIPERLAN name
  A number, the HIPERLAN identifier
    Name to identifier mapping should not clash
  Similar to the 802.11 concept of a Basic Service Set (BSS) or an Extended Service Set (ESS)
  You belong to a HIPERLAN if you have the same name and identifier
HIPERLAN discovery
  Joining node sends Lookup PDU
  One of the established nodes sends a Confirm PDU including the HIPERLAN name and identifier
  Similar to 802.11 probe and probe response

## Slide 7
MAC Service Provision
Queue of packets is NOT necessarily a FIFO
Packet selected for transmission based on priority
Priority determined by
  Residual lifetime
  User priority
  Expected number of radio hops
Highest priority packets jump to the front of the queue!
  Shorter lifetime means higher priority means less queuing time
  Therefore, QoS can be supported for a mixture of applications
Channel Access Control (CAC)
  Accepts MAC packets for transmission, with priority as a parameter
  (CAC covered by another presentation)

## Slide 8
MAC Service Provision
Mapping MAC QoS to MAC priority
  1. Generate priority
  2. Order by priority
  3. Select head of queue for CAC

## Slide 9
MAC Layer Error Control and Filtering
Error Control
  Packet is discarded once a good acknowledgement (ACK) is received
    Multicast and broadcast packets are not acknowledged
  OR when lifetime expires
Receive Filtering
  Duplicates may occur in radio networks
    Because of missing ACK
    Broadcast may be relayed by more than one node
  Receiver filters on destination address
  Receiver also checks source sequence number for duplicates

## Slide 10
Security
Implementation of security features is optional
Security is based on encryption with a secret key
  A node may have 3 keys
  The key index is sent “in the clear”
  User data is encrypted
Encryption algorithm is specified
  There is only one algorithm
Key distribution mechanism is not specified

## Slide 11
Power Saving
Implementation of power saving features is optional
Power Saving Node (p-saver)
  Advertises when it will wake to receive individual (point-to-point) data
  The advertised pattern is the Individual Pattern (IP)
  IP includes regular wake and sleep phases
Power Supporting Node (p-supporter)
  Delays transmission to p-saver until the next wake phase
  Advertises when it will send group (point-to-multipoint) data
  The advertised pattern is the Group Pattern (GP)
  GP includes regular wake and sleep phases that p-savers can follow
  P-supporter ensures that group data is sent during wake phase of the GP

## Slide 12
Management Information Base
Power saving / supporting capability
Current radio channel
Observed load
RSSI
HIPERLAN name and identifier
Heard HIPERLANs
(Note that this list is not exhaustive)

## Slide 13
Local Topology Maintenance
Sending and Receiving Hellos
  Nodes announce their presence with regular “Hello” PDUs
  Mutual existence is derived from sending and receiving Hello PDUs
  Nodes who determine “mutual existence” become Neighbours
Decoding Hellos
  Hello PDUs include information about Neighbours
  Decoding a received Hello PDU gives information about my neighbour’s neighbours
    “Two Hop” topology

## Slide 14
Multiple Radio Hop Network
HIPERLAN extends beyond one radio hop
  Range extended using “forwarder” nodes

## Slide 15
Forwarding
Implementation of forwarding features is optional
Forwarders
  A HIPERLAN may extend over a range greater than one radio hop
  Data may be relayed over multiple radio hops via forwarders
Topology Maintenance
  Topology is maintained over the whole HIPERLAN
  Multipoint relays are forwarding nodes chosen to ensure multicast coverage of 2 hops with the minimum number of transmissions
Routing
  Each node computes the best next hop on the route to the destination
  The use of a routing table is similar to IP routing, but the genreation of the routing table is done automatically by the HIPERLAN protocol

## Slide 16
HIPERLAN and 802.11 MAC Comparison