## Slide 1
HIPERLAN 1: the 23 Mbps Wireless LAN How compatible with IEEE Project 802?
Peter Ransome, pdr@techprt.co.uk The Technology Partnership
Larry Taylor, lt@techprt.co.uk
Tim Phipps, tgcp@symbionics.co.uk Symbionics

## Slide 2
Presentation agenda
Introduction to HIPERLAN, what is it?
The HIPERLAN 1 MAC
The HIPERLAN 1 CAC (Channel Access Control), a possible link between the 802.11 MAC and the HIPERLAN 1 PHY?
The HIPERLAN 1 PHY
Question time

## Slide 3
Introduction
Why Wireless?
What facilities must we have from a WLAN?
What facilities would we like from a WLAN?
What is HIPERLAN?
What does HIPERLAN 1 give us?
Why such a high performance?

## Slide 4
Why Wireless?
Convergence of communications and computing into a single device
Lowest overall network system cost in certain scenarios
Alternative option for certain last drops on wired LAN
Allows untethered working

## Slide 5
What MUST we get from a WLAN?
User data delivery (& close approximation to IEEE 802.x facilities)
Forwarding
Equitable multiple access
Acceptable level of security
Neighbourhood discovery
Usable battery life
Accommodation of the wireless medium issues

## Slide 6
What would we like from a WLAN?
User priority system (for time-bounded services)
Allowability of uncoordinated deployment, and non-centralised operation
Allowability of ambulant usage
Tiny implementation, compatible with PDA/HPC
Support for extreme power-saving nodes
Cheap units!

## Slide 7
What is HIPERLAN? (HIgh PERformance Radio LAN)
Type I: distributed WLAN, 5 GHz (published European Standard: MAC and PHY) ... (the subject of this session)
Type II: W-ATM, 5 GHz, 1999?
Type III: wireless remote access, WLL?, 1999? 5 or17 GHz
Type IV: very high rate wireless infrastructure 155 Mbps ATM, 2000?

## Slide 8
WLAN product introductions
Jan 96
Jan 97
Jan 98
Jan 99
1 Mbps
5
Mbps
25
Mbps
IEEE
802.11
products
100k
bps
Proprietary
ISM
products
HIPERLAN
products
Proprietary
ISM/U-NII
products
Jan 2000?
802.11 HR

## Slide 9
What does HIPERLAN 1 give me? (user perspective)
On-Air Bit Rate 23.5294 Mbit/s
Node Coverage 50 m typical
Built-in Mobility PC type II format, Walking Speed use Europe-wide legality maybe USA too in future?
No Fixed Infrastructure
Overlapping HIPERLANs permitted
  No Frequency Planning, no user license
Connectivity to Wired Networks
  Ethernet, Token Ring, ATM

## Slide 10
HIPERLAN 1 PC-card: Product perspective
Antenna array system:
  prismatic card extension
  broadband HIPERLAN/U-NII
5 GHz RF: SiGe or GaAs front-end
IF: integrated Si
Converters: current technology
Modem: integrated digital state machines
Protocol controller: hardware and microcontroller
PC-card interface

## Slide 11
HIPERLAN: terminal architecture
TX radio
RX radio
Modem
A/D, D/A
CAC
HIPERLAN
Processor
Host
Processor
Application
Protocol Stack
MAC
CAC/PHY
PHY
Sw

## Slide 12
Does HIPERLAN 1 meet WLAN needs?
Service definition based on ISO 15 802-1
Statistical approximation to time-bounded services
“Forwarders”, “Power-savers”, “Power-saver supporters”, Ultra-low duty cycle allowable, lowest power (unequalised receiver) mode for monitoring traffic
Ad-hoc deployment, with centralised operation allowable as merely one special case.
Highly efficient, equitable priority and contention resolution on a per-node basis
PC-card implementation, $120 BOM

## Slide 13
When does HIPERLAN 1 offer these?
Right now!
Functional specification published October 1996, ETSI ETS 300 652
Conformance testing specification (radio & protocol), ETSI ETS 300 836
http://www.etsi.fr
Compliant products expected during 1998

## Slide 14
Why such a high performance?
Delivery at MAC SAP is 19 Mbps, but this is shared between network stations
It’s not just high bit-rate that’s needed, it’s also low latency ...
  ... and low delay variance
... and satisfaction of user requirements raised by
  experience with wired LANs
  “need” for multimedia, colour and movement
the future is broadband
the trend is to decentralised ad-hoc networking

## Slide 15
The HIPERLAN 1 Channel Access Control Sub-layer
Larry Taylor The Technology Partnership
+44 1763 262626
lt@techprt.co.uk

## Slide 16
Reminder : IEEE 802.11 Channel Access
Listen Before Talk protocol
Provides Data Transfer Servic
  2 Control Functions defined (DCF & PCF)
  Acknowledged Unicast, un-Acknowledged Multicast transfers
  Non-preemptive hieracrchical independence
  4 priority levels defined via Inter-Frame Spacing
    SIFS, PIFS, DIFS, EIFS
Secondary transfer functions enumerated for many specific cases
  e.g. Segmentation, Virtual busy, Contention Free etc.
Exponential, slotted backoff after collision

## Slide 17
HIPERLAN CAC Service
Implements MAC facilities over the shared HIPERLAN channel
Priority Access Scheme - EY-NPMA
Hierarchical Independence of Priorities
Contention Resolution within Priority Level
Synchronized & Channel Free accesses
Channel Permission management

## Slide 18
HIPERLAN Channel Access

## Slide 19
HIPERLAN Transfer Service
Global Channel Access Mechanism in 3 phases
  Prioritization
  Contention
  Transmission
Hidden Elimination
Data coded in Low Bitrate & High Bitrate parts

## Slide 20
Contention Resolution
IEEE 802.11 defines an exponentially increasing slotted backoff mechanism
HIPERLAN defines an exponetial probability distribution for the extension stage of the priority assertion signal, followed by a linear probability distribution function for the yield stage. (Designed for 3.5% residual collision rate.)
HIPERLAN contention resolution algorithm is part of the access mechanism

## Slide 21
HIPERLAN Channel Permission Function
HIPERLAN spectrum divided into 5 channels
  5.15 - 5.25 GHz, 3 channels
  5.25 - 5.30 GHz 2 Channels
Higher frequency channels are available at national discretion
Mechanism needed to prevent illegal transmissions
Channel Permission function

## Slide 22
CAC Summary
HIPERLAN CAC Service provides the transfer service to the HIPERLAN MAC
Priority and contention resolution coded into a single active signal
HIPERLAN CAC and 802.11 MAC Transfer Services share much in common
  non-pre-emptive hierarchically independent priorities
  Ack’d unicast and un-Ack’d multicast transmissions
Differs in Contention Resolution approach
  802.11 backoff
  HIPERLAN probabilistic signalling in LBT access mechanism

## Slide 23
The HIPERLAN 1 PHY layer
Peter Ransome
The Technology Partnership
+44 1763 262626
pdr@techprt.co.uk

## Slide 24
Spectrum: USA and Europe
U-NII bands
  5.15 GHz to 5.25 GHz, 50 mW PEP, less than 2.5 mW/MHz, +6dBi ant. gain
  5.25 GHz to 5.35 GHz, 250 mW PEP, less than 12.5 mW/MHz, +6dBi ant gain
  5.725 GHz to 5.825 GHz, 1W PEP, less than 50 mW/MHz, +6dBi ant. gain
HIPERLAN 1 band
  5.15 GHz to 5.25 GHz throughout Europe
  5.25 GHz to 5,3 GHz extensions on national bases
  allowed transmit power, 1W EIRPEP in both bands, HIPERLAN modulation
HIPERLAN 1 in U-NII (from Tx in-band spectrum aspect)?
  1W EIRPEP device is illegal
  100 mW EIRPEP device (class B) legal if rebanded to 5.7 GHz U-NII
  10 mW device legal throughout U-NII

## Slide 25
HIPERLAN channels & modulation
5 channels spaced at 23.5294 MHz
  wide band-edges left to allow simple Tx filtering
Cellular spectrum sharing model does not apply
  HIPERLANs will share spectrum equitably
High-rate and low-rate modulation specified
Single carrier high-rate modulation
  GMSK, BT=0.3
  23.5294 Msymbol/s
  constant envelope: cheaper, more efficient Tx PA
  allows equalisation as if a linear scheme

## Slide 26
Low-bit-rate modulation
the initial content of all HIPERLAN 1 bursts
MSK at 1/16 of full data rate
transmitted at full power (hence higher spectral density than for high-rate modulation)
allows power saving in the receiver
  carries length and destination address information
  can be received without equalization

## Slide 27
High bit-rate reception problems
Equalization of high rate signalling
  antenna diversity and directivity is possible at 5.2 GHz in PC-card format
  HIPERLAN provides a long training sequence
  antenna selection can be performed during training
  designer can balance speed of training, antenna complexity, equalizer
Battery life
  low bit-rate header provides information without receiver equalization
  power-saving modes are supported
  transmit power is reasonable for a usable coverage range
  constant envelope transmit modulation means less backoff in transmitter
Channel stability
  HIPERLAN 1 burst duration is limited
  for ambulant motion, the channel can be considered as stable
  symbol clock is tightly constrained to RF carrier
  hence receivers need only track the carrier, and not retrain during bursts

## Slide 28
Co-existence with IEEE 802.11 HR?
Co-existence raises the possibility of hybrid WLANs
U-NII band includes HIPERLAN 1 band
targeted products and users for 802.11 and HIPERLAN 1 align BUT
HIPERLAN 1 Tx power level is above U-NII limits for some devices, though class A (10 mW) is legal
HIPERLAN 1 band occupancy protocol is known U-NII sharing rules not yet settled?

## Slide 29
Interoperability with IEEE 802.11 HR?
would provide “world-” products
HIPERLAN 1 standard is complete and available in USA
HIPERLAN 1 MAC services align to IEEE/ISO BUT
Certain 802.11 MAC services are unavailable in HIPERLAN 1, and vice versa

## Slide 30
HIPERLAN 1 PHY derivative usable as IEEE 802.11 HR?
HIPERLAN 1 fits data rate goal of 802.11 HR
U-NII band includes HIPERLAN 1 band
HIPERLAN 1 MAC services are comprehensive BUT ???
this is a topic for discussion in 802.11 PHY group meeting Montreal, 11/11/97
  (the eleventh hour?, actually the afternoon session)

## Slide 31
Question time

## Slide 32
Time for the bar