## Slide 1
Proposed 802.11 High Rate PHY Technique
Harris High Rate data modulation
Notes: This paper discusses an approach for extending the 802.11 standard to accommodate high rates of 10 Mbps or better. Harris Semiconductor has a technique that it offers to the 802.11 as suitable for inclusion into the standard. Harris has implemented this technique in an integrated circuit and has performed tests on the first silicon which are reported here. The first samples of this device will be available for distribution late this year.

## Slide 2
Suggested Technical Approach
Utilize MOK/PSK modulation techniques to realize 4 to 8 bits/symbol
Use existing preamble and header to insure interoperability.
Increase symbol rate to 1.375 MSps (8 chip symbols) and hold existing spread rate
Use existing 802.11 DS parts for the RF & IF circuits
Notes: The high rate scheme chosen will not impact the design of the RF and IF parts currently employed. This means a small redesign effort and the ability to drop in a new baseband processor into the existing radios to get the higher rates.
One issue to be addressed in the modem design is the switch to a different symbol rate once into the PDU. Since the spread rate is unchanged, this was not difficult.
The new scheme uses an absolute phase reference. The PLCP preamble is BPSK and as such, will provide a 180 degree phase ambiguity. By using the last bit out of the modulator prior to the PDU as a phase reference, we establish an absolute phase reference.

## Slide 3
11 Bit Barker Word
56
59
65
6A
03
0C
30
3f
3-ary modified Walsh Functions
22 MHz
11 MBps
QMBOK
5.5 Mbps
BMBOK
802.11 DSSS QPSK
2MBps
Barker
QPSK
802.11 DSSS BPSK
1 MBps Barker
BPSK
11 chips
1 MSps
1 bit encoded to
2 code words
11 chips
1 MSps
2 bits encoded to
4 code words
8 chips
1.375 MSps
4 bits encoded to
16 code words
8 bits encoded to
2x16 code words
8 chips
1.375 MSps
I
Q
I,Q
I
Q
I,Q
Modulation Scheme
Notes: The Harris suggested high rate modulation is a form of M-ary Bi-Orthogonal keying. We propose that both Binary and Quadrature forms of this modulation be used to provide multiple rates for stressed links.

## Slide 4
Harris High Rate 802.11 Features
Harris approach allows a total raw system throughput of 33 MBps in the band versus 20 MBps for 32 MCps MSK and 6 for the existing 802.11 2 MBps
Less interference with FH and DS by using less bandwidth and shorter packets
Less complexity; can work without equalizer or channel estimator (but can use them for more greater delay spread since it has enough preamble)
Notes: The Harris high rate waveform allows up to 33 Mbps total throughput in the ISM band in (3) 11 Mbps channels. A wideband system would have fewer channels and therefore less overall throughput.
Since the waveform has the same spectrum properties as the existing DS waveform, its interference to FH systems gets less because of shorter time on the air.
The minimal increase in complexity of the high rate system does not alter the size of the hardware, so it will fit into a PCMCIA package. The proposed waveform can work with either short or long preambles. The long preambles currently implemented allows backwards compatibility and time for antenna diversity and for equalizers or channels estimators to initialize.
The new methods shown are benign in that they do not increase the current occupied bandwidth. Up to 5.5 times higher data rates are achieved.
The mechanism for rate switching has already been incorporated and the new rates fit with the definitions already established
The waveform has the same AM component as the current waveform, and requires only 5 dB of power amplifier backoff to achieve its spectral mask. PPM waveforms require more backoff.
The MAC protocol is unaffected by this technique.

## Slide 5
More Features
Less power amplifier backoff than PPM
Less bandwidth than 16 chips per symbol
Simple implementation
No MAC changes

## Slide 6
4x
3x
2x
1x
802.11 11Mbps 11Mbps 11Mbps
1-2Mbps No Eq. Eq 100nsec Eq 200nsec
Implementation Penalty Vs (Multipath)Delay Spread Mitigation
Implementation
Penalty
Notes: This waveform can work without the need for a channel estimator or equalizer for those channels such as office buildings and homes where the delay spread is small. This makes for the lowest cost implementation.
Where improved performance or longer delay spread is needed, a simple channel estimator and cross sub channel interference suppressor can be added with a nominal increase in baseband processing cost.
When robust performance is needed, a complex channel corrector capability can be added without changing the basic radiated waveform or preamble.
The benefits of a good high rate waveform are an increased longevity in the marketplace and no obsolescence of the early entries. By making the units interoperable, they can be introduced seamlessly into the market. Keeping the channel distortion correction in the receiver allows the system designer to choose only the degree of performance needed for the job.
.

## Slide 7
Performance
Has proven -85 dBm sensitivity for 2% PER
Will pass FCC CW jamming test with margin
  FCC allows SNR to be defined as Es/N0
  Measured 2 dB of margin on CW jammer test
Range demonstrated to over 100 ft
Notes: The performance of the new waveform for higher rates has been modeled and simulated. The theoretical performance of MOK is well known and covered in general texts. Typically, it is somewhat better than BPSK since it has coding properties built into the waveform and sends code symbols rather than bits. Since the modulation carries 11 times as many bits as the 1 MBps case, it requires about 9 dB more Es/N0 than BPSK. The measured performance in a typical radio implementation has shown about -85 dBm sensitivity for 2% PER.
One primary concern is passing the FCC requirements on processing gain. We have queried the FCC about this waveform and have gotten an approval providing the waveform passes the CW jamming test. We also got the interpretation that the SNR in the test can be considered Es/N0.
Our simulations and tests show that it will pass the test under these interpretations.

## Slide 8
Range Testing
Harris has implemented the technique in an integrated circuit and demonstrated that in a typical radio design.
Since a suitable MAC is not available we tested the radio with a substitute controller that allows BER and PER testing in the actual environment and the lab.
We tested the PER performance in our facility in Palm Bay.

## Slide 9
The floor plan of the test area

## Slide 10
Pictures of test area

## Slide 11
Pictures of test area

## Slide 12
Pictures of test area

## Slide 13
Pictures of test area

## Slide 14
Range testing
These tests show achieved transmission rates for 512 byte packets
and are all in the 50-100 ft range.. No/Yes refers to rotation of the radio.

## Slide 15
Pick One
of 8 Walsh
Functions
MUX
1:8
3
3
DATA
IN
I OUT
Q OUT
1.375 MHz
11 MHz
1
1
Data Rate = 8 bits/symbol * 1.375 MSps = 11 MBps
Pick One
of 8 Walsh
Functions
Scrambler
1
1
MOK Modulation Approach for 11 MBps
Notes: This slide shows how to form our suggested modulation type. M-ary orthogonal keying has been known for many decades, and indeed, can be shown to be a generalization of many standard waveforms such as FSK. In this scheme, the spread function is picked from a set of M orthogonal vectors by the data word. Since the I and Q channels can be considered independent when coherently processed, both can be modulated this way. That allows us to pack 8 bits into each symbol. The most well known orthogonal vector set is the Walsh function set. It is available for 8 and 16 chip vectors and has true orthogonality.
To make the modulation have the same bandwidth as the existing 802.11 DS modulation, the symbol rate is increased to 1.375 MSps while the spread rate is kept at 11 MCps. This makes the overall bit rate 11 MBps.

## Slide 16
MOK properties
This modulation is the most power efficient available
The spectrum is like 802.11 DSSS
Multipath performance is nominal for the SNR
Requires a cover sequence to avoid the Wal0 CW modulation (modified Walsh Functions)
Requires coherent processing
Moderate implementation complexity (~25% extra baseband processing circuitry)
Notes: MOK modulation has been shown to have slightly better Eb/N0 performance than BPSK due to embedded coding properties. This makes the waveform the most power efficient of the many candidates. This allows the modulation to tolerate more interference than other waveforms. Since there are more bits per symbol with this modulation, it naturally requires more Es/N0 than BPSK, but the increase is minimized.
The spectrum of this waveform is sinx/x, which is the same as the 802.11 waveform now, but without some of the little blips that the 11 bit sequence causes.
The multipath performance will depend on the Eb/N0 and phase distortion tolerance of the waveform. We have shown through simulation, that this signal will have an adequate performance in the indoor environment. It is obviously worse than the 1 MBps case which can tolerate an SNR of 0 dB.
The Walsh function set includes one member that is all 0s. This is undesirable, but easily fixed by covering the sequence with another sequence which will not destroy the orthogonality.
To use both I and Q channels independently requires that the system process the signal coherently with an absolute phase knowledge. This is not a large concern as the PLCP preamble and header can supply the necessary means to lock up a PLL in a given state. This and the parallel correlators for the demodulation moderately increase the complexity of the demodulator.

## Slide 17
MUX
1:4
3
DATA
IN
I,Q OUT
1.375 MHz
11 MHz
1
Data Rate = 4 bits/symbol * 1.375 MSps = 5.5 MBps
Pick One
of 8 Walsh
Functions
Scrambler
1
MOK Modulation Approach for 5.5 MBps
Notes: Operating the basic MOK receiver with only the I channel modulated gives half the base rate and makes for a more rugged system. In this mode, the Q channel is turned off and the I channel supplied to both the I and Q channel modulator ports.
The receiver demodulator can use a limiter since the desired signal dominates in the IF bandwidth. This makes it simpler to implement than an AGCd design.

## Slide 18
5.5 MBps properties
The 5.5 MBps mode uses BPSK modulation which is more rugged than QPSK due to absence of I/Q cross sub channel interference
Stations can easily fall back to this mode when stressed, then 1 MBps if really stressed.
Notes: The BPSK MOK mode has twice the phase tolerance and is therefore more rugged with respect to phase disturbances due to channel distortion due multipath. It is also 3 dB more sensitive.
Since multipath is one of the greatest limitations to range and effects QPSK much more than BPSK, this mode is expected to operate almost as good as the QPSK 2 MBps mode.
In an 802.11 network, this provides a good intermediate fallback rate for stressed links. The network access point can negotiate for the best rate supportable with each station. Having rates of 1, 2, 5.5, and 11 MBps, allows a large variation to account for gap filling and other network necessities.

## Slide 19
HFA 3860 BER performance
Notes: The expected performance of the MBOK technique can be derived from various texts and shows an improvement over PSK of about 1.6 dB. The achieved performance for a low cost implementation has about 3 dB or less of implementation loss.

## Slide 20
HFA 3860 PER performance
Notes: The packet error rates generally follow the bit error rate curves adjusted for the number of bits. Deviations are due to demodulator performance. Generally, the SNR of the 1 Mbps preamble and header is so high that the acquisition is usually perfect.
The curves show the theory for 1 bit and for 1, 100, and 1000 symbols. The measured performance shows the data for 100 and 1000 symbols.

## Slide 21
BER versus Clock Offset Performance
Notes: The performance of the Harris implementation is based on the performance of the symbol tracking loops. Our implementation has better tracking on the new high rate modes than the 802.11 modes. This is due to using 1/8th chip tracking on the high rate modulation and 1/4th chip tracking on the lower rate modulations.

## Slide 22
BER versus Carrier Offset Performance
Notes: The PER curves show that the acquisition performance is adequate out to 1.5 times the maximum offset allowed. Once you get out to +100 PPM, the performance degrades substantially. This is because the carrier phase roll gets close to 90 degrees per symbol of the header. Exceeding 90 degrees per symbol makes the phase shift ambiguous and the modem may lock up on a sidelobe.

## Slide 23
Processing Gain test results
Notes: This slide shows the CW jammer test run at IF over a few points to verify that our analysis was correct. The results follow the analysis reasonable well and show that the technique will pass the FCC's tests for CW jamming. We also scanned a fixed level CW signal at 12 dB PG. over the whole band and found no frequencies where the modem was especially susceptible to CW jamming. This result indicates that the full radio should have no problem in passing the FCC's test for PG.
The full radio test is on going as we speak.

## Slide 24
Propagation Simulations without Diversity
Notes: Simulations results show probability of a missed packet with
100 trials per point
Packet length 200 symbols
3 bit A/D , carrier and chip loops active
3 pole Butterworth SAW
Single antenna, no diversity

## Slide 25
Propagation Simulations with Optimal Diversity
Notes: Simulations results show probability of a missed packet
100 trials per point
Packet length 200 symbols
3 bit A/D , carrier and chip loops active
3 pole Butterworth SAW
Dual antennas, completely independent samples, best antenna chosen (an ideal case)

## Slide 26
Frequency disturbance tolerance
FM deviation at 1kHz to cause modem to break lock
  1 Mbps >400kHz
  5.5 Mbps 48 kHz
  11 Mbps 25 kHz
FM deviation at 1kHz to cause 10-5 BER
  1 Mbps >400kHz
  5.5 Mbps 48 kHz
  11 Mbps 25 kHz
FM deviation at 1kHz to cause packet errors
  1 Mbps >400kHz
  5.5 Mbps 40 kHz
  11 Mbps 20 kHz
Notes: The ability of the modem to achieve given performance in the face of frequency dynamics which might relate to motion was tested by FM modulating one of the local oscillators of the radio. The performance indicates that the modulation can be tracked through fairly large disturbances and

## Slide 27
Like signal jamming
The ability of the modulation to tolerate other networks in the area was tested. The results for S/J that causes 5% PER are:
Notes: The ability of the signal to take jamming by a like signal will impact the ability to collocate nets. This set of data shows how the system will tolerate other DS signals of the various rates.
From the data we can see that the 1 Mbps radio is little effected by the higher rates since they are non correlating. On the other hand, the 1 Mbps radio jams the preamble of all the higher rates better than any other.

## Slide 28
The possibilities
low cost with no post processing
better with simple cross channel estimator and corrector
very good performance with lots of processing
all the above with the same waveform

## Slide 29
Interoperability
If the committee decides to ignore compatibility, short headers can be used.
Antenna diversity and equalization need a somewhat longer header than the shortest possible for maximum throughput.

## Slide 30
Variations
Additional research is underway on variations to the chosen sequences for better multipath performance.
If the 8 chips per symbol is a problem, higher numbers of chips per symbol are possible at some compromise in the data rate or spread rate.