## Slide 1
IEEE 802.11 Wireless Access Method and Physical Specification
Title: Summary of DS/GFSK High Speed 2.4 GHz PHY
Date: November 10, 1997
Author: Dean Kawaguchi
Symbol Technologies, Inc.
2145 Hamilton Ave
San Jose, CA. 95125
Telephone: (408)369-2629
FAX: (408)369-2737
email: DeanK@psd.symbol.com

## Slide 2
Review of DS/GFSK Proposal
DS/GFSK addresses key requirements
  Interoperability with both FH and DS
    Hopping and non hopping modes, hopping based on FH PHY sequences
  Interference immunity in ISM band
    GFSK is most bandwidth efficient of binary modulations (1.1 * chip rate)
    Hopping over 8 channels in 5 Mbps mode, 4 in 10 Mbps mode
  Multipath robustness
    Good capture effect of FSK + DS spreading
  Good sensitivity performance
    5 Mbps mode same as 1 Mbps FH, 10 Mbps 3 dB worse
  Low speed preamble for interoperability, high speed for throughput
    Both possible with fast acquisition of GFSK
  Low cost and need for architectural options
    Constant amplitude, more efficient power amplifier

## Slide 3
High Speed PHY Proposal
A succinct summary of the proposed high speed DS PHY is as follows:
  DS spreading: 4 bits/symbol and 8 chips/symbol bi-orthogonal Walsh codes
  Modulation: Binary GFSK with deviation h=0.7; 1.5 dB preemphasis
  Data rates: 1.25 Msym/sec (5 Mbps) and 2.5 Msym/sec (10 Mbps)
  Chipping rates: 10 Mcps and 20 Mcps
  Bandwidths: 11 MHz and 22 MHz
  Channelization: 8 channels w/10 MHz spacing, 4 channels with 20 MHz spacing

## Slide 4
DS Spreading Format
The DS spreading formats used by Harris and Micrilor uses simple yet effective bi-orthogonal Walsh codes
The 8 chips per symbol used by Harris is more bandwidth efficient which is crucial to satisfy the interference fighting channelization mentioned earlier
The 4 bits/8 chips per symbol used at 1.25 (or 1.375) Msps and at 2.5 Msps would produce 5 and 10 Mbps at a chipping rate 10 and 20 Mcps

## Slide 5
Hopping and interoperability with 1&2 Mbps FH PHY
The hopping can be synchronized to interoperate with the 1 and 2 Mbps FH PHY

## Slide 6
Interoperability with FH PHY
Interoperability preamble using FH 1 Mbps with rate switch sync period
HS preamble mode for max throughput and operation in HS capable units only environments
  HS preamble is ­16 µs including time for diversity selection
In either mode, CCA on all 1 MHz channels in wideband channel possible at reduced sensitivity
Full sensitivity on 1 MHz channel associated on with digital implementations

## Slide 7
Low cost, many architectural options
An FSK system has been the lowest cost due to the simplicity, inherent robustness, and use of nonlinear components.
There are many options and design optimizations which will allow manufacturers to optimize for various applications and price/performance tradeoffs.
Digital implementation with parallel demod, subband tuning for 1 MHz channel requires only additional gates in ASIC
1 MHz SAW for full selectivity performance 1/2 Mbps only mode, tune synthesizer to channel
Existing DS RF and IF chip sets may also be used
Intellectual property - Walsh codes and binary GFSK on wireless is probably not patentable any more.