## Slide 1
1
Further Considerations for Implementation of Adaptive Data Rates
by D. Hurne and D. Draper
Golden Bridge Technology
Notes: 1
1

## Slide 2
2
Goals for next generation of WLANs
Higher speed
Compatibility with existing systems
Universal applicability to variety of platforms
Notes: 2
2

## Slide 3
3
Higher speed
Operate in ISM band
Channel data rate of up to 20 Mbps
Direct sequence spread spectrum operation compliant to FCC rules
Notes: 3
3

## Slide 4
4
Compatibility with existing systems
Minimal modification to existing protocol software implementation
Seamless operation in a mixed environment, i.e., present IEEE 802.11 and new high speed version
Notes: 4
4

## Slide 5
5
Universal applicability to variety of platforms
Low power consumption
Low cost
Trade-off between cost/power consumption/data rate
Notes: 5
5

## Slide 6
6
Current IEEE802.11 system
Physical Layer
  Current system uses 11 chip Barker code as spreading code
  Each data bit spread by entire code sequence
  (RF) Modulation is BPSK or QPSK
  Data rate varied by changing modulation method
  Chip rate is 11 Mcps
  RF bandwidth is 22 MHz
Packet Structure
  Well defined fields (sync, set-up, data, etc)
  CRC protection of select fields
Notes: 6
6

## Slide 7
7
Proposed system description
Spreading sequence
Stacked carrier principle
Transmitter block diagram
Increased data rate method
Data rates
Variable data rate method
RF signal bandwidth
RF and despread signal constellation
Coexistence and interoperability
Interoperability scenario
System complexity
Notes: 7
7

## Slide 8
8
Spreading sequence
IEEE 802.11 spreading code is the 11 bit Barker Code:
  +1 -1 +1 +1 -1 +1 +1 +1 -1 -1 -1
The augmented Barker code appends a ‘-1’ chip at the end
+1 -1 +1 +1 -1 +1 +1 +1 -1 -1 -1 -1
The augmented Barker code set uses all phases of the original Barker code and appends a ‘-1’ chip at the end
  Code 1: +1 -1 +1 +1 -1 +1 +1 +1 -1 -1 -1 -1
  Code 2: -1 +1 +1 -1 +1 +1 +1 -1 -1 -1 +1 -1
  ...
  Code 11: -1+1 -1 +1 +1 -1 +1 +1 +1 -1 -1 -1
Augmented Barker codes form orthogonal set
Notes: 8
8

## Slide 9
9
Stacked carrier principle
Use each member of orthogonal code set to spread spectrum modulate individual data bits
Add spread spectrum signals
Transmit composite signal
Notes: 9
9

## Slide 10
10
Transmitter block diagram
DATA
DEMUX
AUGMENTED BARKER
GENERATOR; CODE #11
AUGMENTED BARKER
GENERATOR; CODE #2
AUGMENTED BARKER
GENERATOR; CODE #1
SUM
DATA
DEMUX
AUGMENTED BARKER
GENERATOR; CODE #11
AUGMENTED BARKER
GENERATOR; CODE #2
AUGMENTED BARKER
GENERATOR; CODE #1
SUM
DATA
DEMUX
DATA IN
I - DATA OUT
Q - DATA OUT
New high data rate system packet (except MPDU) or present IEEE 802.11 same as present systems.
Transmitter block diagram for new high data rate system MPDU is illustrated below
COVER
CODE
COVER
CODE
COVER
CODE
COVER
CODE
COVER
CODE
COVER
CODE
Notes: 10
10

## Slide 11
11
Increased data rate method
Transmitted data rate increases as number of orthogonal codes used increases (one data bit per code)
Implementations can use 1 to 11 Augmented Barker Codes
Individual data bits can be recovered due to the orthogonal nature of the spreading code set
Cover Code has same clock as Augmented Barker Code
Cover Code is 4095 bits long
Notes: 11
11

## Slide 12
12
Data rates
Chip rate: 11 Mcps
Processing gain:
  IEEE 802.11 Mode: 11
  Proposed new method:
    All except frame body and CRC32: 11
    Frame body and CRC32: 12
Data rates:
  IEEE 802.11 Mode: 1 Mbps (BPSK), 2 Mbps (QPSK)
  Proposed new method: 1.83, 3.67, up to 20.16 Mbps in increments of 1.83 Mbps
Notes: 12
12

## Slide 13
13
Variable data rate method
Proposed new method
  System can use 1 code, 2 codes, … , 11 codes
  Chip rate (Mcps) - 11
  PG (augmented Barker code) - 12
  Data rate (Mbps, BPSK modulation, per code) - 11/12
  Data rate (Mbps , QPSK modulation , per code) - 11/6
  Min data rate (Mbps , QPSK modulation , 1 code - 11/6
  Max data rate (Mbps , QPSK modulation , 11 codes - 20 1/6
IEEE 802.11 compatible method
  Same as BPSK, QPSK modulation using one code. Code is Barker code, data rate is 1 and 2 Mbps and PG = 11
Notes: 13
13

## Slide 14
14
RF signal bandwidth
Chip rate is constant and identical to the present IEEE 802.11 standard (11 Mcps).
RF bandwidth requirements remain identical to present IEEE 802.11 standard based systems
Notes: 14
14

## Slide 15
15
RF and despread signal constellation
RF signal constellation (number of points)
  1 code (11/6 Mbps) - 4
  2 codes (11/3 Mbps) - 9
  …
  11 codes (20 1/6 Mbps) - 144
Outer constellation points are low probability; RF can be in soft compression
Despread signal constellation always QPSK
Notes: 15
15

## Slide 16
16
Coexistence and interoperability
Proposed high data rate system can fully coexist and interoperate with legacy systems, subject to new higher data rates limitations
Notes: 16
16

## Slide 17
17
Interoperability scenario
All systems acquire same spread spectrum SYNC preamble
All systems detect the same SFD field
All systems demodulate the same SIGNAL field - this field indicates the data format of the MPDU field. It can indicate:
  IEEE802.11 (1 or 2 Mbps)
  Proposed new data rate (one of 11 data rates)
All systems demodulate the same SERVICE field
All systems demodulate the same LENGTH field
All systems demodulate the same CRC16 field
New systems can then demodulate MPDU at enhanced data rates or at present IEEE 802.11 data rates
Notes: 17
17

## Slide 18
18
System complexity
System complexity increase is small due to utilization of matched filter based technology to implement the following functions:
  Spread spectrum acquisition
  Signal despreading
  BPSK / QPSK demodulation
  RF tracking (± 25 PPM)
  Chip tracking (DLL)
  Diversity processing (selection or Rake with MR combining)
  Clear channel assessment (CCA) using energy detection at IF and post despreading.
Notes: 18
18

## Slide 19
19
System performance
System performance - multipath
System performance - RF tracking
Sensitivity to AGC setting (1)
Sensitivity to AGC setting (2)
Notes: 19
19

## Slide 20
20
System performance - multipath
Robust performance due to matched filter based technology.
Multipath resistance for several data rates, 100 byte packet, FER=10e-1, no diversity processing (RAKE)
Notes: 20
20

## Slide 21
21
System performance - RF tracking
Digital Costas loop removes frequency offsets of ± 25 PPM.
SNR (dB) required for several data rates to achieve FER=10e-1 for 100 byte packet. Frequency offsets of 0 and 125 KHz are considered.
Notes: 21
21

## Slide 22
22
Sensitivity to AGC setting (1)
BER vs AGC setting for 8, 10, 12 dB. Data rate of 1.83 Mbps at a frequency offset of 0 KHz (left) and 80 KHz (right).
Notes: 22
22

## Slide 23
23
Sensitivity to AGC setting (2)
BER vs AGC setting for 8, 10, 12 dB. Data rate of 12.83 Mbps at a frequency offset of 0 KHz (left) and 80 KHz (right).
Notes: 23
23

## Slide 24
24
Conclusions
Proposed system outlines a flexible signal structure that can be efficiently processed by high performance matched filter based architectures.
Interoperable with existing systems and capable of trading off cost, power consumption and data rate (11 rates, 1.83 to 20 Mbps plus present 1 and 2 Mbps) while maintaining full interoperability.
A full range of existing systems, from smallest ( and most restricted in power consumption) to largest can communicate using new IEEE Wireless LAN protocol.
Matched filter based operation can take advantage of multipath to enhance system performance at little or no additional hardware complexity.
Direct sequence spread spectrum signal structure complies with FCC ISM band definition.
Notes: 24
24