## Slide 1
L-Pulse Position Modulation (L-PPM) Proposal for 5 GHz High-Speed PHY submitted to IEEE 802.11 by Reza Ahy RadioLAN, Inc.

## Slide 2
Outline
5 GHz High-Speed PHY Goals
L-PPM Characteristics
L-PPM Symbol Detection Errors
Indoor Communication Channel
L-PPM over Multipath, Dispersive Channel
20 Mbps L-PPM Issues
FCC & L-PPM
L-PPM Product Feasibility
Conclusions

## Slide 3
5 GHz High-Speed PHY Goals
20 Mbps nominal rate
10 Mbps fall-back rate
Robustness against multipath
Low-Cost
Low-Power
Maximize System Capacity

## Slide 4
L-PPM Characteristics
Power-efficient RF transmission
Simple Transmiters (compared to OFDM, QPSK & others)
Power-efficient DC
AWGN moderate bandwidth efficiency
Multipath-channel good bandwidth efficiency
Low hardware complexity
Low cost
Chip
Slot
Block
Symbol XXXX

## Slide 5
L-PPM Symbol Detection Errors
Multipath-induced ISI error
Erasure error
False-alarm error
Wrong-slot error

## Slide 6
Indoor Communication Channel
Multipath (Rayleigh envelope)
Dispersive (Delay spread)
Frequency selelctive Fading
Time-varying

## Slide 7
L-PPM over Multipath, Dispersive Channel
Challenges
  ISI
  ICI
  Multipath distortion
  Multipath Fading
Possibilities
  Systems approach
  Distributed signal conditioning & processing of the signal
  10 Mbps systems feasible with very simple solutions

## Slide 8
20 Mbps L-PPM Issues
Higher-order L-PPM candidates (16-PPM)
Feasibility is NOT the question: Low-cost implmentation is.
Sub-optimal simple receivers are OK
Maximum-likelihood Estimation (MLSE) Recivers could be too complex
Chip & Frame Synchronization

## Slide 9
FCC & L-PPM
L-PPM efficient power transmission is a plus.
L-PPM for ISM bands
  RadioLAN 10 Mbps, 5.8 GHz FCC-approved products
    Desktop solutions: December 1996.
    Laptop solutions: July 1997.
L-PPM for U-NII bands
    FCC-approved RadioLAN U-NII product: May 1997.

## Slide 10
L-PPM Product Feasibility
RadioLAN Products: 10 Mbps
Irda Products: 4 Mbps
IEEE 802.11 IR-based products

## Slide 11
Conclusions
L-PPM meets the modulation method criteria of
  20 Mbps
  Multipath-robust,
  Low-cost
  Low-power
  Power efficient
L-PPM Radio LANs have been demonstrated as 10 Mbps products.
L-PPM low-cost IR LANs have been demonstrated as 4 & 16 Mbps products.
L-PPM could potentially co-exist with IEEE 802.11 low-speed.