## Slide 1
Proposal for 5-GHz PHY
John H. Cafarella
MICRILOR, Inc.

## Slide 2
Key Features
Wide Transmission Bandwidth
Low EB/N0
16 Chips/
Symbol
Changing
PN Codes
Noncoherent 4 x 4-ary BiOrthogonal Signaling
24-/18-Mbps Data Rate
“Good”
PN Codes
Power-Efficient Transmission
Intra-Symbol Multipath Tolerance
(Transmission Security)
Code Channelization
Inter-Symbol Multipath Tolerance
MSK Spreading Modulation
Saturated Power Amplifier
Spectral Confinement
Frequency Channelization
enabling
link
design
system
Minimal Acquisition Time
Low Preamble Overhead
Robust Links
Overlapped BSAs
High Throughput
12-dB Processing Gain
Low Battery Drain
Multipath Resolution

## Slide 3
Robust Links
Wide Transmission Bandwidth
16 Chips/
Symbol
Changing
PN Codes
“Good”
PN Codes
Intra-Symbol Multipath Tolerance
Inter-Symbol Multipath Tolerance
Robust Links
12-dB Processing Gain
Multipath Resolution
BSSTspread=
Resolving paths gives more independent trials
Reduced strength per path, but
Low probability that all fade
D11-97/119 demonstrates for diffuse Rayleigh
Even better with specular multipath

## Slide 4
Robust Links
Wide Transmission Bandwidth
16 Chips/
Symbol
Changing
PN Codes
“Good”
PN Codes
Intra-Symbol Multipath Tolerance
Inter-Symbol Multipath Tolerance
Robust Links
12-dB Processing Gain
Multipath Resolution
Functional processing gain (PG) of 12 dB
Probably required as the UNII band fills up

## Slide 5
Robust Links
Wide Transmission Bandwidth
16 Chips/
Symbol
Changing
PN Codes
“Good”
PN Codes
Intra-Symbol Multipath Tolerance
Inter-Symbol Multipath Tolerance
Robust Links
12-dB Processing Gain
Multipath Resolution
Test with specular multipath, without noise
  must consider crosscorrelation side lobes
D11-97/117 documents preferred 16-bit codes
  best 8 of 2048 cosets
Must analyze self-interference with sum of four
correlator outputs
correct channel
another channel

## Slide 6
Robust Links
Wide Transmission Bandwidth
16 Chips/
Symbol
Changing
PN Codes
“Good”
PN Codes
Intra-Symbol Multipath Tolerance
Inter-Symbol Multipath Tolerance
Robust Links
12-dB Processing Gain
Multipath Resolution
Repeated spreading code correlates with far-out multipath
  strong intersymbol interference (ISI)
Use 4 cosets cyclically
  no correlated ISI for four symbols
Could use 8 cosets, but
  not really needed
  better to have 2 groups of 4 codes for spatial re-use
symbol
Extended multipath

## Slide 7
High Throughput
Noncoherent 4 x 4-ary BiOrthogonal Signaling
Minimal Acquisition Time
Low Preamble Overhead
High Throughput
“Good” PN Codes
16 Walsh Functions
Baseband Tx Signal
1-bit DPSK
2-bits
PN code
Walsh correlator
Baseband Rx I Signal
Baseband Rx Q Signal
Largest of 4 Magnitudes
Largest of 4 Magnitudes
Largest of 4 Magnitudes
Largest of 4 Magnitudes
2-bits
compare with previous
1-bit DPSK
power-efficient implementation of 16 complex correlators
2-bits
2-bits
2-bits
1-bit DPSK
1-bit DPSK
1-bit DPSK
compare with previous
compare with previous
compare with previous
2-bits
2-bits
2-bits
1-bit DPSK
1-bit DPSK
1-bit DPSK
S
x
12 bits/symbol with 6-dB peak/average envelope
24-/18-Mbps Data Rate
Walsh correlator

## Slide 8
High Throughput
Noncoherent 4 x 4-ary BiOrthogonal Signaling
Minimal Acquisition Time
Low Preamble Overhead
High Throughput
“Good” PN Codes
16 Walsh Functions
Baseband Tx Signal
1-bit DPSK
2-bits
PN code
Walsh correlator
Baseband Rx I Signal
Baseband Rx Q Signal
Largest of 4 Magnitudes
Largest of 4 Magnitudes
Largest of 4 Magnitudes
Largest of 4 Magnitudes
2-bits
compare with previous
1-bit DPSK
power-efficient implementation of 16 complex correlators
2-bits
2-bits
1-bit DPSK
1-bit DPSK
compare with previous
compare with previous
compare with previous
2-bits
2-bits
1-bit DPSK
1-bit DPSK
S
x
9 bits/symbol constrains the modulator to constant envelope!
consistency check ?
24-/18-Mbps Data Rate
Walsh correlator

## Slide 9
Examples of Tx Waveforms

## Slide 10
High Throughput
Noncoherent 16-ary BiOrthogonal Signaling
Minimal Acquisition Time
Low Preamble Overhead
High Throughput
“Good” PN Codes
Noncoherent: no PLL, no settling time
Good PN codes: no equalizer, no adaptation time
DPSK on SFD & SIGNAL: no CRC required
SFD
SIGNAL
SYNC
LENGTH
PHY header ~20 ms
DPSK only
AGC | Search | Select largest path | wait
24 Mbps
18 Mbps
10 Mbps
24-/18-Mbps Data Rate

## Slide 11
Power Efficiency
Low EB/N0
Noncoherent 16-ary BiOrthogonal Signaling
Power-Efficient Transmission
MSK Spreading Modulation
Saturated Power Amplifier
Low Battery Drain
Exploits bandwidth for robustness
9.3 to 10.5 dB EB/N0 for 10-6 PSE
Similar in efficiency t0 DPSK
PSE~10-6
Shannon limit

## Slide 12
Power Efficiency
Low EB/N0
Noncoherent 16-ary BiOrthogonal Signaling
Power-Efficient Transmission
MSK Spreading Modulation
Saturated Power Amplifier
Low Battery Drain
MSK allows operation into power-amp saturation
  constrained-amplitude mode only
  9 bits/symbol
  but 6-dB greater average power
PA efficiency greatly improves
D11-97/118 describes generation and performance
9 bit/symbol operating point
12 bit/symbol operating point

## Slide 13
Channelization and Coexistence
“Good”
PN Codes
Code Channelization
MSK Spreading Modulation
Spectral Confinement
Frequency Channelization
Overlapped BSAs
MSK1 (or MSK shaping) enhances channelization
32-Mchip/s
  two wideband2 per 100-MHz
options if 16-Mchip/s
  a wideband and two narrowband3 per 100-MHz
  four narrowband per 100-MHz
108 to 144 Mbps capacity in 6 to 12 frequency channels
1 D11-97/118 describes MSK generation
2 wideband = 24 or 18 Mbps
3 narrowband = 12 or 9 Mbps
- 40 dB
- 40 dB
- 40 dB
0 dB
0 dB
0 dB

## Slide 14
Channelization and Coexistence
“Good”
PN Codes
Code Channelization
MSK Spreading Modulation
Spectral Confinement
Frequency Channelization
Overlapped BSAs
Selected best 8 codes (of 2048) for demodulating data in multipath
Selected best 8 codes for preamble search (and acquisition) in multipath
Mutual rejection much better than “random” implied by processing gain
Many strategies for code assignment
  unique pairing of data/search codes gives 8 code channels
  arbitrary pairing of data/search codes gives 64 code channels
  intra-frame code changing greatly expands the possibilities
Can be combined with six to twelve frequency channels
D11-97/117 describes data codes

## Slide 15
Summary of Possible Data Modes
16-ary BiOrthogonal
4 x 4-ary BiOrthogonal
16-ary BiOrthogonal
10 Mbps
18 Mbps
24 Mbps
5 Mbps
9 Mbps
12 Mbps
2
-92 dBm
-86 dBm4
-86 dBm
-95 dBm
-89 dBm4
-89 dBm
32 MHz1
2
16 MHz2
4 x 4-ary BiOrthogonal
Modulation Option
Data Rate
Threshold
Chip Rate
2 twelve total channels in UNII band
1 six total channels in UNII band
4 x 4-ary BiOrthogonal (constrained3)
4 x 4-ary BiOrthogonal (constrained)
3 constant envelope MSK
4 average transmitter power increases by 6 dB